## Slide 1: Wireless Networks
Guevara Noubir
noubir@ccs.neu.edu

## Slide 2: Administrative Issues
Research oriented course (not necessarily theoretical)
Groups of 4 students
Make a list of email addresses
Grading:
  Quiz: 4*5% = 20%
  Midterm: 30%
  Project: 50%
    20%: literature survey/report
    20%: implementation/simulation
    10%: presentation
  (grades are individual: you should show your contribution to the project)
Make your group ASAP and choose your project
Meet with me this week to start working on the project
  Send me an email anytime to schedule a meeting (even the same day)
Who may drop the class? (so that I can accept more students)

## Slide 3: Projects
Development of a low data-rate wireless gateway (based on uCLinux boards and RF Monolithics 915MHz transceivers). Requires knowledge of linux and basic HW design
Simulation of routing protocols of wireless multi-hop ad-hoc networks using ns2 environment (e.g., DSDV, DSR, AODV)
Cellular systems radio resource management: analysis and simulation of radio resource management algorithms for wireless cellular communication systems (Dynamic Channel Assignment)
Cellular systems radio resource management: Base-Stations placement
Development of a simple environment for simulating wireless signals propagation and nodes mobility
Analysis and simulation of adaptive algorithms to improve IEEE802.11 WLAN.
Analysis and simulation of the performance of Bluetooth scatternets
Broadcast/multicast protocols of wireless multi-hop ad hoc networks
Analysis of power consumption in low-power devices
Efficient routing and medium access control schemes for sensor networks
Internet Protocols for the 3rd generation of wireless cellular communication systems
Cryptographically enforced fairness in wireless multi-hop ad-hoc networks
Co-existence issues of Bluetooth and IEEE802.11

## Slide 4: Course Outline
Overview of Wireless Systems: terminology, types of systems, issues, etc.
Radio technology - physical layer: (from the antenna to the base-band)
Wireless LANs: IEEE802.11, Hiperlan1/2, Bluetooth
Wireless network layer: Mobile-IP, Ad Hoc (DSDV, DSR, AODV, TORA)
Wireless Transport Layer Issues
Cellular telecommunication systems
Radio resource management in cellular networks

## Slide 5: Wireless Communication Systems
Target Information Systems: “Anytime, Anywhere, Anyform”
Applications: Ubiquitous Computing/Information Access
Market in continuous growth:
  35-60% annual growth of PCS
  Number of subscribers:
    by 2001: over 700M mobile phones
    by 2003: 1 billion wireless subscribers (source Ericsson)
  300% growth in wireless data from 1995-1997
Large diversity of standards and products!!!
Confusing terminology
Notes: Modify

## Slide 6
ad hoc
IMT200, WLAN,
DAB, GSM,
TETRA, ...
Personal Travel Assistant,
DAB, PDA, laptop,
GSM, cdmaOne, WLAN,
Bluetooth, ...

## Slide 7: Evolution of Number of Subscribers
Data from Source:
EMC World Cellular Database (www.emc-database.com)
GSM World Association (www.gsm.org)
http://www.gsmworld.com/membership/ass_sub_stats.html
GSM subscribers
Cellular subscribers (analogue, CDMA, GSM, etc.)

## Slide 8: Wireless Communication
Types of wireless communications?
Radio frequency spectrum
Wireless versus Mobile:
  Can we have wired-mobile node or wireless-fixed node?
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair
Notes: What is a wirless communication
Smoke signals, Infra-red, radio, visible light receivers (human receivers)
What ae VLF and LF signals used for? submarine
Microware = 1GHz-300GHz (relation to microwave oven)

## Slide 9: Attributes of Wireless & Mobile Communication Systems
Wireless:
  limited bandwidth: frequencies have to be coordinated, useful frequencies are almost all occupied
  broadcast medium: requires efficient access mechanisms
  variable link quality (noise, disconnection, interference)
  high latency, higher jitter (cellular):
    connection setup time: several hundred milliseconds
    Packet/bit interleaving
  heterogeneous air interfaces
  security: easier snooping
Mobility:
  user and terminal location is a dynamic system variable
  speed of mobile impact wireless bandwidth
  Security: easier spoofing
Portability:
  limited battery capacity
  limited computing
  limited storage memory
  small dimensions (limited user interfaces)
Notes: Types of interference
Attenuation: is it good or bad? Reuse but infrastructure

## Slide 10: Classification of Wireless Personal Communication
Mobility scale:
  within a house or building: cordless telephone, WLAN
  within a campus, city: (cellular radio, WLAN, wide area wireless data, radio paging, extended cordless)
  throughout the world: cellular radio, paging, satellite-based wireless
Communication modes:
  two-way voice
  data
  messaging
  video

## Slide 11: Wireless Systems: Past, Present and Future
Cellular
Wireless Area Data
Paging
Cordless
WLANs
WLANs
WLANs
Macro-cellular
Micro-cellular
Macro-cellular
Micro-cellular
Messaging
Phone point
WPABX
Cordless
Satellites
High-tier PCS
Low-tier PCS
Sensor Networks

## Slide 12: Evolution of Some Wireless Systems
cellular phones
satellites
wireless LAN
1992:
GSM
1994: DCS 1800
2005?:
UMTS/IMT-2000
1987: CT1+
1982:
Inmarsat-A
1992:
Inmarsat-B
Inmarsat-M
1998:
Iridium
1989:
CT 2
1991:
DECT
199x:
proprietary
1995/96/97:
IEEE 802.11,
HIPERLAN
2005?:
MBS, WATM
1988:
Inmarsat-C
analog
digital
1991:
D-AMPS
1991:
CDMA
1981:
NMT 450
1986:
NMT 900
1980: CT0
1984: CT1
1983:
AMPS
1993:
PDC
Notes: Advantage of digital over analog?

## Slide 13: Wireless “Standards”
IMT-2000:
CDMA2000,
WCDMA
Notes: Modify from pereira etc.

## Slide 14: Cordless Telephones (1970s- )
Evolved from analog to digital:
  Low transmission power:10mW (limited radio range)
  Low transmission delay: 10ms
  Dynamic Channel Allocation
Products
  Europe-Asia:
    CT-2 (864-868MHz, bitrate 72Kpbs), DECT (1880-1990MHz, 1.2MBps)
  USA: several products based on spread-spectrum or very low power transmission systems over the ISM frequency bands (900MHz, 2.4GHz)
  Japan: PHS (1895-1907MHz, upto 384KBps)
New services on cordless phones:
  PhonePoint (CT-2, PHS), WPABX (DECT)
  Limitations: reduced coverage, inefficient handoffs,
  Combination with cellular phones: GSM-DECT dual mode

## Slide 15: Cellular Mobile Radio Systems (Past/Present)
Characteristics:
  two-way voice service
  high mobility
    higher coverage, vehicular speed handoffs
  messaging etc.
  Mobile transmission power: ~2W
  Low data rate: <10KBps
  Higher RTT: ~200ms (due to interleaving, FEC etc.)
Standards/Products:
  Global Standard for Mobile (GSM):
    ~400M subscribers (Europe, Asia, USA)
    Extensions: HSCSD, GPRS
  Japanese of Personal Digital Cellular (JDC or PDC)
  USA: IS-54/IS-136/DAMPS, GSM (TDMA) or IS-95 (CDMA)

## Slide 16: Table of Wireless PCS
Notes: Page 15-8

## Slide 17: Cellular Mobile Radio Systems (Future)
Third Generation PCS initiated by ITU’s call for proposals (IMT2000)
  Convergence of wireless PCS into a unique system
  Efficient coverage
  High data rates: 144Kbps (high mobility), 384Kbps (low mobility), and up-to 2MBps for indoor
  Multi-QoS connections (data-rate, delay, FER)
Most likely: three standards
  WCDMA:
    ETSI proposal (FRAMES European project) [www.3GPP.org]
    ARIB proposal (Japan)
  CDMA2000 is an enhancement of Qualcomm’s IS-95 [www.3GPP2.org]
  EDGE: convergence of 2nd generation PCS (TDMA)
    GSM, D-AMPS, IS-54, IS-136

## Slide 19: Wide-Area Wireless Data Systems
Characteristics:
  high mobility (vehicular/pedestrian speed)
  wide range coverage
Products:
  ARDIS (USA: Motorola), RAM (Ericsson): low data rate <8Kbps
  Metricom (76Kbps):
    large number of inexpensive base stations,
    connected through wireless links
    each base stations has small coverage
    Deployed in San Francisco Bay area, Washington D.C.
    Slow frequency hopping, Pwr <1W over 902-928MHz ISM band
Wide area wireless data systems did not succeed to attract enough users!

## Slide 20: Wide-Area Wireless Data Systems
Notes: Fig from 15-12

## Slide 21: Wireless Local Area Networks
Characteristics:
  low-mobility
  high data-rate: 1MBps-25MBps
  campus/building coverage
Products/standards:
  IEEE802.11, Hiperlan 1/2, Bluetooth, HomeRF,
  Altair Plus, AirLan, Freeport, Intersect, LAWN, WILAN, RadioPort, ArLAN, Radio Link, Range LAN 1-2, Netware, FreeLink
Operate over ISM frequency Band:
  2.4GHz, 900MHz, 5GHz

## Slide 22: Other Wireless Systems
Paging/Messaging:
  Evolution: from 1 bits info, to two-way
  Combined with CT-2 (Phone point), GSM (Short Message Service: SMS)
Satellite-Based Mobile Systems:
  Large coverage
  Constellation of satellites (LEO)
  Products:
    Iridium (Motorola)
    Globalstar
    Teledesic (Lockheed Martin, Microsoft, Motorola)

## Slide 23: General Issues
Our main focus in this course is on:
  Primarily on WLAN, IP stacks over wireless
  Secondarily on PCS
Basic differences between PCS and WLAN
  WLAN
    Designed for high bit-rate data transmission
    Internet Protocols oriented
    Low-scale mobility, small area coverage
    Use unlicensed ISM frequency bands
  PCS
    Originally (2nd generation) designed for voice communication
    Limited bit-rate data transmission
    Large scale mobility and coverage (high-speed, big cells
    Operate over licensed frequency bands
Notes: Plannification, teletraffic.

## Slide 24: Common Components of Wireless Systems
Antenna:
  transducer that transforms an electric signal into an electro-magnetic signal and reciprocally
Radio-Frequency Front-End:
  Filters
  Power-Amplifier
  Mixers
  PLLs
Base-Band:
  Demodulation, Forward Error Correction
Multiple-Access Scheme
  FDMA, TDMA, CDMA, etc.

## Slide 25: EE view vs. CS view
Multiplex
Multiple
Access
Channel
encoder
Modulator
Power-Amplifier
RF Filter
Demultiplex
Multiple
Access
Channel
decoder
Demodulator&
Equalizer
Power-Amplifier
RF Filter
Source Coder
Source Decoder
Source Decoder
Carrier fc
Carrier fc
Source Coder
Electrical Engineer view:
ignores issues of routing, reliable transport, various applications requirements
Notes: Single application model
Up-conversion after the modulator
Spreading before the up-conversion

## Slide 26: EE view vs. CS view
Computer Network Engineer view
Physical Interface
Data Link Control
Transport
Network
Session
Application
Presentation
OSI stack
Physical Interface
Data Link Control
IP
ARP
…
UDP
TCP
TCP
FTP
Telnet
…
Lack of coordination between higher layers and physical layer

## Slide 27: WLAN Architectures
Terminology:
  Mobile Terminal (MT) or Mobile Station (MS) to denote and mobile node
  Access Point (AP) or Base-Station (BS) to denote the central entity that coordinates and wirelessly connects the mobiles to the wired network
Types of WLAN:
  Infrastructure WLAN
  Ad Hoc WLAN:
    Single: peer-to-peer communication
    Multi-hop: nodes act both as terminals and routers

## Slide 28: Issues in WLAN
Physical Layer
  How to resist to the wireless link limitations?  multiple error control coding schemes
Medium Access Layer
  Coordination of nodes
  Dealing wireless limitations (medium sensing and collisions detections)
Network Layer
  How to maintain the routing tables in the context of highly mobile nodes (multi-hop routing)?
Transport Layer
  TCP is optimized for congestion avoidance how to extend to error control
Application Layer
  How to satisfy the application requirements (delay, throughput)?
  How can the application adapt to the channel?
Resource conservation:
  Power-consumption, bandwidth optimization
  Planning for infrastructure networks (location identification, tele-traffic analysis)
  Self-configuration for multi-hop ad hoc networks
Notes: Routing: On-Demand routes with caching?
TCP modifications

## Slide 29: PCS Architectures
BS: Base Station
MSC: Mobile Switching Center
VLR: Visitor Location Register
HLR: Home Location Register
PSTN: Public Switched Telephone Network
POTS: Plain Old Telephone System
MSC
VLR
MSC
VLR
HLR
PSTN

## Slide 30: Issues in PCS
Planning
  Infrastructure planning:
    Location of base stations
  Resources planning and management:
    Frequency, timeslots, codes
    Fixed (FCA), Dynamic (DCA), Hybrid, etc.
Mobility:
  Handover (or handoff) types:
    Soft/hard/seamless (data flow), backward/forward (control flow)
    Mobile controlled (DECT, PACS), network controlled (AMPS, CT-2), mobile assisted (GSM, IS-95)
    Intra-system handover, inter-system handover
  Admission Control
  Roaming
Notes: Complexity of BS is much higher than in WLAN
PCS:
Smart antenna
Power control advantages
Doppler shift
RRM

## Slide 31: Summary
Main Wireless Systems:
  WLAN: IEEE802.11, Bluetooth (more for short-range low bit-rate interconnection)
  Cellular:
    Today: GSM (= DCS1800, PCS1900), CdmaOne (= IS-95), DAMPS (= TDMA, IS-136, IS-54)
    Near future: WCDMA (UMTS = 3GPP), Cdma2000 (=3GPP2)