## Slide 1: Wireless Networks: Physical Layer: Modulation, FEC
Guevara Noubir
Noubir@ccs.neu.edu

## Slide 2: Lecture focus
Modulation techniques
Bit Error Rate
Reducing the BER
Forward Error Correction
  Block codes
  Convolutional codes
Notes: Estimate BER and understand how the BER varies => fadings
In a wired network we try to understand the reasons for congestion
If you take an IEEE802.11 card you can always monitor the SNR from the config soft. You don’t have that for ethernet

## Slide 3: Modulation
What is modulation?
  Mapping a digital sequence of information bits into an analog signal suitable for transmission over the communication medium (channel)
  Process during which the amplitude, frequency, or the phase of a carrier changes in accordance with the information to be transmitted
  Modulation associates each n bits to a signal Si(t) chosen among M = 2n signals
Baseband transmission versus carrier modulation transmission
  Baseband: signal within [0, fs] (e.g., cable)
  Carrier modulation: signal within [f-fs, f+fs]
Basic modulation schemes:
  Amplitude modulation, Phase modulation, Frequency modulation

## Slide 4: Fourier Transforms
Any function s(t) can be represented as a superposition of complex sinusoids of weight: S(f)
  Fourier transform
  Inverse Fourier transform
Cos and Sin are orthogonal => can be used to independently modulate 2 sequences of symbols => I (In-phase) and Q (Quadrature phase) channels

## Slide 5: Modulation Schemes
Analog:
  Amplitude modulation
  Frequency modulation
Main digital modulation schemes:
  Amplitude modulation:
    On-Off Keying (OOK): simplest modulation scheme (AM): carrier amplitude is 1 or 0 depending on the value of the information to be transmitted
    Pulse Amplitude Modulation (PAM): use M = 2m amplitudes
  Frequency-Shift Keying (FSK):
    BFSK: use two different tones (frequencies) f0, f1. Use f0 to transmit a 0 information bit, and f1 to transmit an information bit equal to 1
    MFSK: generalized to M = 2m frequencies to transmit m bits simultaneously
  Phase-Shift Keying (PSK):
    BPSK: use two signals shifted by 180 degrees: s0, and s1
    MPSK: use signals with different phases and amplitudes: QPSK etc.
Notes: Pages 130 for formulas

## Slide 6: Modulation Schemes
Phase Shift Keying:
Frequency Shift Keying:
Amplitude Shift Keying:
Amplitude Phase Keying:

## Slide 7: Choosing the Modulation Scheme
Compactness of the power spectrum density: minimize interference on adjacent channels (60-80dB)
Good performance in terms of BER
Envelope properties: constant envelope to avoid problems caused by non-linear amplifiers

## Slide 8: Additive White Gaussian Noise
Noise:
  As previously seen, noise has several sources
  Thermal noise source is the motion of electrons in amplifiers and circuits
  Its statistics were determined using quantum mechanics
  It is flat for all frequencies up to 1012Hz.
  We generally call it: Additive White Gaussian Noise (AWGN)
  Its probability density function (pdf) (zero mean noise voltage):
Notes: Interleaver transform non awgn into awgn
Sigma^2 = N0/2

## Slide 9: Bit Error Rate [Sklar1988]
BER for coherently detected BPSK:
BER for coherently detected BFSK:

## Slide 10: Error Control
Two main techniques:
  Forward Error Correction
  Automatic Repeat reQuest
In practice:
  Combinations: Hybrid ARQ I and Hybrid ARQ II
ARQ:
  Stop&Wait, GoBackN, Selective Repeat
FEC:
  Block codes, convolutional codes

## Slide 11: Block Codes
Information bits (word):
  u = (u1, u2, …, uk)
Code word (n>k):
  v = (v1, v2, …, vn)
Systematic versus non-systematic
Binary versus Non-Binary
Use of codes:
  Error detection, error correction, erasure correction
  How to build codes with high error correction capability?
Examples:
  Hamming code, BCH codes, RS codes

## Slide 12: Hamming Distance for Block Codes
The Hamming distance between two code words is the number of places where they differ
The Hamming distance d of a Block code is the minimum distance between two code words
Error Detection:
  Upto d-1 errors
Error Correction:
  Upto
Combine: d2+l+1
Notes: Use for error correction

## Slide 13: Coding Gain
Definition:
  The coding gain is the amount of additional SNR that would be required to provide the same BER performance for an uncoded signal
If the code is capable of correcting at most t errors and PUC is the BER of the channel without coding, then the probability that a bit is in error using coding is:
Notes: Application for Puc = 10-3
Useful if errors are not happening in bursts: if always 2 bits in error
Golay code

## Slide 14: Example of Binary Block Code (7, 4)
Any two different code words are different on at least three different coordinates. This code has Hamming distance 3.
Notice that the last 4 bits of the code word are the same as the message
  This is a systematic coding
  The other 3 bits are redundancy bits

## Slide 15: Linear Block
A block code of length n and 2k code words is called a linear (n, k) code iff its 2k code words form a k-dimensional subspace of the vector space of all n-tuples over the field GF(2)
Informal Meaning: linear combinations of codewords are also codewords
The linear code is completely specified by k independent codewords (G generator matrix)
The encoder needs only to store the matrix G
Example: Linear code (7, 4)
To encode u = (1 1 0 1): v = 1g0 + 1g1 + 0g2 + 1g3

## Slide 16: Parity-Check Matrix (H)
For every kxn generator matrix G (with k linearly independent rows), there exists a (n-k)xn matrix H (with (n-k) linearly independent rows) called parity check matrix such that: any vector in the row space of G is orthogonal to any row of H and any vector that is orthogonal to all the rows of H is in the row space of G:
The 2n-k combinations of the rows of H form an (n-k)-dimensional subspace. It is the null space of C the (n, k) code generated by G. It is called the dual space of C and noted Cd.
For any v in C and w in Cd we have v w = 0

## Slide 17: Systematic Coding
A linear block code is called systematic iff the code words can be divided into two parts: Message part (k bits), and a redundancy checking part (n-k bits)
Systematic code generator matrix: G = [P Ik]; H = [In-k PT]; GHT=0
Redundant Checking part
Message part
n-k digits
k digits

## Slide 18: Hamming Codes (2m-1, 2m-m-1)
Parameters of Hamming codes (m>2):
  Code length: n = 2m-1
  Number of information bits: k = 2m-m-1
  Number of parity check bits: n-k = m
  Minimum distance: 3
  Error-correcting capability: t = (3-1)/2 = 1
Parity check matrix of a Hamming code: H = [Im Q]
  Im is the identity matrix mxm
  Q consists of 2m-m-1 columns which are the m-tuples of weight 2 or more
  Example:

## Slide 19: Minimum Distance of Block Codes
The minimum distance dmin of a block code is the minimum distance between any two code words:
  dmin = min {d(v, w), s.t. v, w C, v  w}
  dmin = min {w(v + w), s.t. v, w C, v  w}
  dmin = min {w(x), s.t. x C, x  0} (because C is a vector sub-space)
Example: Minimum Distance of Hamming Codes?

## Slide 20: Cyclic Block Codes
Definition:
  An (n, k) linear code C is called a cyclic code if every cyclic shift of a code vector in C is also a code vector
  Codewords can be represented as polynomials of degree n. For a cyclic code all codewords are multiple of some polynomial g(X) modulo Xn+1 such that g(X) divides Xn+1. g(X) is called the generator polynomial.
Examples:
  Hamming codes, Golay Codes, BCH codes, RS codes
  BCH codes were independently discovered by Hocquenghem (1959) and by Bose and Chaudhuri (1960)
  Reed-Solomon codes (non-binary BCH codes) were independently introduced by Reed-Solomon

## Slide 21: Systematic Cyclic Codes
Data bits:
Polynomial representation:
The CRC is also viewed as a polynomial:
The transmitted frame can be represented as:

## Slide 22: Systematic Cyclic Codes
The CRC is the remainder of dividing the information polynomial S(D) by a generator polynomial g(D).
Example: divide D5+D3 by D3+D2+1

## Slide 23: Cyclic Block Codes
A cyclic Hamming code of length 2m-1 with m>2 is generated by a primitive polynomial p(X) of degree m
Hamming code (31, 26)
  g(X) = 1 + X2 + X5, l = 3
Golay Code:
  cyclic code (23, 12)
  minimum distance 7
  generator polynomials: either g1(X) or g2(X)

## Slide 24: Bose Chaudhuri and Hocquenghem (BCH) Codes
For any positive integer m (m>2) and t (t<2m-1), there exists a BCH code:
  Block length: 2m-1
  Parity bits: n - k  mt
  Minimum distance: dmin  2t + 1
  generator polynomial is the lowest-degree polynomial over GF(2) such that:
  , 2,  3, …, 2t are its roots.  is the primitive root of unity in the extension field GF(2n).
Such a BCH code is capable of correcting t errors
The generator polynomial is:
  g(X) = LCM{1(X), 2(X), …, 2t(X)}
  for i = i’2l, i(X) = i’(X) (because i and i’ are conjugates), thus
  g(X) = LCM{1(X), 3(X), …, 2t-1(X)}
Since any minimal polynomial has degree m or less, then degree (n - k) of g is at most mt
If t = 1, then g is a primitive polynomial and we have a Hamming code
Notes: Reed-Solomon Codes are a special case of BCH codes

## Slide 25: Convolutional codes
(n, k, K) convolutional code: inputs k bits, outputs n bits and has register depth K
Rate: k/n
Example of binary convolutional encoder
  n = 2, k = 1, K = 3. Rate ½
Representations:
  State, Tree, Trellis
Decoding:
  Soft decision vs. Hard decision
  Viterbi Algorithm, sequential decoding, feedback decoding

## Slide 26: Representations of Convolutional Codes
State Coding:
  K-1 registers + input => state diagram (finite state machine)
Input bit mi
Registers
State at ti
State at ti+1
Output
-
000
00
00
-
1
100
00
10
11
1
110
10
11
01
0
011
11
01
01
1
101
01
10
01
1
110
10
11
00
0
011
11
01
01
0
001
01
00
11
00
11
01
10
00
11
11
00
01
01
10
10
Input = 0
Input = 1

## Slide 27: Representations of Convolutional Codes
Trellis representation:
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11

## Slide 28: Viterbi Decoding Algorithm
Principle:
  Computes a measure of similarity (distance) between the received signal and all potential trellis paths
  For each state keeps only one “more likely” path
Algorithm:
  For each input
    For each state:
      Determine the distance/weight of the branches leading to it
      Keep only the best branch
    If all surviving paths at time ti pass through some state S at time ti-j then commit to S(ti-j)

## Slide 29: Viterbi Decoding
Input: 11011011010
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
11 01 01 01 01 01 00 01 01 00 10
1 1 0 1 1 0 1 1 0 1 0

## Slide 30: Other Techniques
Equalization:
  Reason: multi-path generates Inter-Symbol Interference (ISI)
  An equalizer is a filter that inverts the effect of the channel
  Generally uses training sequences to estimate the channel
Interleaving:
  Reason: in some channels errors occur in bursts and channel coding is only efficient when errors are randomly distributed
  Goal: transforms a burst of errors into randomly distributed errors
  Types: bit level, frame level
  Drawbacks: delay
  How: matrix bit-interleaving. Bits enter on the rows and are output column by column

## Slide 31: Other Techniques (Cont’d)
Diversity techniques:
  Micro-diversity:
    Time diversity: transmit at different moments (separated by channel coherence time: inverse of the Doppler frequency). Generally combined with ARQ and FEC
    Drawback: may reduce throughput
  Space diversity:
    Use multiple antennas separated by 0.5 and/or 0.8: ~3dB gain.
    Drawback: requires equipment to process multiple input signals
  Polarization: orthogonally polarized signals are uncorrelated
    Multiple polarization achieves 6-10dB gain
  Frequency diversity:
    Use frequencies separated by a value higher than the coherence bandwidth (=> frequency hopping schemes)
Smart antennas

## Slide 32: Spread Spectrum Technology
Problem of radio transmission:
  frequency dependent fading can wipe out narrow band signals for duration of the interference; multi-path fading; eavesdropping; collisions; time imprecision
Solution: spread the narrow band signal into a broad band signal using a special code
protection against narrow band interference
protection against narrowband interference
Side effects:
  coexistence of several signals without dynamic coordination (CDMA); “tap-proof”, fine time resolution (GPS); clock recovery …
Techniques: Direct Sequence, Frequency Hopping, (Time Hopping)
detection at
receiver
interference
spread signal
signal
spread
interference
f
f
power
power

## Slide 33: Effects of Spreading and Interference
P
f
i)
P
f
ii)
sender
P
f
iii)
P
f
iv)
receiver
f
v)
user signal
broadband interference
narrowband interference
P
Notes: Explain

## Slide 34: Spreading and Frequency Selective Fading
frequency
channel quality
1
2
3
4
5
6
narrow band signal
guard space
2
2
2
2
2
frequency
channel quality
1
spread spectrum
narrowband channels
spread spectrum channels

## Slide 35: DSSS (Direct Sequence Spread Spectrum)
XOR of the signal with pseudo-random number (chipping sequence)
  many chips per bit (e.g., 128) result in higher bandwidth of the signal
  Examples: Barker code: 11100010010(IEEE802.11), Hadamard, Kazami codes
Advantages
  reduces frequency selective fading
  in cellular networks
    base stations can use the same frequency range
    several base stations can detect and recover the signal
    soft handover
Disadvantages
  precise power control necessary
user data
chipping
sequence
resulting
signal
0
1
0
1
1
0
1
0
1
0
1
0
0
1
1
1
XOR
0
1
1
0
0
1
0
1
1
0
1
0
0
1
=
tb
tc
tb: bit period
tc: chip period
Notes: Resistance to multipat

## Slide 36: DSSS (Direct Sequence Spread Spectrum)
X
user data
chipping
sequence
modulator
radio
carrier
spread
spectrum
signal
transmit
signal
transmitter
demodulator
received
signal
radio
carrier
X
chipping
sequence
lowpass
filtered
signal
receiver
integrator
products
decision
data
sampled
sums
correlator

## Slide 37: FHSS (Frequency Hopping Spread Spectrum) I
Discrete changes of carrier frequency
  sequence of frequency changes determined via pseudo random number sequence
Two versions
  Fast Hopping: several frequencies per user bit
  Slow Hopping: several user bits per frequency
Advantages
  frequency selective fading and interference limited to short period
  simple implementation
  uses only small portion of spectrum at any time
Disadvantages
  not as robust as DSSS
  simpler to detect

## Slide 38: FHSS (Frequency Hopping Spread Spectrum)
user data
slow
hopping
(3 bits/hop)
fast
hopping
(3 hops/bit)
0
1
tb
0
1
1
t
f
f1
f2
f3
t
td
f
f1
f2
f3
t
td
tb: bit period td: dwell time

## Slide 39: FHSS (Frequency Hopping Spread Spectrum)
modulator
user data
hopping
sequence
modulator
narrowband
signal
spread
transmit
signal
transmitter
received
signal
receiver
demodulator
data
frequency
synthesizer
hopping
sequence
demodulator
frequency
synthesizer
narrowband
signal