## Slide 1: Wireless Networks: Medium Access Control
Slides adapted from “Mobile Communications” by J. Schiller
Guevara Noubir
Notes: Add summary of results from Tabbane
Add RTS/CTS from 802.11 or 3510

## Slide 2: Motivation
Can we apply media access methods from fixed networks?
Example CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  send as soon as the medium is free, listen into the medium if a collision occurs (original method in IEEE 802.3)
Problems in wireless networks
  signal strength decreases proportional to the square of the distance
  the sender would apply CS and CD, but the collisions happen at the receiver
  it might be the case that a sender cannot “hear” the collision, i.e., CD does not work
  furthermore, CS might not work if, e.g., a terminal is “hidden”

## Slide 3: Motivation - hidden and exposed terminals
Hidden terminals
  A sends to B, C cannot receive A
  C wants to send to B, C senses a “free” medium (CS fails)
  collision at B, A cannot receive the collision (CD fails)
  A is “hidden” for C
Exposed terminals
  B sends to A, C wants to send to another terminal (not A or B)
  C has to wait, CS signals a medium in use
  but A is outside the radio range of C, therefore waiting is not necessary
  C is “exposed” to B
B
A
C

## Slide 4: Motivation - near and far terminals
Terminals A and B send, C receives
  signal strength decreases proportional to the square of the distance
  the signal of terminal B therefore drowns out A’s signal
  C cannot receive A
If C for example was an arbiter for sending rights, terminal B would drown out terminal A already on the physical layer
Also severe problem for CDMA-networks - precise power control needed!
A
B
C

## Slide 5: Access methods SDMA/FDMA/TDMA
SDMA (Space Division Multiple Access)
  segment space into sectors, use directed antennas
  cell structure
FDMA (Frequency Division Multiple Access)
  assign a certain frequency to a transmission channel between a sender and a receiver
  permanent (e.g., radio broadcast), slow hopping (e.g., GSM), fast hopping (FHSS, Frequency Hopping Spread Spectrum)
TDMA (Time Division Multiple Access)
  assign the fixed sending frequency to a transmission channel between a sender and a receiver for a certain amount of time
The multiplexing schemes are now used to control medium access!
Notes: 15

## Slide 6: FDD/FDMA - general scheme, example GSM
f
t
124
1
124
1
20 MHz
200 kHz
890.2 MHz
935.2 MHz
915 MHz
960 MHz

## Slide 7: TDD/TDMA - general scheme, example DECT
1
2
3
11
12
1
2
3
11
12
t
downlink
uplink
417 µs

## Slide 8: Frequency Division Multiple Access
Concept:
  assign different frequency bands to different users
  no sharing of a frequency band between two users
  user separation using band-pass filters
  continuous flow
  two-way: two frequency bands or Time Division Duplex (TDD)
Advantages: simple receivers
  longer symbol duration: no-need for equalization
    low inter-symbol interference
    e.g., 50kb/s QPSK =>40s >> 1-10s delay spread
Drawbacks:
  frequency guard bands, costly tight RF band-filters,
  long fading duration: need slow frequency hopping
  may need spatial diversity (multiple antennas/beam forming) Rx/Tx

## Slide 9: Frequency Selection
Frequency management:
  Fixed (cellular phones-base stations): reuse factor
  On demand (cellular phones-mobile terminals)
  Dynamic (cordless/WLAN): based on sensing interference levels
  Problems: congestion management, dynamic load, …
Antenna implications:
  High antennas (e.g., 50m): higher coverage but higher interference between base stations (need for synchronization)
  Low antennas: higher attenuation, lower coverage, better reuse
Conclusion:
  Pure FDMA is only interesting for simple cordless systems (CT-2)

## Slide 10: Time Division Multiple Access
Concept:
  use the same frequency over non-overlapping periods of time
Advantages:
  simple filters (window)
  transmit and receive over the same frequency channel
Drawbacks:
  users must be synchronized with BS (master clock over a BCH)
  guard times: common 30-50s, may be less in recent systems
  short symbol duration: need for equalization, training sequences...
    high inter-symbol interference
    e.g., 50Kbps, QPSK, 8 users:
      5 s symbol duration
      delay spread: 1s (cordless), upto 20s for cellular

## Slide 11: FDMA/TDMA
First channel allocation:
  random access channel (RACH) to send short requests
  ALOHA type protocol over the RACH
One can use both FDMA and TDMA
  examples: GSM system, D-AMPS
M9
M5
M6
M1
M2
M3
M4
M9
M5
M6
M1
M2
M3
M4
Time
Frequency
cycle

## Slide 12: Access method CDMA
CDMA (Code Division Multiple Access)
  all terminals send on the same frequency probably at the same time and can use the whole bandwidth of the transmission channel
  codes generate signals with “good-correlation” properties
  signals from another user appear as “noise” (use spread spectrum technology)
  signals are spread over a wideband using pseudo-noise sequences (e.g., each sender has a unique random number, the sender XORs the signal with this random number)
  the receiver can “tune” into this signal if it knows the pseudo random number, tuning is done via a correlation function
Disadvantages:
  higher complexity of a receiver (receiver cannot just listen into the medium and start receiving if there is a signal)
  all signals should have the same strength at a receiver (near-far effect)
Advantages:
  all terminals can use the same frequency => no planning needed; macrodiversity
  huge code space (e.g. 232) compared to frequency space
  interferences (e.g. white noise) is not coded
  forward error correction and encryption can be easily integrated
Notes: 28

## Slide 13: CDMA in theory
Sender A
  sends Ad = 1, key Ak = 010011 (assign: „0“= -1, „1“= +1)
  sending signal As = Ad * Ak = (-1, +1, -1, -1, +1, +1)
Sender B
  sends Bd = 0, key Bk = 110101 (assign: „0“= -1, „1“= +1)
  sending signal Bs = Bd * Bk = (-1, -1, +1, -1, +1, -1)
Both signals superimpose in space
  interference neglected (noise etc.)
  As + Bs = (-2, 0, 0, -2, +2, 0)
Receiver wants to receive signal from sender A
  apply key Ak bitwise (inner product)
    Ae = (-2, 0, 0, -2, +2, 0)  Ak = 2 + 0 + 0 + 2 + 2 + 0 = 6
    result greater than 0, therefore, original bit was „1“
  receiving B
    Be = (-2, 0, 0, -2, +2, 0)  Bk = -2 + 0 + 0 - 2 - 2 + 0 = -6, i.e. „0“

## Slide 14: CDMA on signal level I
data A
key A
signal A
data  key
key
sequence A
1
0
1
1
0
0
1
0
0
1
0
0
0
1
0
1
1
0
0
1
1
0
1
1
0
1
1
1
0
0
0
1
0
0
0
1
1
0
0
Ad
Ak
As
Real systems use much longer keys resulting in a larger distance
between single code words in code space.

## Slide 15: CDMA on signal level II
signal A
data B
key B
key
sequence B
signal B
As + Bs
data  key
1
0
0
0
0
0
1
1
0
1
0
1
0
0
0
0
1
0
1
1
1
1
1
1
0
0
1
1
0
1
0
0
0
0
1
0
1
1
1
Bd
Bk
Bs
As

## Slide 16: CDMA on signal level III
Ak
(As + Bs) * Ak
integrator
output
comparator
output
As + Bs
0
1
0
1
0
1
data A
Ad

## Slide 17: CDMA on signal level IV
integrator
output
comparator
output
Bk
(As + Bs) * Bk
As + Bs
0
1
1
1
0
0
data B
Bd

## Slide 18: CDMA on signal level V
comparator
output
(1)
(1)
?
wrong
key K
integrator
output
(As + Bs) * K
As + Bs

## Slide 19: CDMA: Direct Sequence
Each mobile is allocated a PN sequence:
The elements of the PN-sequence are called chips
To transmit one bit 1/0 send the PN-Seq/inv-PN-Seq
Example Hadamard Matrix:
  Each mobile uses one row
  The rows are orthogonal

## Slide 20: Aloha/slotted aloha
Mechanism
  random, distributed (no central arbiter), time-multiplex
  Slotted Aloha additionally uses time-slots, sending must always start at slot boundaries
Aloha
Slotted Aloha
sender A
sender B
sender C
collision
sender A
sender B
sender C
collision
t
t

## Slide 21: Carrier Sense Protocols
Use the fact that in some networks you can sense the medium to check whether it is currently free
  1-persistent CSMA
  non-persistent CSMA
  p-persistent protocol
  CSMA with collision Detection (CSMA/CD): not applicable to wireless systems
1-persistent CSMA
  when a station has a packet:
    it waits until the medium is free to transmit the packet
    if a collision occurs, the station waits a random amount of time
  first transmission results in a collision if several stations are waiting for the channel

## Slide 22: Carrier Sense Protocols (Cont’d)
non-persistent CSMA
  when a station has a packet:
    if the medium is free, transmit the packet
    otherwise wait for a random period of time and repeat the algorithm
  higher delays, but better performance than pure ALOHA
p-persistent protocol
  when a station has a packet wait until the medium is free:
    transmit the packet with probability p
    wait for next slot with probability 1-p
  better throughput than other schemes but higher delay
CSMA with collision Detection (CSMA/CD)
  stations abort their transmission when they detect a collision
  e.g., Ethernet, IEEE802.3 but not applicable to wireless systems

## Slide 23: DAMA - Demand Assigned Multiple Access
Channel efficiency only 18% for Aloha, 36% for Slotted Aloha (assuming Poisson distribution for packet arrival and packet length)
Reservation can increase efficiency to 80%
  a sender reserves a future time-slot
  sending within this reserved time-slot is possible without collision
  reservation also causes higher delays
  typical scheme for satellite links
Examples for reservation algorithms:
  Explicit Reservation according to Roberts (Reservation-ALOHA)
  Implicit Reservation (PRMA)
  Reservation-TDMA

## Slide 24: Access method DAMA: Explicit Reservation
Explicit Reservation (Reservation Aloha):
  two modes:
    ALOHA mode for reservation: competition for small reservation slots, collisions possible
    reserved mode for data transmission within successful reserved slots (no collisions possible)
  it is important for all stations to keep the reservation list consistent at any point in time and, therefore, all stations have to synchronize from time to time
Aloha
reserved
Aloha
reserved
Aloha
reserved
Aloha
collision
t
Notes: 24

## Slide 25: Access method DAMA: PRMA
Implicit reservation (PRMA - Packet Reservation MA):
  a certain number of slots form a frame, frames are repeated
  stations compete for empty slots according to the slotted aloha principle
  once a station reserves a slot successfully, this slot is automatically assigned to this station in all following frames as long as the station has data to send
  competition for this slots starts again as soon as the slot was empty in the last frame
frame1
frame2
frame3
frame4
frame5
1
2
3
4
5
6
7
8
time-slot
collision at reservation attempts
A
C
D
A
B
A
F
A
C
A
B
A
A
B
A
F
A
B
A
F
D
A
C
E
E
B
A
F
D
t
ACDABA-F
ACDABA-F
AC-ABAF-
A---BAFD
ACEEBAFD
reservation
Notes: 25

## Slide 26: Access method DAMA: Reservation-TDMA
Reservation Time Division Multiple Access
  every frame consists of N mini-slots and x data-slots
  every station has its own mini-slot and can reserve up to k data-slots using this mini-slot (i.e. x = N * k).
  other stations can send data in unused data-slots according to a round-robin sending scheme (best-effort traffic)
N mini-slots
N * k data-slots
reservations for data-slots
other stations can use free data-slots
based on a round-robin scheme
e.g. N=6, k=2
Notes: 26

## Slide 27: MACA - collision avoidance
MACA (Multiple Access with Collision Avoidance) uses short signaling packets for collision avoidance
  RTS (request to send): a sender request the right to send from a receiver with a short RTS packet before it sends a data packet
  CTS (clear to send): the receiver grants the right to send as soon as it is ready to receive
Signaling packets contain
  sender address
  receiver address
  packet size
Variants of this method can be found in IEEE802.11 as DFWMAC (Distributed Foundation Wireless MAC)

## Slide 28: MACA examples
MACA avoids the problem of hidden terminals
  A and C want to send to B
  A sends RTS first
  C waits after receiving CTS from B
MACA avoids the problem of exposed terminals
  B wants to send to A, C to another terminal
  now C does not have to wait for it cannot receive CTS from A
A
B
C
RTS
CTS
CTS
A
B
C
RTS
CTS
RTS

## Slide 29: MACA variant: DFWMAC in IEEE802.11
idle
wait for the
right to send
wait for ACK
sender
receiver
packet ready to send; RTS
time-out;
RTS
CTS; data
ACK
RxBusy
idle
wait for
data
RTS; RxBusy
RTS;
CTS
data;
ACK
time-out 
data;
NAK
ACK: positive acknowledgement
NAK: negative acknowledgement
RxBusy: receiver busy
time-out 
NAK;
RTS

## Slide 30: Polling mechanisms
If one terminal can be heard by all others, this “central” terminal (a.k.a. base station) can poll all other terminals according to a certain scheme
  now all schemes known from fixed networks can be used (typical mainframe - terminal scenario)
Example: Randomly Addressed Polling
  base station signals readiness to all mobile terminals
  terminals ready to send can now transmit a random number without collision with the help of CDMA or FDMA (the random number can be seen as dynamic address) or with collisions (over the Random Access CHannel)
  the base station now chooses one address for polling from the list of all random numbers (collision if two terminals choose the same address)
  the base station acknowledges correct packets and continues polling the next terminal
  this cycle starts again after polling all terminals of the list

## Slide 31: ISMA (Inhibit Sense Multiple Access)
Current state of the medium is signaled via a “busy tone”
  the base station signals on the downlink (base station to terminals) if the medium is free or not
  terminals must not send if the medium is busy
  terminals can access the medium as soon as the busy tone stops
  the base station signals collisions and successful transmissions via the busy tone and acknowledgements, respectively (media access is not coordinated within this approach)
  mechanism used, e.g., for CDPD (USA, integrated into AMPS)

## Slide 32: SAMA - Spread Aloha Multiple Access
Aloha has only a very low efficiency, CDMA needs complex receivers to be able to receive different senders with individual codes at the same time
Idea: use spread spectrum with only one single code (chipping sequence) for spreading for all senders accessing according to aloha
1
sender A
0
sender B
0
1
t
narrow band
send for a
shorter period
with higher power
spread the signal e.g. using the chipping sequence 110101 („CDMA without CD“)
Problem: find a chipping sequence with good characteristics
1
1
collision

## Slide 33: Comparison SDMA/TDMA/FDMA/CDMA

## Slide 34: Throughputs of Some Random Access Protocols
G: load (includes both successful transmissions and retransmissions)
S: successful transmission
a: ratio of propagation delay to the packet transmission delay
Protocol
Throughput
Pure-ALOHA
S = Ge-2G
Slotted-ALOHA
S = Ge-G
Non slotted 1-persistent
Slotted 1-persistent CSMA
Nonpersistent non slotted
CSMA
Nonpersistent slotted
CSMA