## Slide 1: Wireless Networking: IEEE802.11
Slides partially adapted from “Mobile Communications” by J. Schiller
Read Chapter 7.

## Slide 2: Characteristics of wireless LANs
Advantages
  very flexible within the reception area
  Ad-hoc networks without previous planning possible
  (almost) no wiring difficulties (e.g. historic buildings, firewalls)
  more robust against disasters like, e.g., earthquakes, fire - or users pulling a plug...
Disadvantages
  typically very low bandwidth compared to wired networks (1-11 Mbit/s)
  many proprietary solutions, especially for higher bit-rates, standards take their time (e.g. IEEE 802.11)
  products have to follow many national restrictions if working wireless, it takes a vary long time to establish global solutions like, e.g., IMT-2000

## Slide 3: Design goals for wireless LANs
  global, seamless operation
  low power for battery use
  no special permissions or licenses needed to use the LAN
  robust transmission technology
  simplified spontaneous cooperation at meetings
  easy to use for everyone, simple management
  protection of investment in wired networks
  security (no one should be able to read my data), privacy (no one should be able to collect user profiles), safety (low radiation)
  transparency concerning applications and higher layer protocols, but also location awareness if necessary

## Slide 4: Comparison: infrared vs. radio transmission
Infrared
  uses IR diodes, diffuse light, multiple reflections (walls, furniture etc.)
Advantages
  simple, cheap, available in many mobile devices
  no licenses needed
  simple shielding possible
Disadvantages
  interference by sunlight, heat sources etc.
  many things shield or absorb IR light
  low bandwidth
Example
  IrDA (Infrared Data Association) interface available everywhere
Radio
  typically using the license free ISM band at 2.4 GHz
Advantages
  experience from wireless WAN and mobile phones can be used
  coverage of larger areas possible (radio can penetrate walls, furniture etc.)
Disadvantages
  very limited license free frequency bands
  shielding more difficult, interference with other electrical devices
Example
  IEEE802.11, Bluetooth, Hiperlan

## Slide 5: Comparison: infrastructure vs. ad-hoc networks
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point

## Slide 6: 802.11 - Architecture of an infrastructure network
Distribution System
Portal
802.x LAN
Access
Point
802.11 LAN
BSS2
802.11 LAN
BSS1
Access
Point
Station (STA)
  terminal with access mechanisms to the wireless medium and radio contact to the access point
Basic Service Set (BSS)
  group of stations using the same radio frequency
Access Point
  station integrated into the wireless LAN and the distribution system
Portal
  bridge to other (wired) networks
Distribution System
  interconnection network to form one logical network (EES: Extended Service Set) based on several BSS
STA1
STA2
STA3
ESS
Notes: <number>
Prof. Dr. Dr. h.c. G. Krüger
E. Dorner / Dr. J. Schiller
Universität Karlsruhe
Institut für Telematik
Mobilkommunikation
SS 1998
9

## Slide 7: 802.11 - Architecture of an ad-hoc network
Direct communication within a limited range
  Station (STA): terminal with access mechanisms to the wireless medium
  Basic Service Set (BSS): group of stations using the same radio frequency
802.11 LAN
BSS2
802.11 LAN
BSS1
STA1
STA4
STA5
STA2
STA3

## Slide 8: IEEE standard 802.11
mobile terminal
access point
server
fixed terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure network
LLC
LLC

## Slide 9: 802.11 - Layers and functions
PLCP Physical Layer Convergence Protocol
  clear channel assessment signal (carrier sense)
PMD Physical Medium Dependent
  modulation, coding
PHY Management
  channel selection, MIB
Station Management
  coordination of all management functions
PMD
PLCP
MAC
LLC
MAC Management
PHY Management
MAC
  access mechanisms, fragmentation, encryption
MAC Management
  synchronization, roaming, MIB, power management
PHY
DLC
Station Management

## Slide 10: 802.11 - Physical layer
3 versions: 2 radio (typ. 2.4 GHz), 1 IR
  data rates 1 or 2 Mbit/s
FHSS (Frequency Hopping Spread Spectrum)
  spreading, despreading, signal strength, typ. 1 Mbit/s
  min. 2.5 frequency hops/s (USA), two-level GFSK modulation
DSSS (Direct Sequence Spread Spectrum)
  DBPSK modulation for 1 Mbit/s (Differential Binary Phase Shift Keying), DQPSK for 2 Mbit/s (Differential Quadrature PSK)
  preamble and header of a frame is always transmitted with 1 Mbit/s, rest of transmission 1 or 2 Mbit/s
  chipping sequence: +1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1 (Barker code)
  max. radiated power 1 W (USA), 100 mW (EU), min. 1mW
Infrared
  850-950 nm, diffuse light, typ. 10 m range
  carrier detection, energy detection, synchonization
Notes: Two levels GFSK for 2Mbps

## Slide 11: FHSS PHY packet format
synchronization
SFD
PLW
PSF
HEC
payload
PLCP preamble
PLCP header
80
16
12
4
16
variable
bits
Synchronization
  synch with 010101... pattern
SFD (Start Frame Delimiter)
  0000110010111101 start pattern
PLW (PLCP_PDU Length Word)
  length of payload incl. 32 bit CRC of payload, PLW < 4096
PSF (PLCP Signaling Field)
  data rate of payload (1 or 2 Mbit/s)
HEC (Header Error Check)
  CRC with x16+x12+x5+1
Notes: The Preamble SYNC field is an 80-bit field containing an alternating zero-one pattern, transmitted starting with zero and ending with one, to be used by the PHY sublayer to detect a potentially receivable signal, select an antenna if diversity is utilized, and reach steady-state frequency offset correction and synchronization with the received packet timing.
The SFD consists of the 16-bit binary pattern 0000 1100 1011 1101 (transmitted leftmost bit Þrst). The Þrst bit of the SFD follows the last bit of the sync pattern. The SFD defines the frame timing.

## Slide 12: DSSS PHY packet format
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16
Synchronization
  synch., gain setting, energy detection, frequency offset compensation
SFD (Start Frame Delimiter)
  1111001110100000
Signal
  data rate of the payload (0A: 1 Mbit/s DBPSK; 14: 2 Mbit/s DQPSK)
Service Length
  future use, 00: 802.11 compliant  length of the payload
HEC (Header Error Check)
  protection of signal, service and length, x16+x12+x5+1
Notes: The SYNC field shall consist of 128 bits of scrambled 1 bit. This field shall be provided so that the receiver
can perform the necessary operations for synchronization.
The SFD shall be provided to indicate the start of PHY dependent parameters within the PLCP Preamble.
The SFD shall be a 16-bit field, X'F3A0' (msb to lsb). The lsb shall be transmitted Þrst in time.
The 8-bit IEEE 802.11 signal Þeld indicates to the PHY the modulation that shall be used for transmission
(and reception) of the MPDU. The data rate shall be equal to the Signal Þeld value multiplied by 100 kbit/s.

## Slide 13: 802.11 - MAC layer I - DFWMAC
Traffic services
  Asynchronous Data Service (mandatory)
    exchange of data packets based on “best-effort”
    support of broadcast and multicast
  Time-Bounded Service (optional)
    implemented using PCF (Point Coordination Function)
Access methods
  DFWMAC-DCF CSMA/CA (mandatory)
    collision avoidance via randomized „back-off“ mechanism
    minimum distance between consecutive packets
    ACK packet for acknowledgements (not for broadcasts)
  DFWMAC-DCF w/ RTS/CTS (optional)
    Distributed Foundation Wireless MAC
    avoids hidden terminal problem
  DFWMAC- PCF (optional)
    access point polls terminals according to a list

## Slide 14: 802.11 - MAC layer II
Priorities
  defined through different inter frame spaces
  SIFS (Short Inter Frame Spacing)
    highest priority, for ACK, CTS, polling response
  PIFS (PCF IFS)
    medium priority, for time-bounded service using PCF
  DIFS (DCF, Distributed Coordination Function IFS)
    lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS
Notes: aSIFSTime = aRxRFDelay + aRxPLCPDelay + aMACProcessingDelay + aRxTxTurnaroundTime.
aSlotTime = aCCATime + aRxTxTurnaroundTime + aAirPropagationTime + aMACProcessingDelay.
PIFS = aSIFSTime + aSlotTime
DIFS = aSIFSTime + 2aSlotTime
EIFS = aSIFSTime + (8 ACKSize) + aPreambleLength + aPLCPHeaderLngth+ DIFS
For DSSS:
aSlotTime 20 µs
aSIFSTime 10 µs
aCCATime < 15 µs
aRxTxTurnaroundTime <5 µs
SIFS =
PIFS =
DIFS =

## Slide 15: 802.11 - CSMA/CA access method I
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
  station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
  if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
  if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
  if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
slot time
direct access if medium is free  DIFS
Notes: <number>
Prof. Dr. Dr. h.c. G. Krüger
E. Dorner / Dr. J. Schiller
Universität Karlsruhe
Institut für Telematik
Mobilkommunikation
SS 1998
12

## Slide 16: 802.11 - competing stations - simple version
t
busy
boe
station1
station2
station3
station4
station5
packet arrival at MAC
DIFS
boe
boe
boe
busy
elapsed backoff time
bor
residual backoff time
busy
medium not idle (frame, ack etc.)
bor
bor
DIFS
boe
boe
boe
bor
DIFS
busy
busy
DIFS
boe
busy
boe
boe
bor
bor

## Slide 17: 802.11 - CSMA/CA access method II
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (CRC)
  automatic retransmission of data packets in case of transmission errors
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 18: 802.11 - DFWMAC
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  sender can now send data at once, acknowledgement via ACK
  other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 19: Fragmentation
t
SIFS
DIFS
data
ACK1
other
stations
receiver
sender
frag1
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)
NAV (frag1)
NAV (ACK1)
SIFS
ACK2
frag2
SIFS

## Slide 20: DFWMAC-PCF I
PIFS
stations‘
NAV
wireless
stations
point
coordinator
D1
U1
SIFS
NAV
SIFS
D2
U2
SIFS
SIFS
SuperFrame
t0
medium busy
t1

## Slide 21: DFWMAC-PCF II
t
stations‘
NAV
wireless
stations
point
coordinator
D3
NAV
PIFS
D4
U4
SIFS
SIFS
CFend
contention
period
contention free period
t2
t3
t4
7.20.1

## Slide 22: 802.11 - Frame format
Types
  control frames, management frames, data frames
Sequence numbers
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  sending time, checksum, frame control, data
Frame
Control
Duration
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Data
CRC
2
2
6
6
6
6
2
4
0-2312
bytes
Version, Type, Subtype, To DS, From DS, More Fragments, Retry,
Power Management, More Data, Wired Equivalent Privacy (WEP), and Order
Notes: There are three frame types: control (e.g., RTS/CTS/Ack), data, and management (e.g., association). Each of the frame types have several defined subtypes.
Sequence control: fragment number, sequence number (remains constant for the same frame/fragment)

## Slide 23: MAC address format
DS: Distribution System
AP: Access Point
DA: Destination Address (final recipient)
SA: Source Address (initiator)
BSSID: Basic Service Set Identifier
RA: Receiver Address (immediate recipient)
TA: Transmitter Address (immediate sender)

## Slide 24: 802.11 - MAC management
Synchronization
  try to find a LAN, try to stay within a LAN
  timer etc.
Power management
  sleep-mode without missing a message
  periodic sleep, frame buffering, traffic measurements
Association/Reassociation
  integration into a LAN
  roaming, i.e. change networks by changing access points
  scanning, i.e. active search for a network
MIB - Management Information Base
  managing, read, write
Notes: Each STA shall maintain a TSF timer with modulus 2 64 counting in increments of microseconds. STAs expect to receive beacons at a nominal rate. The interval between beacons is deÞned by the aBeaconPeriod parameter of the STA. A STA sending a beacon shall set the value of the beaconÕs timestamp so that it equals the value of the STAÕs TSF timer at the time that the Þrst bit of the timestamp is transmitted to the PHY plus the transmitting STAs delays through its local PHY from the MAC-PHY interface to its interface with the wireless medium (antenna, LED emission surface, etc.). The algorithms in this clause deÞne a mechanism that maintains the synchronization of the TSF timers in a BSS to within 4 µs plus the maximum propagation delay of the PHY for PHYs of 1 Mb/s, or greater.

## Slide 25: Synchronization using a Beacon (infrastructure)
beacon interval
t
medium
access
point
busy
B
busy
busy
busy
B
B
B
value of the timestamp
B
beacon frame

## Slide 26: Synchronization using a Beacon (ad-hoc)
t
medium
station1
busy
B1
beacon interval
busy
busy
busy
B1
value of the timestamp
B
beacon frame
station2
B2
B2
random delay

## Slide 27: Power management
Idea: switch the transceiver off if not needed
States of a station: sleep and awake
Timing Synchronization Function (TSF)
  stations wake up at the same time
Infrastructure
  Traffic Indication Map (TIM)
    list of unicast receivers transmitted by AP
  Delivery Traffic Indication Map (DTIM)
    list of broadcast/multicast receivers transmitted by AP
Ad-hoc
  Ad-hoc Traffic Indication Map (ATIM)
    announcement of receivers by stations buffering frames
    more complicated - no central AP
    collision of ATIMs possible (scalability?)

## Slide 28: Power saving with wake-up patterns (infrastructure)
TIM interval
t
medium
access
point
busy
D
busy
busy
busy
T
T
D
T
TIM
D
DTIM
DTIM interval
B
B
B
broadcast/multicast
station
awake
p
PS poll
p
d
d
d
data transmission
to/from the station
Notes: PS poll: Power Save poll

## Slide 29: Power saving with wake-up patterns (ad-hoc)
awake
A
transmit ATIM
D
transmit data
t
station1
B1
B1
B
beacon frame
station2
B2
B2
random delay
A
a
D
d
ATIM
window
beacon interval
a
acknowledge ATIM
d
acknowledge data

## Slide 30: 802.11 - Roaming
No or bad connection? Then perform:
Scanning
  scan the environment, i.e., listen into the medium for beacon signals (passive) or send probes (active) into the medium and wait for an answer
Reassociation Request
  station sends a request to one or several AP(s)
Reassociation Response
  success: AP has answered, station can now participate
  failure: continue scanning
AP accepts Reassociation Request
  signal the new station to the distribution system
  the distribution system updates its data base (i.e., location information)
  typically, the distribution system now informs the old AP so it can release resources
Notes: Active scanning vs. Passive scanning

## Slide 31: Future developments
IEEE 802.11a
  compatible MAC, but now 5 GHz band
  transmission rates higher than 20 Mbit/s
  close cooperation with BRAN (ETSI Broadband Radio Access Network)
IEEE 802.11b
  higher data rates at 2.4 GHz
  proprietary solutions already offer 11 Mbit/s
IEEE WPAN (Wireless Personal Area Networks)
  market potential
  compatibility
  low cost/power, small form factor

## Slide 32: Bluetooth
Consortium: Ericsson, Intel, IBM, Nokia, Toshiba - many other members
Scenarios:
  connection of peripheral devices
    loudspeaker, joystick, headset
  support of ad-hoc networking
    small devices, low-cost
  bridging of networks
    e.g., GSM via mobile phone - Bluetooth - laptop
Simple, cheap, replacement of IrDA, low range, lower data rates, low-power
  Worldwide operation: 2.4 GHz,
  Resistance to jamming and selective frequency fading:
    FHSS over 79 channels (of 1MHz each), 1600hops/s
  Coexistence of multiple piconets: CDMA
  Links: synchronous connections SCO (e.g., voice) and asynchronous connectionless ACL
  Interoperability: protocol stack supporting TCP/IP, OBEX, SDP
  Range: 10 meters, can be extended to 100 meters
Documentation: over 1000 pages specification:
www.ccs.neu.edu/course/com3525/ or from www.bluetooth.com

## Slide 33: Network Topology
Piconet = set of Bluetooth nodes synchronized to a master node
  The piconet hopping sequence is derived from the master MAC address (BD_ADDR IEEE802 48 bits compatible address)
Scatternet = set of piconet
Master-Slaves can switch roles
A node can only be master of one piconet. Why?
Piconet 1
Master
Master
Piconet 2
Scatternet
Slave

## Slide 34: Protocol Architecture
BT Radio (2.4 GHZ Freq. Band):
Modulation: Gaussian Frequency Shift Keying
Baseband: FH-SS (79 carriers), CDMA (hopping sequence from the node MAC address)
Audio: interfaces directly with the baseband. Each voice connection is over a 64Kbps SCO link. The voice coding scheme is the Continuous Variable Slope Delta (CVSD)
Link Manager Protocol (LMP): link setup and control, authentication and encryption
Host Controller Interface: provides a uniform method of access to the baseband, control registers, etc through USB, PCI, or UART
Logical Link Control and Adaptation Layer (L2CAP): higher protocols multiplexing, packet segmentation/reassembly, QoS
Service Discover Protocol (SDP): protocol of locating services provided by a Bluetooth device
Telephony Control Specification (TCS): defines the call control signaling for the establishment of speech and data calls between Bluetooth devices
RFCOMM: provides emulation of serial links (RS232). Upto 60 connections
HCI
Bluetooth Radio
Baseband
Audio
Link Manager (LMP)
L2CAP
RFCOMM
TCS
SDP
TCP/UDP
PPP
AT
Commands
OBEX
Application
OBEX: OBject EXchange (e.g., vCard)

## Slide 35: Bluetooth Piconet MAC
Each node has a Bluetooth Device Address (BD_ADDR). The master BD_ADDR determines the sequence of frequency hops
Types of connections:
  Synchronous Connection-Oriented link (SCO) (symmetrical, circuit switched, point-to-point)
  Asynchronous Connectionless Link (ACL): (packet switched, point-2-multipoint, master-polls)
Packet Format:
  Access code: synchronization, when piconet active derived from master
  Packet header (for ACL): 1/3-FEC, MAC address (1 master, 7 slaves), link type, alternating bit ARQ/SEQ, checksum
f(k)
f(k+1)
f(k+2)
f(k+3)
f(k+4)
f(k+4)
f(k+4)
f(k+7)
Master
Slave 1
Slave 2
bits
access code
packet header
payload
72
54
0-2745
bits
MAC address
type
flow
ARQN
SEQN
HEC
3
4
1
1
1
8
Notes: Slot duration: 625seconds
Why don’t we transmit during all the slot?

## Slide 36: Types of packets
SCO packets:
Do not have a CRC (except for the data part of DV) and are never retransmitted. Intended for High-quality Voice (HV).
ACL packets: Data Medium-rate (DM) and Data High-rate (DH)
Type
Payload
(bytes)
FEC
CRC
Symm.
max-rate kbps
HV1
10
1/3
No
64
HV2
20
2/3
No
64
HV3
30
No
No
64
DV
10+(1-10)D
2/3D
Yes D
64+57.6D
Type
Payload
(bytes)
FEC
CRC
Symm.
max-rate kbps
Asymm.
max-rate (DL/UL)
DM1
0-17
2/3
Yes
108.8
108.8/108.9
DM3
0-121
2/3
Yes
258.1
387.2/54.4
DM5
0-224
2/3
Yes
286.7
477.8/36.3
DH1
0-27
No
Yes
172.8
172.8/172.8
DH3
0-183
No
Yes
390.4
585.6/86.4
DH5
0-339
no
Yes
433.9
723.2/185.6

## Slide 37: States of a Bluetooth Device (PHY layer)
STANDBY
inquiry
page
connected
transmit
PARK
HOLD
SNIFF
unconnected
connecting
active
low power
BT device addressing:
BD_ADDR (48 bits)
AM_ADDR ( 3bits): ACTIVE, HOLD, or SNIFF
PM_ADDR (8 bits): PARK Mode address (exchanged with the AM_ADDR when entering PARK mode)
AR_ADDR (8 bits): not unique used to come back from PARK to ACTIVE state
ACTIVE (connected/transmit): the device is uniquely identified by a 3bits AM_ADDR and
is fully participating
SNIFF state: participates in the piconet only within the SNIFF interval
HOLD state: keeps only the SCO links
PARK state (low-power): releases AM_ADDR but stays synchronized with master

## Slide 38: Bluetooth Device Operation [Page 105 of 1084]
Inquiry:
  Goal: aims at discovering other neighboring devices
  Inquiring node:
    Sends an inquiry message (packet with only the access code: General Inquiry Access Code: GIAC or Dedicated IAC: DIAC). This message is sent over a subset of all possible frequencies.
    The inquiry frequencies are divided into two hopping sets of 16 frequencies each.
    In inquiry state the node will send upto NINQUIRY sequences on one set of 16 frequencies before switching to the other set of 16 frequencies. Upto 3 switches can be executed. Thus the inquiry may last upto 10.24 seconds.
  To be discovered node:
    Enters an inquiry_scan mode: listens over one frequency for Tw_inquiry_scal time
    When hearing the inquiry_message (and after a backoff procedure) enter and inquiry_response mode: send a Frequency Hop Sync (FHS) packet (BD_ADDR, native clock)
  After discovering the neighbors and collecting information on their address and clock, the inquiring node can start a page routine to setup a piconet

## Slide 39: Bluetooth Device Operation (Cont’d) [Page 102 of 1084]
Page:
  Goal: e.g., setup a piconet after an inquiry
  Paging node (master):
    Sends a page message (i.e., packet with only Device Access Code of paged node) over 32 frequency hops (from DAC and split into 2*16 freq.)
    Repeated until a response is received
    When a response is received send a FHS message to allow the paged node to synchronize
  Paged node (slave):
    Listens on its hopping sequence
    When receiving a page message, send a page_response and wait for the FHS of the pager

## Slide 40: Link Manager Protocol
Security: shared secret key
  Authentication: challenge response
  Weak Encryption: combination of (Linear Feedback Shift Registers) LFSR
Connections setup/release (SCO/ACL)
Master-slave switch
Power-control
Scheduling

## Slide 41: Scatternets
piconets
Each piconet has one master and up to 7 slaves
Master determines hopping sequence, slaves have to synchronize
Participation in a piconet = synchronization to hopping sequence
Communication between piconets = devices jumping back and forth between the piconets