## Slide 1: Wireless Networks: Network Protocols/Mobile IP
Motivation
Data transfer
Encapsulation
Security
IPv6
Problems
DHCP
Ad-hoc networks
Routing protocols
Adapted from J. Schiller, “Mobile Communications”

## Slide 2: Motivation for Mobile IP
Routing
  based on IP destination address, network prefix (e.g. 129.13.42) determines physical subnet
  change of physical subnet implies change of IP address to have a topological correct address (standard IP) or needs special entries in the routing tables
Specific routes to end-systems?
  change of all routing table entries to forward packets to the right destination
  does not scale with the number of mobile hosts and frequent changes in the location, security problems
Changing the IP-address?
  adjust the host IP address depending on the current location
  almost impossible to find a mobile system, DNS updates take too much time
  TCP connections break, security problems

## Slide 3: Requirements to Mobile IP (RFC 2002)
Transparency
  mobile end-systems keep their IP address
  continuation of communication after interruption of link possible
  point of connection to the fixed network can be changed
Compatibility
  support of the same layer 2 protocols as IP
  no changes to current end-systems and routers required
  mobile end-systems can communicate with fixed systems
Security
  authentication of all registration messages
Efficiency and scalability
  only little additional messages to the mobile system required (connection typically via a low bandwidth radio link)
  world-wide support of a large number of mobile systems in the whole Internet

## Slide 4: Terminology
Mobile Node (MN)
  system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
  system in the home network of the MN, typically a router
  registers the location of the MN, tunnels IP datagrams to the COA
Foreign Agent (FA)
  system in the current foreign network of the MN, typically a router
  forwards the tunneled datagrams to the MN, typically also the default router for the MN
Care-of Address (COA)
  address of the current tunnel end-point for the MN (at FA or MN)
  actual location of the MN from an IP point of view
  can be chosen, e.g., via DHCP
Correspondent Node (CN)
  communication partner

## Slide 5: Example network
mobile end-system
Internet
router
router
router
end-system
FA
HA
MN
home network
foreign network
(physical home network
for the MN)
(current physical network for the MN)
CN

## Slide 6: Data transfer to the mobile system
Internet
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
1. Sender sends to the IP address of MN,
HA intercepts packet (proxy ARP)
2. HA tunnels packet to COA, here FA,
by encapsulation
3. FA forwards the packet to the MN
CN

## Slide 7: Data transfer from the mobile system
Internet
receiver
FA
HA
MN
home network
foreign network
sender
1
1. Sender sends to the IP address of the receiver as usual, FA works as default router
CN

## Slide 8: Overview
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 9: Network integration
Agent Advertisement
  HA and FA periodically send advertisement messages into their physical subnets
  MN listens to these messages and detects, if it is in the home or a foreign network (standard case for home network)
  MN reads a COA from the FA advertisement messages
Registration (always limited lifetime!)
  MN signals COA to the HA via the FA, HA acknowledges via FA to MN
  these actions have to be secured by authentication
Advertisement
  HA advertises the IP address of the MN (as for fixed systems), i.e. standard routing information
  routers adjust their entries, these are stable for a longer time (HA responsible for a MN over a longer period of time)
  packets to the MN are sent to the HA,
  independent of changes in COA/FA

## Slide 10: Agent advertisement
preference level 1
router address 1
#addresses
type
addr. size
lifetime
checksum
COA 1
COA 2
type
sequence number
length
0
7
8
15
16
31
24
23
code
preference level 2
router address 2
. . .
registration lifetime
. . .
R
B
H
F
M
G
V
reserved
ICMP-Type = 0; Code = 0/16; Extension Type = 16

## Slide 11: Registration
t
MN
HA
registration
request
registration
reply
t
MN
FA
HA
registration
request
registration
request
registration
reply
registration
reply

## Slide 12: Mobile IP registration request
home agent
home address
type
lifetime
0
7
8
15
16
31
24
23
rsv
identification
COA
extensions . . .
S
B
D
M
G
V
UDP packet on port 343

## Slide 13: Encapsulation
original IP header
original data
new data
new IP header
outer header
inner header
original data

## Slide 14: Encapsulation I
Encapsulation of one packet into another as payload
  e.g. IPv6 in IPv4 (6Bone), Multicast in Unicast (Mbone)
  here: e.g. IP-in-IP-encapsulation, minimal encapsulation or GRE (Generic Record Encapsulation)
IP-in-IP-encapsulation (mandatory in RFC 2003)
  tunnel between HA and COA
Care-of address COA
IP address of HA
TTL
IP identification
IP-in-IP
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
TCP/UDP/ ... payload

## Slide 15: Encapsulation II
Minimal encapsulation (optional) [RFC2004]
  avoids repetition of identical fields
  e.g. TTL, IHL, version, TOS
  only applicable for unfragmented packets, no space left for fragment identification
care-of address COA
IP address of HA
TTL
IP identification
min. encap.
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
IP address of MN
original sender IP address (if S=1)
S
lay. 4 protoc.
IP checksum
TCP/UDP/ ... payload
reserved

## Slide 16: Generic Routing Encapsulation [RFC 1701]
original
header
original data
new data
new header
outer header
GRE header
original data
original header
Care-of address COA
IP address of HA
TTL
IP identification
GRE
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
TCP/UDP/ ... payload
routing (optional)
sequence number (optional)
key (optional)
offset (optional)
checksum (optional)
protocol
rec.
rsv.
ver.
C
R
K
S
s

## Slide 17: Optimization of packet forwarding
Triangular Routing
  sender sends all packets via HA to MN
  higher latency and network load
“Solutions”
  sender learns the current location of MN
  direct tunneling to this location
  HA informs a sender about the location of MN
  big security problems!
Change of FA
  packets on-the-fly during the change can be lost
  new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
  this information also enables the old FA to release resources for the MN

## Slide 18: Change of foreign agent
CN
HA
FAold
FAnew
MN
t
request
update
ACK
data
data
MN changes location
registration
update
ACK
data
data
data
warning
update
ACK
data
data
registration

## Slide 19: Reverse tunneling (RFC 2344)
Internet
receiver
FA
HA
MN
home network
foreign network
sender
3
2
1
1. MN sends to FA
2. FA tunnels packets to HA
by encapsulation
3. HA forwards the packet to the
receiver (standard case)
CN

## Slide 20: Mobile IP with reverse tunneling
Router accept often only “topological correct“ addresses (firewall!)
  a packet from the MN encapsulated by the FA is now topological correct
  furthermore multicast and TTL problems solved (TTL in the home network correct, but MN is to far away from the receiver)
Reverse tunneling does not solve
  problems with firewalls, the reverse tunnel can be abused to circumvent security mechanisms (tunnel hijacking)
  optimization of data paths, i.e. packets will be forwarded through the tunnel via the HA to a sender (double triangular routing)
The new standard is backwards compatible
  the extensions can be implemented easily and cooperate with current implementations without these extensions

## Slide 21: Mobile IP and IPv6
Mobile IP was developed for IPv4, but IPv6 simplifies the protocols
  security is integrated and not an add-on, authentication of registration is included
  COA can be assigned via auto-configuration (DHCPv6 is one candidate), every node has address autoconfiguration
  no need for a separate FA, all routers perform router advertisement which can be used instead of the special agent advertisement
  MN can signal a sender directly the COA, sending via HA not needed in this case (automatic path optimization)
  „soft“ hand-over, i.e. without packet loss, between two subnets is supported
    MN sends the new COA to its old router
    the old router encapsulates all incoming packets for the MN and forwards them to the new COA
    authentication is always granted

## Slide 22: Problems with mobile IP
Security
  authentication with FA problematic, for the FA typically belongs to another organization
  no protocol for key management and key distribution has been standardized in the Internet
  patent and export restrictions
Firewalls
  typically mobile IP cannot be used together with firewalls, special set-ups are needed (such as reverse tunneling)
QoS
  many new reservations in case of RSVP
  tunneling makes it hard to give a flow of packets a special treatment needed for the QoS
Security, firewalls, QoS etc. are topics of current research and discussions!

## Slide 23: Security in Mobile IP
Security requirements (Security Architecture for the Internet Protocol, RFC 1825, RFC 1826, RFC 1827)
  Integrity any changes to data between sender and receiver can be detected by the receiver
  Authentication sender address is really the address of the sender and all data received is really data sent by this sender
  Confidentiality only sender and receiver can read the data
  Non-Repudiation sender cannot deny sending of data
  Traffic Analysis creation of traffic and user profiles should not be possible
  Replay Protection receivers can detect replay of messages

## Slide 24: IP security architecture I
not encrypted
encrypted
Two or more partners have to negotiate security mechanisms to setup a security association
  typically, all partners choose the same parameters and mechanisms
Two headers have been defined for securing IP packets:
  Authentication-Header
    guarantees integrity and authenticity of IP packets
    if asymmetric encryption schemes are used, some non-repudiation level can also be provided
  Encapsulation Security Payload
    protects confidentiality between communication partners
Authentification-Header
IP-Header
UDP/TCP-Paket
authentication header
IP header
UDP/TCP data
ESP header
IP header
encrypted data

## Slide 25: IP security architecture II
Mobile Security Association for registrations
  parameters for the mobile host (MH), home agent (HA), and foreign agent (FA)
Extensions of the IP security architecture
  extended authentication of registration
  prevention of replays of registrations
    time stamps: 32 bit time stamps + 32 bit random number
    nonces: 32 bit random number (MH) + 32 bit random number (HA)
registration reply
registration request
registration request
MH
FA
HA
registration reply
MH-HA authentication
MH-FA authentication
FA-HA authentication

## Slide 26: Key distribution
Home agent distributes session keys
foreign agent has a security association with the home agent
mobile host registers a new binding at the home agent
home agent answers with a new session key for foreign agent and mobile node
FA
MH
HA
response:
EHA-FA {session key}
EHA-MH {session key}

## Slide 27: DHCP: Dynamic Host Configuration Protocol [RFC 2131]
Application
  simplification of installation and maintenance of networked computers
  supplies systems with all necessary information, such as IP address, DNS server address, domain name, subnet mask, default router etc.
  enables automatic integration of systems into an Intranet or the Internet, can be used to acquire a COA for Mobile IP
Client/Server-Model
  the client sends via a MAC broadcast a request to the DHCP server (might be via a DHCP relay)
client
relay
client
server
DHCPDISCOVER
DHCPDISCOVER

## Slide 28: DHCP - protocol mechanisms
time
server
(not selected)
client
server
(selected)
initialization
collection of replies
selection of configuration
initialization completed
release
confirmation of
configuration
delete context
determine the
configuration
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST (reject)
DHCPACK
DHCPRELEASE
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST (options)
determine the
configuration

## Slide 29: DHCP characteristics
Server
  several servers can be configured for DHCP, coordination not yet standardized (i.e., manual configuration)
Renewal of configurations
  IP addresses have to be requested periodically, simplified protocol
Options
  available for routers, subnet mask, NTP (network time protocol) timeserver, SLP (service location protocol) directory, DNS (domain name system)
Big security problems!
  no authentication of DHCP information specified yet
  <draft-ietf-dhc-authentication-16.txt:2001>

## Slide 30: Ad hoc networks
Standard Mobile IP needs an infrastructure
  Home Agent/Foreign Agent in the fixed network
  DNS, routing etc. are not designed for mobility
Sometimes there is no infrastructure!
  remote areas, ad-hoc meetings, disaster areas
  cost can also be an argument against an infrastructure!
Main topic: routing
  no default router available
  every node should be able to forward
A
B
C

## Slide 31: Routing examples for an ad-hoc network
N1
N4
N2
N5
N3
N1
N4
N2
N5
N3
good link
weak link
time = t1
time = t2

## Slide 32: Traditional routing algorithms
Distance Vector
  periodic exchange of messages with all physical neighbors that contain information about who can be reached at what distance
  selection of the shortest path if several paths available
Link State
  periodic notification of all routers about the current state of all physical links
  router get a complete picture of the network
Example
  ARPA packet radio network (1973), DV-Routing
  every 7.5s exchange of routing tables including link quality
  updating of tables also by reception of packets
  routing problems solved with limited flooding

## Slide 33: Problems of traditional routing algorithms
Dynamic of the topology
  frequent changes of connections, connection quality, participants
Limited performance of mobile systems
  periodic updates of routing tables need energy without contributing to the transmission of user data, sleep modes difficult to realize
  limited bandwidth of the system is reduced even more due to the exchange of routing information
  links can be asymmetric, i.e., they can have a direction dependent transmission quality
Problem
  protocols have been designed for fixed networks with infrequent changes and typically assume symmetric links

## Slide 34: DSDV (Destination Sequenced Distance Vector)
Routing Protocols: DSDV
Destination-Sequenced Distance Vector:
  Each node maintains a routing table listing:
    <dest, next-hop, metric, SeqNum>:
    The favored route is changed if a new route with higher SeqNum is received, or if the new route has equal SeqNum and lower metric
  Nodes send advertisement with evenly increased SeqNum
  When a node detects a broken link he sends an advertisement with  metric and SeqNum=PrevSeqNum+1
  Damping fluctuations:
    Fluctuations are due to out-of-order arrival of route advertisement
    Proposed solution: maintain a settling time estimation for routes
    Route with an  metric are advertised without delay

## Slide 35: Dynamic source routing I <draft-ietf-manet-dsr-05.txt:2001>
Split routing into discovering a path and maintaining a path
Discover a path
  only if a path for sending packets to a certain destination is needed and no path is currently available
Maintaining a path
  only while the path is in use, one has to make sure that it can be used continuously
No periodic updates needed!

## Slide 36: Dynamic source routing II
Path discovery
  broadcast a Route Request packet with destination address and unique ID
  if a station receives a broadcast packet
    if the station is the receiver (i.e., has the correct destination address) then return the packet to the sender (path was collected in the packet): Route Reply
    if the packet has already been received earlier (identified via ID) then discard the packet
    otherwise, append own address and broadcast packet
  sender receives packet with the current path (address list)
Optimizations
  limit broadcasting if maximum diameter of the network is known
  caching of address lists (i.e. paths) from passing packets (overhearing)
    stations can use the cached information for path discovery (own paths or paths for other hosts)

## Slide 37: Dynamic Source Routing III
Maintaining paths
  after sending a packet
    wait for a layer 2 acknowledgement (if applicable)
    listen into the medium to detect if other stations forward the packet (if possible)
    request an explicit acknowledgement
  if a station encounters problems it can inform the sender of a packet or look-up a new path locally

## Slide 38: Clustering of ad-hoc networks
Internet
super cluster
cluster

## Slide 39: Interference-based routing
Routing based on assumptions about interference between signals
S1
N5
N3
N4
N1
N2
R1
R2
N6
N8
S2
N9
N7
neighbors
(i.e. within radio range)

## Slide 40: Examples for interference based routing
Least Interference Routing (LIR)
  calculate the cost of a path based on the number of stations that can receive a transmission
Max-Min Residual Capacity Routing (MMRCR)
  calculate the cost of a path based on a probability function of successful transmissions and interference
Least Resistance Routing (LRR)
  calculate the cost of a path based on interference, jamming and other transmissions
LIR is very simple to implement, only information from direct neighbors is necessary