## Slide 1: Signal Encoding Techniques
Lecture 3
G. Noubir
noubir@ccs.neu.edu

## Slide 2: Reasons for Choosing Encoding Techniques
Digital data, digital signal
  Equipment less complex and expensive than digital-to-analog modulation equipment
Analog data, digital signal
  Permits use of modern digital transmission and switching equipment
Notes: What is modulation?
  Mapping a digital sequence of information bits into an analog signal suitable for transmission over the communication medium (channel)
  Process during which the amplitude, frequency, or the phase of a carrier changes in accordance with the information to be transmitted
  Modulation associates each n bits to a signal Si(t) chosen among M = 2n signals
Baseband transmission versus carrier modulation transmission
  Baseband: signal within [0, fs] (e.g., cable)
  Carrier modulation: signal within [f-fs, f+fs]
Basic modulation schemes:
  Amplitude modulation, Phase modulation, Frequency modulation

## Slide 3: Reasons for Choosing Encoding Techniques
Digital data, analog signal
  Some transmission media will only propagate analog signals
  E.g., optical fiber and unguided media
Analog data, analog signal
  Analog data in electrical form can be transmitted easily and cheaply
  Done with voice transmission over voice-grade lines

## Slide 4: Signal Encoding Criteria
What determines how successful a receiver will be in interpreting an incoming signal?
  Signal-to-noise ratio
  Data rate
  Bandwidth
An increase in data rate increases bit error rate
An increase in SNR decreases bit error rate
An increase in bandwidth allows an increase in data rate

## Slide 5: Factors Used to Compare Encoding Schemes
Signal spectrum
  With lack of high-frequency components
    => less bandwidth required
  With no dc (direct current) component
    => ac coupling via transformer possible (electrical isolation)
  Transfer function of a channel is worse near band edges
    => concentrate transmitted power in the middle
Clocking
  Ease of determining beginning and end of each bit position

## Slide 6: Factors Used to Compare Encoding Schemes
Signal interference and noise immunity
  Performance in the presence of noise
Cost and complexity
  The higher the signal rate to achieve a given data rate, the greater the cost

## Slide 7: Basic Encoding Techniques
Digital data to analog signal
  Amplitude-shift keying (ASK)
    Amplitude difference of carrier frequency
  Frequency-shift keying (FSK)
    Frequency difference near carrier frequency
  Phase-shift keying (PSK)
    Phase of carrier signal shifted

## Slide 8: Basic Encoding Techniques

## Slide 9: Amplitude-Shift Keying
One binary digit represented by presence of carrier, at constant amplitude
Other binary digit represented by absence of carrier
    where the carrier signal is Acos(2πfct)

## Slide 10: Amplitude-Shift Keying
Susceptible to sudden gain changes
Inefficient modulation technique
On voice-grade lines, used up to 1200 bps
Used to transmit digital data over optical fiber

## Slide 11: Binary Frequency-Shift Keying (BFSK)
Two binary digits represented by two different frequencies near the carrier frequency
    where f1 and f2 are offset from carrier frequency fc by equal but opposite amounts

## Slide 12: Binary Frequency-Shift Keying (BFSK)
Less susceptible to error than ASK
On voice-grade lines, used up to 1200bps
Used for high-frequency (3 to 30 MHz) radio transmission
Can be used at higher frequencies on LANs that use coaxial cable

## Slide 13: Multiple Frequency-Shift Keying (MFSK)
More than two frequencies are used
More bandwidth efficient but more susceptible to error
    f i = f c + (2i – 1 – M)f d
    f c = the carrier frequency
    f d = the difference frequency
    M = number of different signal elements = 2 L
    L = number of bits per signal element

## Slide 14: Multiple Frequency-Shift Keying (MFSK)

## Slide 15: Multiple Frequency-Shift Keying (MFSK)
To match data rate of input bit stream, each output signal element is held for:
  Ts=LT seconds
    where T is the bit period (data rate = 1/T)
One signal element encodes L bits

## Slide 16: Multiple Frequency-Shift Keying (MFSK)
Total bandwidth required
  2Mfd
Minimum frequency separation required 2fd=1/Ts
Therefore, modulator requires a bandwidth of
  Wd=2L/LT=M/Ts

## Slide 17: Phase-Shift Keying (PSK)
Two-level PSK (BPSK)
  Uses two phases to represent binary digits

## Slide 18: Phase-Shift Keying (PSK)
Differential PSK (DPSK)
  Phase shift with reference to previous bit
    Binary 0 – signal burst of same phase as previous signal burst
    Binary 1 – signal burst of opposite phase to previous signal burst

## Slide 19: Phase-Shift Keying (PSK)
Four-level PSK (QPSK)
  Each element represents more than one bit

## Slide 20: Phase-Shift Keying (PSK)
Multilevel PSK
  Using multiple phase angles with each angle having more than one amplitude, multiple signals elements can be achieved
    D = modulation rate, baud
    R = data rate, bps
    M = number of different signal elements = 2L
    L = number of bits per signal element

## Slide 21: Performance
Bandwidth of modulated signal (BT)
  ASK, PSK BT=(1+r)R
  FSK BT=2DF+(1+r)R
    R = bit rate
    0 < r < 1; related to how signal is filtered
    DF = f2-fc=fc-f1

## Slide 22: Performance
Bandwidth of modulated signal (BT)
  MPSK
  MFSK
    L = number of bits encoded per signal element
    M = number of different signal elements

## Slide 23: Quadrature Amplitude Modulation
QAM is a combination of ASK and PSK
  Two different signals sent simultaneously on the same carrier frequency

## Slide 24: Quadrature Amplitude Modulation

## Slide 25: Additive White Gaussian Noise
Noise:
  As previously seen, noise has several sources
  Thermal noise source is the motion of electrons in amplifiers and circuits
  Its statistics were determined using quantum mechanics
  It is flat for all frequencies up to 1012Hz.
  We generally call it: Additive White Gaussian Noise (AWGN)
  Its probability density function (pdf) (zero mean noise voltage): (2=N0/2)
Notes: Interleaver transform non awgn into awgn
Sigma^2 = N0/2

## Slide 26: Bit Error Rate [Sklar1988]
BER for coherently detected BPSK:
BER for coherently detected BFSK:

## Slide 27: Reasons for Analog Modulation
Modulation of digital signals
  When only analog transmission facilities are available, digital to analog conversion required
Modulation of analog signals
  A higher frequency may be needed for effective transmission
  Modulation permits frequency division multiplexing

## Slide 28: Basic Encoding Techniques
Analog data to analog signal
  Amplitude modulation (AM)
  Angle modulation
    Frequency modulation (FM)
    Phase modulation (PM)

## Slide 29: Amplitude Modulation
Amplitude Modulation
    cos2fct = carrier
    x(t) = input signal
    na = modulation index
      Ratio of amplitude of input signal to carrier
  a.k.a double sideband transmitted carrier (DSBTC)

## Slide 30: Spectrum of AM signal

## Slide 31: Amplitude Modulation
Transmitted power
    Pt = total transmitted power in s(t)
    Pc = transmitted power in carrier

## Slide 32: Single Sideband (SSB)
Variant of AM is single sideband (SSB)
  Sends only one sideband
  Eliminates other sideband and carrier
Advantages
  Only half the bandwidth is required
  Less power is required
Disadvantages
  Suppressed carrier can’t be used for synchronization purposes

## Slide 33: Angle Modulation
Angle modulation
Phase modulation
  Phase is proportional to modulating signal
    np = phase modulation index

## Slide 34: Angle Modulation
Frequency modulation
  Derivative of the phase is proportional to modulating signal
    nf = frequency modulation index

## Slide 35: Angle Modulation
Compared to AM, FM and PM result in a signal whose bandwidth:
  is also centered at fc
  but has a magnitude that is much different
    Angle modulation includes cos( (t)) which produces a wide range of frequencies
Thus, FM and PM require greater bandwidth than AM

## Slide 36: Angle Modulation
Carson’s rule
  where
The formula for FM becomes

## Slide 37: Basic Encoding Techniques
Analog data to digital signal
  Pulse code modulation (PCM)
  Delta modulation (DM)

## Slide 38: Analog Data to Digital Signal
Once analog data have been converted to digital signals, the digital data:
  can be transmitted using NRZ-L
  can be encoded as a digital signal using a code other than NRZ-L
  can be converted to an analog signal, using previously discussed techniques

## Slide 39: Pulse Code Modulation
Based on the sampling theorem
Each analog sample is assigned a binary code
  Analog samples are referred to as pulse amplitude modulation (PAM) samples
The digital signal consists of block of n bits, where each n-bit number is the amplitude of a PCM pulse

## Slide 40: Pulse Code Modulation

## Slide 41: Pulse Code Modulation
By quantizing the PAM pulse, original signal is only approximated
Leads to quantizing noise
Signal-to-noise ratio for quantizing noise
Thus, each additional bit increases SNR by 6 dB, or a factor of 4

## Slide 42: Delta Modulation
Analog input is approximated by staircase function
  Moves up or down by one quantization level () at each sampling interval
The bit stream approximates derivative of analog signal (rather than amplitude)
  1 is generated if function goes up
  0 otherwise

## Slide 43: Delta Modulation

## Slide 44: Delta Modulation
Two important parameters
  Size of step assigned to each binary digit ()
  Sampling rate
Accuracy improved by increasing sampling rate
  However, this increases the data rate
Advantage of DM over PCM is the simplicity of its implementation

## Slide 45: Reasons for Growth of Digital Techniques
Growth in popularity of digital techniques for sending analog data
  Repeaters are used instead of amplifiers
    No additive noise
  TDM is used instead of FDM
    No intermodulation noise
  Conversion to digital signaling allows use of more efficient digital switching techniques

## Slide 46: Spread Spectrum

## Slide 47: Spread Spectrum
Input is fed into a channel encoder
  Produces analog signal with narrow bandwidth
Signal is further modulated using sequence of digits
  Spreading code or spreading sequence
  Generated by pseudonoise, or pseudo-random number generator
Effect of modulation is to increase bandwidth of signal to be transmitted

## Slide 48: Spread Spectrum
On receiving end, digit sequence is used to demodulate the spread spectrum signal
Signal is fed into a channel decoder to recover data

## Slide 49: Spread Spectrum

## Slide 50: Spread Spectrum
What can be gained from apparent waste of spectrum?
  Immunity from various kinds of noise and multipath distortion
  Can be used for hiding and encrypting signals
  Several users can independently use the same higher bandwidth with very little interference

## Slide 51: Frequency Hoping Spread Spectrum (FHSS)
Signal is broadcast over seemingly random series of radio frequencies
  A number of channels allocated for the FH signal
  Width of each channel corresponds to bandwidth of input signal
Signal hops from frequency to frequency at fixed intervals
  Transmitter operates in one channel at a time
  Bits are transmitted using some encoding scheme
  At each successive interval, a new carrier frequency is selected

## Slide 52: Frequency Hoping Spread Spectrum
Channel sequence dictated by spreading code
Receiver, hopping between frequencies in synchronization with transmitter, picks up message
Advantages
  Eavesdroppers hear only unintelligible blips
  Attempts to jam signal on one frequency succeed only at knocking out a few bits

## Slide 53: Frequency Hoping Spread Spectrum

## Slide 54: FHSS Using MFSK
MFSK signal is translated to a new frequency every Tc seconds by modulating the MFSK signal with the FHSS carrier signal
For data rate of R:
  duration of a bit: T = 1/R seconds
  duration of signal element: Ts = LT seconds
Tc  Ts - slow-frequency-hop spread spectrum
Tc < Ts - fast-frequency-hop spread spectrum

## Slide 55: FHSS Performance Considerations
Large number of frequencies used
Results in a system that is quite resistant to jamming
  Jammer must jam all frequencies
  With fixed power, this reduces the jamming power in any one frequency band

## Slide 56: Direct Sequence Spread Spectrum (DSSS)
Each bit in original signal is represented by multiple bits in the transmitted signal
Spreading code spreads signal across a wider frequency band
  Spread is in direct proportion to number of bits used
One technique combines digital information stream with the spreading code bit stream using exclusive-OR (Figure 7.6)

## Slide 57: Direct Sequence Spread Spectrum (DSSS)

## Slide 58: DSSS Using BPSK
Multiply BPSK signal,
  sd(t) = A d(t) cos(2 fct)
by c(t) [takes values +1, -1] to get
  s(t) = A d(t)c(t) cos(2 fct)
    A = amplitude of signal
    fc = carrier frequency
    d(t) = discrete function [+1, -1]
At receiver, incoming signal multiplied by c(t)
  Since, c(t) x c(t) = 1, incoming signal is recovered

## Slide 59: DSSS Using BPSK

## Slide 60: Code-Division Multiple Access (CDMA)
Basic Principles of CDMA
  D = rate of data signal
  Break each bit into k chips
    Chips are a user-specific fixed pattern
  Chip data rate of new channel = kD

## Slide 61: CDMA Example
If k=6 and code is a sequence of 1s and -1s
  For a ‘1’ bit, A sends code as chip pattern
    <c1, c2, c3, c4, c5, c6>
  For a ‘0’ bit, A sends complement of code
    <-c1, -c2, -c3, -c4, -c5, -c6>
Receiver knows sender’s code and performs electronic decode function
    <d1, d2, d3, d4, d5, d6> = received chip pattern
    <c1, c2, c3, c4, c5, c6> = sender’s code

## Slide 62: CDMA Example
User A code = <1, –1, –1, 1, –1, 1>
  To send a 1 bit = <1, –1, –1, 1, –1, 1>
  To send a 0 bit = <–1, 1, 1, –1, 1, –1>
User B code = <1, 1, –1, – 1, 1, 1>
  To send a 1 bit = <1, 1, –1, –1, 1, 1>
Receiver receiving with A’s code
  (A’s code) x (received chip pattern)
    User A ‘1’ bit: 6 -> 1
    User A ‘0’ bit: -6 -> 0
    User B ‘1’ bit: 0 -> unwanted signal ignored

## Slide 63: CDMA for Direct Sequence Spread Spectrum

## Slide 64: Categories of Spreading Sequences
Spreading Sequence Categories
  PN sequences
  Orthogonal codes
For FHSS systems
  PN sequences most common
For DSSS systems not employing CDMA
  PN sequences most common
For DSSS CDMA systems
  PN sequences
  Orthogonal codes

## Slide 65: PN Sequences
PN generator produces periodic sequence that appears to be random
PN Sequences
  Generated by an algorithm using initial seed
  Sequence isn’t statistically random but will pass many test of randomness
  Sequences referred to as pseudorandom numbers or pseudonoise sequences
  Unless algorithm and seed are known, the sequence is impractical to predict

## Slide 66: Important PN Properties
Randomness
  Uniform distribution
    Balance property
    Run property
  Independence
  Correlation property
Unpredictability

## Slide 67: Linear Feedback Shift Register Implementation

## Slide 68: Example of M-Sequence
[A3, A2, A1, A0] = [0, 0, 1, 1]
Initial State = 1 0 0 0
M-Sequence: 0001001101011110

## Slide 69: Properties of M-Sequences
Property 1:
  Has 2n-1 ones and 2n-1-1 zeros
Property 2:
  For a window of length n slid along output for N (=2n-1) shifts, each n-tuple appears once, except for the all zeros sequence
Property 3:
  Sequence contains one run of ones, length n
  One run of zeros, length n-1
  One run of ones and one run of zeros, length n-2
  Two runs of ones and two runs of zeros, length n-3
  2n-3 runs of ones and 2n-3 runs of zeros, length 1

## Slide 70: Properties of M-Sequences
Property 4:
  The periodic autocorrelation of a ±1 m-sequence is

## Slide 71: Definitions
Correlation
  The concept of determining how much similarity one set of data has with another
  Range between –1 and 1
    1 The second sequence matches the first sequence
    0 There is no relation at all between the two sequences
    -1 The two sequences are mirror images
Cross correlation
  The comparison between two sequences from different sources rather than a shifted copy of a sequence with itself

## Slide 72: Advantages of Cross Correlation
The cross correlation between an m-sequence and noise is low
  This property is useful to the receiver in filtering out noise
The cross correlation between two different m-sequences is low
  This property is useful for CDMA applications
  Enables a receiver to discriminate among spread spectrum signals generated by different m-sequences

## Slide 73: Gold Sequences
Gold sequences constructed by the XOR of two m-sequences with the same clocking
Codes have well-defined cross correlation properties
Only simple circuitry needed to generate large number of unique codes
In following example (Figure 7.16a) two shift registers generate the two m-sequences and these are then bitwise XORed
Notes: Use preferred pairs of m-sequences

## Slide 74: Gold Sequences

## Slide 75: Gold Sequences
Select a preferred pair of m-sequences
  a m-sequence of period N=2n-1
  a’ = a[q] decimation of a
    gcd(q, n) = 1
    n/4  0
    q is odd and q = (2k+1) or q = (22k-2k+1) for some k
    gcd(n, k) = 1 for n odd; 2 for n=2 mod 4
  Gold codes ={a, a’, a  a’, a  Da’, a  D2a’, a  DN-1a’}
Cross correlation bounded by:
  |R| <= [2(n+1)/2+1]/N for n odd
  |R|<= [2(n+2)/2+1]/N for n even

## Slide 76: Example
a generated by 0 1 0 0 1:
  1111100011011101010000100101100
a’ generated by 0 1 1 1 1:
  1111100100110000101101010001110
O-shift XOR:
  0000000111101101111101110100010

## Slide 77: Orthogonal Codes
Orthogonal codes
  All pairwise cross correlations are zero
  Fixed- and variable-length codes used in CDMA systems
  For CDMA application, each mobile user uses one sequence in the set as a spreading code
    Provides zero cross correlation among all users
Types
  Walsh codes
  Variable-Length Orthogonal codes

## Slide 78: Walsh Codes
Set of Walsh codes of length n consists of the n rows of an n ´ n Walsh matrix:
  W1 = (0)
    n = dimension of the matrix
  Every row is orthogonal to every other row and to the logical not of every other row
  Requires tight synchronization
    Cross correlation between different shifts of Walsh sequences is not zero

## Slide 79: Typical Multiple Spreading Approach
Spread data rate by an orthogonal code (channelization code)
  Provides mutual orthogonality among all users in the same cell
Further spread result by a PN sequence (scrambling code)
  Provides mutual randomness (low cross correlation) between users in different cells

## Slide 80: Barker Code – 11 chips
Used in IEEE802.11 at 1 and 2 Mbps
Sequence: -1 -1 -1 1 1 1 -1 1 1 -1 1
Shifted by 3: 1 –1 1 -1 -1 -1 1 1 1 -1 1
Auto correlation: 1
Cross with shifted version: -1/11