## Slide 1: Coding and Error Control
Lecture 4
G. Noubir
noubir@ccs.neu.edu
Textbook: Chapter 8, “Wireless Communications and Networks”, William Stallings, Prentice Hall

## Slide 2: Coping with Data Transmission Errors
Error detection codes
  Detects the presence of an error
Automatic repeat request (ARQ) protocols
  Block of data with error is discarded
  Transmitter retransmits that block of data
Error correction codes, or forward correction codes (FEC)
  Designed to detect and correct errors

## Slide 3: Error Detection Probabilities
Definitions
    Pb : Probability of single bit error (BER)
    P1 : Probability that a frame arrives with no bit errors
    P2 : While using error detection, the probability that a frame arrives with one or more undetected errors
    P3 : While using error detection, the probability that a frame arrives with one or more detected bit errors but no undetected bit errors

## Slide 4: Error Detection Probabilities
With no error detection
    F = Number of bits per frame

## Slide 5: Error Detection Process
Transmitter
  For a given frame, an error-detecting code (check bits) is calculated from data bits
  Check bits are appended to data bits
Receiver
  Separates incoming frame into data bits and check bits
  Calculates check bits from received data bits
  Compares calculated check bits against received check bits
  Detected error occurs if mismatch

## Slide 6: Error Detection Process

## Slide 7: Parity Check
Parity bit appended to a block of data
Even parity
  Added bit ensures an even number of 1s
Odd parity
  Added bit ensures an odd number of 1s
Example, 7-bit character [1110001]
  Even parity [11100010]
  Odd parity [11100011]

## Slide 8: Cyclic Redundancy Check (CRC)
Transmitter
  For a k-bit block, transmitter generates an (n-k)-bit frame check sequence (FCS)
  Resulting frame of n bits is exactly divisible by predetermined number
Receiver
  Divides incoming frame by predetermined number
  If no remainder, assumes no error

## Slide 9: CRC using Modulo 2 Arithmetic
Exclusive-OR (XOR) operation
Parameters:
    T = n-bit frame to be transmitted
    D = k-bit block of data; the first k bits of T
    F = (n – k)-bit FCS; the last (n – k) bits of T
    P = pattern of n–k+1 bits; this is the predetermined divisor
    Q = Quotient
    R = Remainder

## Slide 10: CRC using Modulo 2 Arithmetic
For T/P to have no remainder, start with
Divide 2n-kD by P gives quotient and remainder
Use remainder as FCS

## Slide 11: CRC using Modulo 2 Arithmetic
Does R cause T/P have no remainder?
Substituting,
  No remainder, so T is exactly divisible by P

## Slide 12: Example
D = 1010001101 (k = 10)
P = 110101 (n-k=5)
R = 01110

## Slide 13: CRC using Polynomials
All values expressed as polynomials
  Dummy variable X with binary coefficients

## Slide 14: CRC using Polynomials
Widely used versions of P(X)
  CRC–12
    X12 + X11 + X3 + X2 + X + 1
  CRC–16
    X16 + X15 + X2 + 1
  CRC – CCITT
    X16 + X12 + X5 + 1
  CRC – 32
    X32 + X26 + X23 + X22 + X16 + X12 + X11 + X10 + X8 + X7 + X5 + X4 + X2 + X + 1

## Slide 15: CRC using Digital Logic
Dividing circuit consisting of:
  XOR gates
    Up to n – k XOR gates
    Presence of a gate corresponds to the presence of a term in the divisor polynomial P(X)
  A shift register
    String of 1-bit storage devices
    Register contains n – k bits, equal to the length of the FCS

## Slide 16: Digital Logic CRC

## Slide 17: Wireless Transmission Errors
Error detection requires retransmission
Detection inadequate for wireless applications
  Error rate on wireless link can be high, results in a large number of retransmissions
  Long propagation delay compared to transmission time

## Slide 18: Block Error Correction Codes
Transmitter
  Forward error correction (FEC) encoder maps each k-bit block into an n-bit block codeword
  Codeword is transmitted; analog for wireless transmission
Receiver
  Incoming signal is demodulated
  Block passed through an FEC decoder

## Slide 19: Forward Error Correction Process

## Slide 20: FEC Decoder Outcomes
No errors present
  Codeword produced by decoder matches original codeword
Decoder detects and corrects bit errors
Decoder detects but cannot correct bit errors; reports uncorrectable error
Decoder detects no bit errors, though errors are present

## Slide 21: Block Code Principles
Hamming distance – for 2 n-bit binary sequences, the number of different bits
  E.g., v1=011011; v2=110001; d(v1, v2)=3
Redundancy – ratio of redundant bits to data bits
Code rate – ratio of data bits to total bits

## Slide 22: Block Codes
The Hamming distance d of a Block code is the minimum distance between two code words
Error Detection:
  Upto d-1 errors
Error Correction:
  Upto
Combine: d2+l+1

## Slide 23: Coding Gain
Definition:
  The coding gain is the amount of additional SNR or Eb/N0 that would be required to provide the same BER performance for an uncoded signal
If the code is capable of correcting at most t errors and PUC is the BER of the channel without coding, then the probability that a bit is in error using coding is:
Notes: Application for Puc = 10-3
Useful if errors are not happening in bursts: if always 2 bits in error
Golay code

## Slide 24: Coding Gain

## Slide 25: Hamming Code
Designed to correct single bit errors
Family of (n, k) block error-correcting codes with parameters:
  Block length: n = 2m – 1
  Number of data bits: k = 2m – m – 1
  Number of check bits: n – k = m
  Minimum distance: dmin = 3
Single-error-correcting (SEC) code
  SEC double-error-detecting (SEC-DED) code

## Slide 26: Example of Binary Block Code (7, 4)
Any two different code words are different on at least three different coordinates. This code has Hamming distance 3.
Notice that the last 4 bits of the code word are the same as the message
  This is a systematic coding
  The other 3 bits are redundancy bits
If initial BER = 10-3 =>

## Slide 27: Hamming Code Process
Encoding: k data bits + (n -k) check bits
Decoding: compares received (n -k) bits with calculated (n -k) bits using XOR
  Resulting (n -k) bits called syndrome word
  Syndrome range is between 0 and 2(n-k)-1
  Each bit of syndrome indicates a match (0) or conflict (1) in that bit position

## Slide 28: Linear Block
A block code of length n and 2k code words is called a linear (n, k) code iff its 2k code words form a k-dimensional subspace of the vector space of all n-tuples over the field GF(2)
Informal Meaning: linear combinations of codewords are also codewords
The linear code is completely specified by k independent codewords (G generator matrix)
The encoder needs only to store the matrix G
Example: Linear code (7, 4)
To encode u = (1 1 0 1): v = 1g0 + 1g1 + 0g2 + 1g3

## Slide 29: Parity-Check Matrix (H)
For every kxn generator matrix G (with k linearly independent rows), there exists a (n-k)xn matrix H (with (n-k) linearly independent rows) called parity check matrix such that: any vector in the row space of G is orthogonal to any row of H and any vector that is orthogonal to all the rows of H is in the row space of G:
The 2n-k combinations of the rows of H form an (n-k)-dimensional subspace. It is the null space of C the (n, k) code generated by G. It is called the dual space of C and noted Cd.
For any v in C and w in Cd we have v w = 0

## Slide 30: Systematic Coding
A linear block code is called systematic iff the code words can be divided into two parts: Message part (k bits), and a redundancy checking part (n-k bits)
Systematic code generator matrix: G = [P Ik]; H = [In-k PT]; GHT=0
Redundant Checking part
Message part
n-k digits
k digits

## Slide 31: Hamming Codes (2m-1, 2m-m-1)
Parameters of Hamming codes (m>2):
  Code length: n = 2m-1
  Number of information bits: k = 2m-m-1
  Number of parity check bits: n-k = m
  Minimum distance: 3
  Error-correcting capability: t = (3-1)/2 = 1
Parity check matrix of a Hamming code: H = [Im Q]
  Im is the identity matrix mxm
  Q consists of 2m-m-1 columns which are the m-tuples of weight 2 or more
  Example:

## Slide 32: Minimum Distance of Block Codes
The minimum distance dmin of a block code is the minimum distance between any two code words:
  dmin = min {d(v, w), s.t. v, w C, v  w}
  dmin = min {w(v + w), s.t. v, w C, v  w}
  dmin = min {w(x), s.t. x C, x  0} (because C is a vector sub-space)
Example: Minimum Distance of Hamming Codes?

## Slide 33: Cyclic Linear Block Codes
Definition:
  An (n, k) linear code C is called a cyclic code if every cyclic shift of a code vector in C is also a code vector
  Codewords can be represented as polynomials of degree n. For a cyclic code all codewords are multiple of some polynomial g(X) modulo Xn+1 such that g(X) divides Xn+1. g(X) is called the generator polynomial.
Examples:
  Hamming codes, Golay Codes, BCH codes, RS codes
  BCH codes were independently discovered by Hocquenghem (1959) and by Bose and Chaudhuri (1960)
  Reed-Solomon codes (non-binary BCH codes) were independently introduced by Reed-Solomon

## Slide 34: Cyclic Codes
Can be encoded and decoded using linear feedback shift registers (LFSRs)
For cyclic codes, a valid codeword (c0, c1, …, cn-1), shifted right one bit, is also a valid codeword (cn-1, c0, …, cn-2)
Takes fixed-length input (k) and produces fixed-length check code (n-k)
  In contrast, CRC error-detecting code accepts arbitrary length input for fixed-length check code

## Slide 35: Cyclic Block Codes
A cyclic Hamming code of length 2m-1 with m>2 is generated by a primitive polynomial p(X) of degree m
Hamming code (31, 26)
  g(X) = 1 + X2 + X5, l = 3
Golay Code:
  cyclic code (23, 12)
  minimum distance 7
  generator polynomials: either g1(X) or g2(X)

## Slide 36: BCH Codes
For positive pair of integers m and t, a (n, k) BCH code has parameters:
  Block length: n = 2m – 1
  Number of check bits: n – k  mt
  Minimum distance:dmin  2t + 1
Correct combinations of t or fewer errors
Flexibility in choice of parameters
  Block length, code rate

## Slide 37: Bose Chaudhuri and Hocquenghem (BCH) Codes
For any positive integer m (m>2) and t (t<2m-1), there exists a BCH code:
  Block length: 2m-1
  Parity bits: n - k  mt
  Minimum distance: dmin  2t + 1
  generator polynomial is the lowest-degree polynomial over GF(2) such that:
  , 2,  3, …, 2t are its roots.  is the primitive root of unity in the extension field GF(2n).
Such a BCH code is capable of correcting t errors
The generator polynomial is:
  g(X) = LCM{1(X), 2(X), …, 2t(X)}
  for i = i’2l, i(X) = i’(X) (because i and i’ are conjugates), thus
  g(X) = LCM{1(X), 3(X), …, 2t-1(X)}
Since any minimal polynomial has degree m or less, then degree (n - k) of g is at most mt
If t = 1, then g is a primitive polynomial and we have a Hamming code
Notes: Reed-Solomon Codes are a special case of BCH codes

## Slide 38: Reed-Solomon Codes
Subclass of nonbinary BCH codes
Data processed in chunks of m bits, called symbols
An (n, k) RS code has parameters:
  Symbol length: m bits per symbol
  Block length: n = 2m – 1 symbols = m(2m – 1) bits
  Data length: k symbols
  Size of check code: n – k = 2t symbols = m(2t) bits
  Minimum distance: dmin = 2t + 1 symbols

## Slide 39: Block Interleaving
Data written to and read from memory in different orders
Data bits and corresponding check bits are interspersed with bits from other blocks
At receiver, data are deinterleaved to recover original order
A burst error that may occur is spread out over a number of blocks, making error correction possible

## Slide 40: Block Interleaving

## Slide 41: Convolutional Codes
Generates redundant bits continuously
Error checking and correcting carried out continuously
  (n, k, K) code
    Input processes k bits at a time
    Output produces n bits for every k input bits
    K = constraint factor
    k and n generally very small
  n-bit output of (n, k, K) code depends on:
    Current block of k input bits
    Previous K-1 blocks of k input bits

## Slide 42: Convolutional Encoder

## Slide 43: Decoding
Trellis diagram – expanded encoder diagram
Viterbi code – error correction algorithm
  Compares received sequence with all possible transmitted sequences
  Algorithm chooses path through trellis whose coded sequence differs from received sequence in the fewest number of places
  Once a valid path is selected as the correct path, the decoder can recover the input data bits from the output code bits

## Slide 44: Representations of Convolutional Codes
Trellis representation:
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11

## Slide 45: Viterbi Decoding Algorithm
Principle:
  Computes a measure of similarity (distance) between the received signal and all potential trellis paths
  For each state keeps only one “more likely” path
Algorithm:
  For each input
    For each state:
      Determine the distance/weight of the branches leading to it
      Keep only the best branch
    If all surviving paths at time ti pass through some state S at time ti-j then commit to S(ti-j)

## Slide 46: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 1 0 1 1 0 1 1 0 1 0

## Slide 47: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0

## Slide 48: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2

## Slide 49: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3

## Slide 50: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3
2
2
3
1

## Slide 51: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3
2
2
3
1
3
3
1
2

## Slide 52: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3
2
2
3
1
3
3
1
2
3
1
3
3

## Slide 53: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3
2
2
3
1
3
3
1
2
3
1
3
3
4
4
3
1

## Slide 54: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3
2
2
3
1
3
3
1
2
3
1
3
3
4
4
3
1
4
4
1
3

## Slide 55: Viterbi Decoding
Input: 1 1 0 1 1 0 1 1 0 1 0
Codeword: 11 01 01 00 01 01 00 01 01 00 10
Received: 11 01 01 01 01 01 00 01 01 00 10
00
11
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
00
11
10
01
States
00
10
01
11
1 0 1 1 0 1 1 0 1 0
11 01 01 01 01 01 00 01 01 00 10
2
0
3
3
2
0
3
3
0
2
1
1
2
3
2
2
3
1
3
3
1
2
3
1
3
3
4
4
3
1
4
4
1
3

## Slide 56: Automatic Repeat reQuest
Mechanism used in data link control and transport protocols
Relies on use of an error detection code (such as CRC)
Flow Control
Error Control

## Slide 57: Flow Control
Assures that transmitting entity does not overwhelm a receiving entity with data
Protocols with flow control mechanism allow multiple PDUs in transit at the same time
PDUs arrive in same order they’re sent
Sliding-window flow control
  Transmitter maintains list (window) of sequence numbers allowed to send
  Receiver maintains list allowed to receive

## Slide 58: Flow Control
Reasons for breaking up a block of data before transmitting:
  Limited buffer size of receiver
  Retransmission of PDU due to error requires smaller amounts of data to be retransmitted
  On shared medium, larger PDUs occupy medium for extended period, causing delays at other sending stations

## Slide 59: Flow Control

## Slide 60: Error Control
Mechanisms to detect and correct transmission errors
Types of errors:
  Lost PDU : a PDU fails to arrive
  Damaged PDU : PDU arrives with errors

## Slide 61: Error Control Requirements
Error detection
  Receiver detects errors and discards PDUs
Positive acknowledgement
  Destination returns acknowledgment of received, error-free PDUs
Retransmission after timeout
  Source retransmits unacknowledged PDU
Negative acknowledgement and retransmission
  Destination returns negative acknowledgment to PDUs in error