## Slide 1: Wireless LANs (IEEE802.1)
Lecture 5
G. Noubir
noubir@ccs.neu.edu
Textbook: chapters 13, 14
Slides partially from “Mobile Communications” by J. Schiller Chapter 7.

## Slide 2: Outline
Wireless LAN Technology
Medium Access Control for Wireless
IEEE802.11

## Slide 3: Wireless LAN Applications
LAN Extension
Cross-building interconnect
Nomadic Access
Ad hoc networking

## Slide 4: LAN Extension
Wireless LAN linked into a wired LAN on same premises
  Wired LAN
    Backbone
    Support servers and stationary workstations
  Wireless LAN
    Stations in large open areas
    Manufacturing plants, stock exchange trading floors, and warehouses

## Slide 5: Multiple-cell Wireless LAN
Notes: CM = control module
UM = user module

## Slide 6: Cross-Building Interconnect
Connect LANs in nearby buildings
  Wired or wireless LANs
Point-to-point wireless link is used
Devices connected are typically bridges or routers

## Slide 7: Nomadic Access
Wireless link between LAN hub and mobile data terminal equipped with antenna
  Laptop computer or notepad computer
Uses:
  Transfer data from portable computer to office server
  Extended environment such as campus

## Slide 8: Ad Hoc Networking
Temporary peer-to-peer network set up to meet immediate need
Example:
  Group of employees with laptops convene for a meeting; employees link computers in a temporary network for duration of meeting

## Slide 9: Wireless LAN Requirements
Throughput
Number of nodes
Connection to backbone LAN
Service area
Battery power consumption
Transmission robustness and security
Collocated network operation
License-free operation
Handoff/roaming
Dynamic configuration

## Slide 10: Wireless LAN Categories
Infrared (IR) LANs
Spread spectrum LANs
Narrowband microwave

## Slide 11: Strengths of Infrared Over Microwave Radio
Spectrum for infrared virtually unlimited
  Possibility of high data rates
Infrared spectrum unregulated
Equipment inexpensive and simple
Reflected by light-colored objects
  Ceiling reflection for entire room coverage
Doesn’t penetrate walls
  More easily secured against eavesdropping
  Less interference between different rooms

## Slide 12: Drawbacks of Infrared Medium
Indoor environments experience infrared background radiation
  Sunlight and indoor lighting
  Ambient radiation appears as noise in an infrared receiver
  Transmitters of higher power required
    Limited by concerns of eye safety and excessive power consumption
  Limits range

## Slide 13: IR Data Transmission Techniques
Directed Beam Infrared
Ominidirectional
Diffused

## Slide 14: Directed Beam Infrared
Used to create point-to-point links
Range depends on emitted power and degree of focusing
Focused IR data link can have range of kilometers
  Cross-building interconnect between bridges or routers

## Slide 15: Ominidirectional
Single base station within line of sight of all other stations on LAN
Station typically mounted on ceiling
Base station acts as a multiport repeater
  Ceiling transmitter broadcasts signal received by IR transceivers
  IR transceivers transmit with directional beam aimed at ceiling base unit

## Slide 16: Diffused
All IR transmitters focused and aimed at a point on diffusely reflecting ceiling
IR radiation strikes ceiling
  Reradiated omnidirectionally
  Picked up by all receivers

## Slide 17: Spread Spectrum LAN Configuration
Multiple-cell arrangement
Within a cell, either peer-to-peer or hub
Peer-to-peer topology
  No hub
  Access controlled with MAC algorithm
    CSMA
  Appropriate for ad hoc LANs

## Slide 18: Spread Spectrum LAN Configuration
Hub topology
  Mounted on the ceiling and connected to backbone
  May control access
  May act as multiport repeater
  Automatic handoff of mobile stations
  Stations in cell either:
    Transmit to / receive from hub only
    Broadcast using omnidirectional antenna

## Slide 19: Narrowband Microwave LANs
Use of a microwave radio frequency band for signal transmission
Relatively narrow bandwidth
Licensed
Unlicensed

## Slide 20: Licensed Narrowband RF
Licensed within specific geographic areas to avoid potential interference
Motorola - 600 licenses in 18-GHz range
  Covers all metropolitan areas
  Can assure that independent LANs in nearby locations don’t interfere
  Encrypted transmissions prevent eavesdropping

## Slide 21: Unlicensed Narrowband RF
RadioLAN introduced narrowband wireless LAN in 1995
  Uses unlicensed ISM spectrum
  Used at low power (0.5 watts or less)
  Operates at 10 Mbps in the 5.8-GHz band
  Range = 50 m to 100 m
Notes: Microwave = signals of frequency higher than 1GHz

## Slide 22: Motivation for Wireless MAC
Can we apply media access methods from fixed networks?
Example CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  send as soon as the medium is free, listen into the medium if a collision occurs (original method in IEEE 802.3)
Problems in wireless networks
  signal strength decreases proportional to the square of the distance
  the sender would apply CS and CD, but the collisions happen at the receiver
  it might be the case that a sender cannot “hear” the collision, i.e., CD does not work
  furthermore, CS might not work if, e.g., a terminal is “hidden”

## Slide 23: Motivation - hidden and exposed terminals
Hidden terminals
  A sends to B, C cannot receive A
  C wants to send to B, C senses a “free” medium (CS fails)
  collision at B, A cannot receive the collision (CD fails)
  A is “hidden” for C
Exposed terminals
  B sends to A, C wants to send to another terminal (not A or B)
  C has to wait, CS signals a medium in use
  but A is outside the radio range of C, therefore waiting is not necessary
  C is “exposed” to B
B
A
C

## Slide 24: Motivation - near and far terminals
Terminals A and B send, C receives
  signal strength decreases proportional to the square of the distance
  the signal of terminal B therefore drowns out A’s signal
  C cannot receive A
If C for example was an arbiter for sending rights, terminal B would drown out terminal A already on the physical layer
Also severe problem for CDMA-networks - precise power control needed!
A
B
C

## Slide 25: Access methods SDMA/FDMA/TDMA
SDMA (Space Division Multiple Access)
  segment space into sectors, use directed antennas
  cell structure
FDMA (Frequency Division Multiple Access)
  assign a certain frequency to a transmission channel between a sender and a receiver
  permanent (e.g., radio broadcast), slow hopping (e.g., GSM), fast hopping (FHSS, Frequency Hopping Spread Spectrum)
TDMA (Time Division Multiple Access)
  assign the fixed sending frequency to a transmission channel between a sender and a receiver for a certain amount of time
The multiplexing schemes are now used to control medium access!
Notes: <number>
<footer>
<header>
<date/time>
15

## Slide 26: FDD/FDMA - general scheme, example GSM
f
t
124
1
124
1
20 MHz
200 kHz
890.2 MHz
935.2 MHz
915 MHz
960 MHz

## Slide 27: TDD/TDMA - general scheme, example DECT
1
2
3
11
12
1
2
3
11
12
t
downlink
uplink
417 µs

## Slide 28: Frequency Division Multiple Access
Concept:
  assign different frequency bands to different users
  no sharing of a frequency band between two users
  user separation using band-pass filters
  continuous flow
  two-way: two frequency bands or Time Division Duplex (TDD)
Advantages: simple receivers
  longer symbol duration: no-need for equalization
    low inter-symbol interference
    e.g., 50kb/s QPSK =>40s >> 1-10s delay spread
Drawbacks:
  frequency guard bands, costly tight RF band-filters,
  long fading duration: need slow frequency hopping
  may need spatial diversity (multiple antennas/beam forming) Rx/Tx

## Slide 29: Frequency Selection
Frequency management:
  Fixed (cellular phones-base stations): reuse factor
  On demand (cellular phones-mobile terminals)
  Dynamic (cordless/WLAN): based on sensing interference levels
  Problems: congestion management, dynamic load, …
Antenna implications:
  High antennas (e.g., 50m): higher coverage but higher interference between base stations (need for synchronization)
  Low antennas: higher attenuation, lower coverage, better reuse
Conclusion:
  Pure FDMA is only interesting for simple cordless systems (CT-2)

## Slide 30: Time Division Multiple Access
Concept:
  use the same frequency over non-overlapping periods of time
Advantages:
  simple filters (window)
  transmit and receive over the same frequency channel
Drawbacks:
  users must be synchronized with BS (master clock over a BCH)
  guard times: common 30-50s, may be less in recent systems
  short symbol duration: need for equalization, training sequences...
    high inter-symbol interference
    e.g., 50Kbps, QPSK, 8 users:
      5 s symbol duration
      delay spread: 1s (cordless), upto 20s for cellular

## Slide 31: FDMA/TDMA
First channel allocation:
  random access channel (RACH) to send short requests
  ALOHA type protocol over the RACH
One can use both FDMA and TDMA
  examples: GSM system, D-AMPS
M9
M5
M6
M1
M2
M3
M4
M9
M5
M6
M1
M2
M3
M4
Time
Frequency
cycle

## Slide 32: Access method CDMA
CDMA (Code Division Multiple Access)
  all terminals send on the same frequency probably at the same time and can use the whole bandwidth of the transmission channel
  codes generate signals with “good-correlation” properties
  signals from another user appear as “noise” (use spread spectrum technology)
  signals are spread over a wideband using pseudo-noise sequences (e.g., each sender has a unique random number, the sender XORs the signal with this random number)
  the receiver can “tune” into this signal if it knows the pseudo random number, tuning is done via a correlation function
Disadvantages:
  higher complexity of a receiver (receiver cannot just listen into the medium and start receiving if there is a signal)
  all signals should have the same strength at a receiver (near-far effect)
Advantages:
  all terminals can use the same frequency => no planning needed; macrodiversity
  huge code space (e.g. 232) compared to frequency space
Notes: <number>
<footer>
<header>
<date/time>
28

## Slide 33: Aloha/slotted aloha
Mechanism
  random, distributed (no central arbiter), time-multiplex
  Slotted Aloha additionally uses time-slots, sending must always start at slot boundaries
Aloha
Slotted Aloha
sender A
sender B
sender C
collision
sender A
sender B
sender C
collision
t
t

## Slide 34: Carrier Sense Protocols
Use the fact that in some networks you can sense the medium to check whether it is currently free
  1-persistent CSMA
  non-persistent CSMA
  p-persistent protocol
  CSMA with collision Detection (CSMA/CD): not applicable to wireless systems
1-persistent CSMA
  when a station has a packet:
    it waits until the medium is free to transmit the packet
    if a collision occurs, the station waits a random amount of time
  first transmission results in a collision if several stations are waiting for the channel
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: Carrier Sense Protocols (Cont’d)
non-persistent CSMA
  when a station has a packet:
    if the medium is free, transmit the packet
    otherwise wait for a random period of time and repeat the algorithm
  higher delays, but better performance than pure ALOHA
p-persistent protocol
  when a station has a packet wait until the medium is free:
    transmit the packet with probability p
    wait for next slot with probability 1-p
  better throughput than other schemes but higher delay
CSMA with collision Detection (CSMA/CD)
  stations abort their transmission when they detect a collision
  e.g., Ethernet, IEEE802.3 but not applicable to wireless systems
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: DAMA - Demand Assigned Multiple Access
Channel efficiency only 18% for Aloha, 36% for Slotted Aloha (assuming Poisson distribution for packet arrival and packet length)
Reservation can increase efficiency to 80%
  a sender reserves a future time-slot
  sending within this reserved time-slot is possible without collision
  reservation also causes higher delays
  typical scheme for satellite links
Examples for reservation algorithms:
  Explicit Reservation according to Roberts (Reservation-ALOHA)
  Implicit Reservation (PRMA)
  Reservation-TDMA

## Slide 37: Access method DAMA: Explicit Reservation
Explicit Reservation (Reservation Aloha used for Sat. Com.):
  two modes:
    ALOHA mode for reservation: competition for small reservation slots, collisions possible
    reserved mode for data transmission within successful reserved slots (no collisions possible)
  it is important for all stations to keep the reservation list consistent at any point in time and, therefore, all stations have to synchronize from time to time
Notes: <number>
<footer>
<header>
<date/time>
24

## Slide 38: Access method DAMA: PRMA
Implicit reservation (PRMA - Packet Reservation MA):
  a certain number of slots form a frame, frames are repeated
  stations compete for empty slots according to the slotted aloha principle
  once a station reserves a slot successfully, this slot is automatically assigned to this station in all following frames as long as the station has data to send
  competition for this slots starts again as soon as the slot was empty in the last frame
frame1
frame2
frame3
frame4
frame5
1
2
3
4
5
6
7
8
time-slot
collision at reservation attempts
A
C
D
A
B
A
F
A
C
A
B
A
A
B
A
G
A
B
A
G
D
A
C
E
E
B
A
G
D
t
ACDABA-F
ACDABA-F
AC-ABAG-
A---BAGD
ACEEBAGD
reservation
successful
reservation
Notes: <number>
<footer>
<header>
<date/time>
25

## Slide 39: Access method DAMA: Reservation-TDMA
Reservation Time Division Multiple Access
  every frame consists of N mini-slots and x data-slots
  every station has its own mini-slot and can reserve up to k data-slots using this mini-slot (i.e. x = N * k).
  other stations can send data in unused data-slots according to a round-robin sending scheme (best-effort traffic)
N mini-slots
N * k data-slots
reservations for data-slots
other stations can use free data-slots
based on a round-robin scheme or Aloha
e.g. N=6, k=2
Notes: <number>
<footer>
<header>
<date/time>
26

## Slide 40: MACA - collision avoidance
MACA (Multiple Access with Collision Avoidance) uses short signaling packets for collision avoidance
  RTS (request to send): a sender request the right to send from a receiver with a short RTS packet before it sends a data packet
  CTS (clear to send): the receiver grants the right to send as soon as it is ready to receive
Signaling packets contain
  sender address
  receiver address
  packet size
Variants of this method can be found in IEEE802.11 as DFWMAC (Distributed Foundation Wireless MAC)

## Slide 41: MACA examples
MACA avoids the problem of hidden terminals
  A and C want to send to B
  A sends RTS first
  C waits after receiving CTS from B
MACA avoids the problem of exposed terminals
  B wants to send to A, C to another terminal
  now C does not have to wait for it cannot receive CTS from A
A
B
C
RTS
CTS
CTS
A
B
C
RTS
CTS
RTS

## Slide 42: MACA variant: DFWMAC in IEEE802.11
idle
wait for the
right to send
wait for ACK
sender
receiver
packet ready to send; RTS
time-out;
RTS
CTS; data
ACK
RxBusy
idle
wait for
data
RTS; RxBusy
RTS;
CTS
data;
ACK
time-out 
data;
NAK
ACK: positive acknowledgement
NAK: negative acknowledgement
RxBusy: receiver busy
time-out 
NAK;
RTS

## Slide 43: Polling mechanisms
If one terminal can be heard by all others, this “central” terminal (a.k.a. base station) can poll all other terminals according to a certain scheme
  now all schemes known from fixed networks can be used (typical mainframe - terminal scenario)
Example: Randomly Addressed Polling
  base station signals readiness to all mobile terminals
  terminals ready to send can now transmit a random number without collision with the help of CDMA or FDMA (the random number can be seen as dynamic address) or with collisions (over the Random Access CHannel)
  the base station now chooses one address for polling from the list of all random numbers (collision if two terminals choose the same address)
  the base station acknowledges correct packets and continues polling the next terminal
  this cycle starts again after polling all terminals of the list

## Slide 44: ISMA (Inhibit Sense Multiple Access)
Current state of the medium is signaled via a “busy tone”
  the base station signals on the downlink (base station to terminals) if the medium is free or not
  terminals must not send if the medium is busy
  terminals can access the medium as soon as the busy tone stops
  the base station signals collisions and successful transmissions via the busy tone and acknowledgements, respectively (media access is not coordinated within this approach)
  mechanism used, e.g., for CDPD (USA, integrated into AMPS)

## Slide 45: Comparison SDMA/TDMA/FDMA/CDMA

## Slide 46: Throughputs of Some Random Access Protocols
G: load (includes both successful transmissions and retransmissions)
S: successful transmission
a: ratio of propagation delay to the packet transmission delay
Protocol
Throughput
Pure-ALOHA
S = Ge-2G
Slotted-ALOHA
S = Ge-G
Non slotted 1-persistent
Slotted 1-persistent CSMA
Nonpersistent non slotted
CSMA
Nonpersistent slotted
CSMA

## Slide 47: Comparison of MAC Algorithms

## Slide 48: IEEE802.11
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point

## Slide 49: 802.11 - Architecture of an infrastructure network
Station (STA)
  terminal with access mechanisms to the wireless medium and radio contact to the access point
Basic Service Set (BSS)
  group of stations using the same radio frequency
Access Point
  station integrated into the wireless LAN and the distribution system
Portal
  bridge to other (wired) networks
Distribution System
  interconnection network to form one logical network (EES: Extended Service Set) based on several BSS
Distribution System
Portal
802.x LAN
Access
Point
802.11 LAN
BSS2
802.11 LAN
BSS1
Access
Point
STA1
STA2
STA3
ESS
Notes: <number>
<footer>
<header>
<date/time>
9

## Slide 50: 802.11 - Architecture of an ad-hoc network
Direct communication within a limited range
  Station (STA): terminal with access mechanisms to the wireless medium
  Basic Service Set (BSS): group of stations using the same radio frequency
802.11 LAN
BSS2
802.11 LAN
BSS1
STA1
STA4
STA5
STA2
STA3

## Slide 51: IEEE standard 802.11
mobile terminal
access point
server
fixed terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure network
LLC
LLC

## Slide 52: 802.11 - Layers and functions
PLCP Physical Layer Convergence Protocol
  clear channel assessment signal (carrier sense)
PMD Physical Medium Dependent
  modulation, coding
PHY Management
  channel selection, MIB
Station Management
  coordination of all management functions
PMD
PLCP
MAC
LLC
MAC Management
PHY Management
MAC
  access mechanisms, fragmentation, encryption
MAC Management
  synchronization, roaming, MIB, power management
PHY
DLC
Station Management

## Slide 54: 802.11 - Physical layer
5 versions: 2 radio (typ. 2.4 GHz), 1 IR
  data rates 1 or 2 Mbit/s
FHSS (Frequency Hopping Spread Spectrum) 2.4 GHz
  spreading, despreading, signal strength, typ. 1 Mbit/s
  min. 2.5 frequency hops/s (USA), two-level GFSK modulation
DSSS (Direct Sequence Spread Spectrum) 2.4GHz
  DBPSK modulation for 1 Mbit/s (Differential Binary Phase Shift Keying), DQPSK for 2 Mbit/s (Differential Quadrature PSK)
  preamble and header of a frame is always transmitted with 1 Mbit/s, rest of transmission 1 or 2 Mbit/s
  chipping sequence: +1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1 (Barker code)
  max. radiated power 1 W (USA), 100 mW (EU), min. 1mW
Infrared
  850-950 nm, diffuse light, typ. 10 m range
  carrier detection, energy detection, synchronization
Notes: Two levels GFSK for 2Mbps

## Slide 55: IEEE 802.11a and IEEE 802.11b
IEEE 802.11a
  Makes use of 5-GHz band
  Provides rates of 6, 9 , 12, 18, 24, 36, 48, 54 Mbps
  Uses orthogonal frequency division multiplexing (OFDM)
  Subcarrier modulated using BPSK, QPSK, 16-QAM or 64-QAM
IEEE 802.11b
  Provides data rates of 5.5 and 11 Mbps
  Complementary code keying (CCK) modulation scheme

## Slide 56: FHSS PHY packet format
synchronization
SFD
PLW
PSF
HEC
payload
PLCP preamble
PLCP header
80
16
12
4
16
variable
bits
Synchronization
  synch with 010101... pattern
SFD (Start Frame Delimiter)
  0000110010111101 start pattern
PLW (PLCP_PDU Length Word)
  length of payload incl. 32 bit CRC of payload, PLW < 4096
PSF (PLCP Signaling Field)
  data rate of payload (1 or 2 Mbit/s)
HEC (Header Error Check)
  CRC with x16+x12+x5+1
Notes: The Preamble SYNC field is an 80-bit field containing an alternating zero-one pattern, transmitted starting with zero and ending with one, to be used by the PHY sublayer to detect a potentially receivable signal, select an antenna if diversity is utilized, and reach steady-state frequency offset correction and synchronization with the received packet timing.
The SFD consists of the 16-bit binary pattern 0000 1100 1011 1101 (transmitted leftmost bit Þrst). The Þrst bit of the SFD follows the last bit of the sync pattern. The SFD defines the frame timing.

## Slide 57: DSSS PHY packet format
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16
Synchronization
  synch., gain setting, energy detection, frequency offset compensation
SFD (Start Frame Delimiter)
  1111001110100000
Signal
  data rate of the payload (0A: 1 Mbit/s DBPSK; 14: 2 Mbit/s DQPSK)
Service Length
  future use, 00: 802.11 compliant  length of the payload
HEC (Header Error Check)
  protection of signal, service and length, x16+x12+x5+1
Notes: The SYNC field shall consist of 128 bits of scrambled 1 bit. This field shall be provided so that the receiver
can perform the necessary operations for synchronization.
The SFD shall be provided to indicate the start of PHY dependent parameters within the PLCP Preamble.
The SFD shall be a 16-bit field, X'F3A0' (msb to lsb). The lsb shall be transmitted Þrst in time.
The 8-bit IEEE 802.11 signal Þeld indicates to the PHY the modulation that shall be used for transmission
(and reception) of the MPDU. The data rate shall be equal to the Signal Þeld value multiplied by 100 kbit/s.

## Slide 58: 802.11 - MAC layer I - DFWMAC
Traffic services
  Asynchronous Data Service (mandatory)
    exchange of data packets based on “best-effort”
    support of broadcast and multicast
  Time-Bounded Service (optional)
    implemented using PCF (Point Coordination Function)
Access methods
  DFWMAC-DCF CSMA/CA (mandatory)
    collision avoidance via randomized „back-off“ mechanism
    minimum distance between consecutive packets
    ACK packet for acknowledgements (not for broadcasts)
  DFWMAC-DCF w/ RTS/CTS (optional)
    Distributed Foundation Wireless MAC
    avoids hidden terminal problem
  DFWMAC- PCF (optional)
    access point polls terminals according to a list

## Slide 59: 802.11 - MAC layer II
Priorities
  defined through different inter frame spaces
  SIFS (Short Inter Frame Spacing)
    highest priority, for ACK, CTS, polling response
  PIFS (PCF IFS)
    medium priority, for time-bounded service using PCF
  DIFS (DCF, Distributed Coordination Function IFS)
    lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS
Notes: aSIFSTime = aRxRFDelay + aRxPLCPDelay + aMACProcessingDelay + aRxTxTurnaroundTime.
aSlotTime = aCCATime + aRxTxTurnaroundTime + aAirPropagationTime + aMACProcessingDelay.
PIFS = aSIFSTime + aSlotTime
DIFS = aSIFSTime + 2aSlotTime
EIFS = aSIFSTime + (8 ACKSize) + aPreambleLength + aPLCPHeaderLngth+ DIFS
For DSSS:
aSlotTime 20 µs
aSIFSTime 10 µs
aCCATime < 15 µs
aRxTxTurnaroundTime <5 µs
SIFS =
PIFS =
DIFS =

## Slide 60: IFS Timing
aSIFSTime = aRxRFDelay + aRxPLCPDelay + aMACProcessingDelay + aRxTxTurnaroundTime.
aSlotTime = aCCATime + aRxTxTurnaroundTime + aAirPropagationTime + aMACProcessingDelay.
PIFS = aSIFSTime + aSlotTime
DIFS = aSIFSTime + 2aSlotTime
EIFS = aSIFSTime + (8 ACKSize) + aPreambleLength + aPLCPHeaderLngth+ DIFS
For DSSS:
  aSlotTime 20 µs
  aSIFSTime 10 µs
  aCCATime < 15 µs
  aRxTxTurnaroundTime <5 µs

## Slide 61: 802.11 - CSMA/CA access method I
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
  station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
  if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
  if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
  if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
slot time
direct access if medium is free  DIFS
Notes: <number>
<footer>
<header>
<date/time>
12

## Slide 62: 802.11 - competing stations - simple version
t
busy
boe
station1
station2
station3
station4
station5
packet arrival at MAC
DIFS
boe
boe
boe
busy
elapsed backoff time
bor
residual backoff time
busy
medium not idle (frame, ack etc.)
bor
bor
DIFS
boe
boe
boe
bor
DIFS
busy
busy
DIFS
boe
busy
boe
boe
bor
bor

## Slide 63: 802.11 - CSMA/CA access method II
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (CRC)
  automatic retransmission of data packets in case of transmission errors
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 64: 802.11 - DFWMAC
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  sender can now send data at once, acknowledgement via ACK
  other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 65: Fragmentation
t
SIFS
DIFS
data
ACK1
other
stations
receiver
sender
frag1
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)
NAV (frag1)
NAV (ACK1)
SIFS
ACK2
frag2
SIFS
Notes: Frag1 contains duration info for (NAV) of frag2 + ack2.

## Slide 66: DFWMAC-PCF I
PIFS
stations‘
NAV
wireless
stations
point
coordinator
D1
U1
SIFS
NAV
SIFS
D2
U2
SIFS
SIFS
SuperFrame
t0
medium busy
t1

## Slide 67: DFWMAC-PCF II
t
stations‘
NAV
wireless
stations
point
coordinator
D3
NAV
PIFS
D4
U4
SIFS
SIFS
CFend
contention
period
contention free period
t2
t3
t4
7.20.1

## Slide 68: 802.11 - Frame format
Types
  control frames, management frames, data frames
Sequence numbers
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  sending time, checksum, frame control, data
Frame
Control
Duration
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Data
CRC
2
2
6
6
6
6
2
4
0-2312
bytes
Version, Type, Subtype, To DS, From DS, More Fragments, Retry,
Power Management, More Data, Wired Equivalent Privacy (WEP), and Order
Notes: There are three frame types: control (e.g., RTS/CTS/Ack), data, and management (e.g., association). Each of the frame types have several defined subtypes.
Sequence control: fragment number, sequence number (remains constant for the same frame/fragment)

## Slide 69: MAC address format
DS: Distribution System
AP: Access Point
DA: Destination Address (final recipient)
SA: Source Address (initiator)
BSSID: Basic Service Set Identifier
RA: Receiver Address (immediate recipient)
TA: Transmitter Address (immediate sender)

## Slide 70: 802.11 - MAC management
Synchronization
  try to find a LAN, try to stay within a LAN
  timer etc.
Power management
  sleep-mode without missing a message
  periodic sleep, frame buffering, traffic measurements
Association/Reassociation
  integration into a LAN
  roaming, i.e. change networks by changing access points
  scanning, i.e. active search for a network
MIB - Management Information Base
  managing, read, write
Notes: Each STA shall maintain a TSF timer with modulus 2 64 counting in increments of microseconds. STAs expect to receive beacons at a nominal rate. The interval between beacons is deÞned by the aBeaconPeriod parameter of the STA. A STA sending a beacon shall set the value of the beaconÕs timestamp so that it equals the value of the STAÕs TSF timer at the time that the Þrst bit of the timestamp is transmitted to the PHY plus the transmitting STAs delays through its local PHY from the MAC-PHY interface to its interface with the wireless medium (antenna, LED emission surface, etc.). The algorithms in this clause deÞne a mechanism that maintains the synchronization of the TSF timers in a BSS to within 4 µs plus the maximum propagation delay of the PHY for PHYs of 1 Mb/s, or greater.

## Slide 71: Synchronization using a Beacon (infrastructure)
beacon interval
t
medium
access
point
busy
B
busy
busy
busy
B
B
B
value of the timestamp
B
beacon frame

## Slide 72: Synchronization using a Beacon (ad-hoc)
t
medium
station1
busy
B1
beacon interval
busy
busy
busy
B1
value of the timestamp
B
beacon frame
station2
B2
B2
random delay

## Slide 73: Power management
Idea: switch the transceiver off if not needed
States of a station: sleep and awake
Timing Synchronization Function (TSF)
  stations wake up at the same time
Infrastructure
  Traffic Indication Map (TIM)
    list of unicast receivers transmitted by AP
  Delivery Traffic Indication Map (DTIM)
    list of broadcast/multicast receivers transmitted by AP
Ad-hoc
  Ad-hoc Traffic Indication Map (ATIM)
    announcement of receivers by stations buffering frames
    more complicated - no central AP
    collision of ATIMs possible (scalability?)

## Slide 74: Power saving with wake-up patterns (infrastructure)
TIM interval
t
medium
access
point
busy
D
busy
busy
busy
T
T
D
T
TIM
D
DTIM
DTIM interval
B
B
B
broadcast/multicast
station
awake
p
PS poll
p
d
d
d
data transmission
to/from the station
Notes: PS poll: Power Save poll

## Slide 75: Power saving with wake-up patterns (ad-hoc)
awake
A
transmit ATIM
D
transmit data
t
station1
B1
B1
B
beacon frame
station2
B2
B2
random delay
A
a
D
d
ATIM
window
beacon interval
a
acknowledge ATIM
d
acknowledge data

## Slide 76: 802.11 - Roaming
No or bad connection? Then perform:
Scanning
  scan the environment, i.e., listen into the medium for beacon signals (passive) or send probes (active) into the medium and wait for an answer
Reassociation Request
  station sends a request to one or several AP(s)
Reassociation Response
  success: AP has answered, station can now participate
  failure: continue scanning
AP accepts Reassociation Request
  signal the new station to the distribution system
  the distribution system updates its data base (i.e., location information)
  typically, the distribution system now informs the old AP so it can release resources
Notes: Active scanning vs. Passive scanning