## Slide 1: Wireless Networks: Network Protocols/Mobile IP
Motivation
Data transfer
Encapsulation
Security
IPv6
Problems
DHCP
Adapted from J. Schiller, “Mobile Communications”

## Slide 2: Motivation for Mobile IP
Routing
  based on IP destination address, network prefix (e.g. 129.13.42) determines physical subnet
  change of physical subnet implies change of IP address to have a topological correct address (standard IP) or needs special entries in the routing tables
Specific routes to end-systems?
  change of all routing table entries to forward packets to the right destination
  does not scale with the number of mobile hosts and frequent changes in the location, security problems
Changing the IP-address?
  adjust the host IP address depending on the current location
  almost impossible to find a mobile system, DNS updates take too much time
  TCP connections break, security problems

## Slide 3: Requirements to Mobile IP (RFC 2002)
Transparency
  mobile end-systems keep their IP address
  continuation of communication after interruption of link possible
  point of connection to the fixed network can be changed
Compatibility
  support of the same layer 2 protocols as IP
  no changes to current end-systems and routers required
  mobile end-systems can communicate with fixed systems
Security
  authentication of all registration messages
Efficiency and scalability
  only little additional messages to the mobile system required (connection typically via a low bandwidth radio link)
  world-wide support of a large number of mobile systems in the whole Internet

## Slide 4: Terminology
Mobile Node (MN)
  system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
  system in the home network of the MN, typically a router
  registers the location of the MN, tunnels IP datagrams to the COA
Foreign Agent (FA)
  system in the current foreign network of the MN, typically a router
  forwards the tunneled datagrams to the MN, typically also the default router for the MN
Care-of Address (COA)
  address of the current tunnel end-point for the MN (at FA or MN)
  actual location of the MN from an IP point of view
  can be chosen, e.g., via DHCP
Correspondent Node (CN)
  communication partner

## Slide 5: Example network
mobile end-system
Internet
router
router
router
end-system
FA
HA
MN
home network
foreign network
(physical home network
for the MN)
(current physical network for the MN)
CN

## Slide 6: Data transfer to the mobile system
Internet
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
1. Sender sends to the IP address of MN,
HA intercepts packet (proxy ARP)
2. HA tunnels packet to COA, here FA,
by encapsulation
3. FA forwards the packet to the MN
CN

## Slide 7: Data transfer from the mobile system
Internet
receiver
FA
HA
MN
home network
foreign network
sender
1
1. Sender sends to the IP address of the receiver as usual, FA works as default router
CN

## Slide 8: Overview
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 9: Network integration
Agent Advertisement
  HA and FA periodically send advertisement messages into their physical subnets
  MN listens to these messages and detects, if it is in the home or a foreign network (standard case for home network)
  MN reads a COA from the FA advertisement messages
Registration (always limited lifetime!)
  MN signals COA to the HA via the FA, HA acknowledges via FA to MN
  these actions have to be secured by authentication
Advertisement
  HA advertises the IP address of the MN (as for fixed systems), i.e. standard routing information
  routers adjust their entries, these are stable for a longer time (HA responsible for a MN over a longer period of time)
  packets to the MN are sent to the HA,
  independent of changes in COA/FA

## Slide 10: Agent advertisement
preference level 1
router address 1
#addresses
type
addr. size
lifetime
checksum
COA 1
COA 2
type
sequence number
length
0
7
8
15
16
31
24
23
code
preference level 2
router address 2
. . .
registration lifetime
. . .
R
B
H
F
M
G
V
reserved
ICMP-Type = 9; Code = 0/16; Extension Type = 16
TTL = 1
Dest-Adr = 224.0.0.1 (multicast on link) or 255.255.255.255 (broadcast)
R: registration required
B: busy
H: home agent
F: foreign agent
M: minimal encapsulation
G: generic routing
encapsulation
V: header compression

## Slide 11: Registration
t
MN
HA
registration
request
registration
reply
t
MN
FA
HA
registration
request
registration
request
registration
reply
registration
reply
Goal: inform the home agent of current location of MN (COA-FA or co-located COA)
Registration expires automatically (lifetime)
Uses UDP port 434

## Slide 12: Mobile IP registration request
home agent
home address
type
lifetime
0
7
8
15
16
31
24
23
rsv
identification
COA
extensions . . .
S
B
D
M
G
V
UDP packet on port 343
Type = 1 for registration request
S: retain prior mobility bindings
B: forward broadcast packets
D: co-located address=> MN decapsulates packets

## Slide 13: Encapsulation
original IP header
original data
new data
new IP header
outer header
inner header
original data

## Slide 14: Encapsulation I
Encapsulation of one packet into another as payload
  e.g. IPv6 in IPv4 (6Bone), Multicast in Unicast (Mbone)
  here: e.g. IP-in-IP-encapsulation, minimal encapsulation or GRE (Generic Record Encapsulation)
IP-in-IP-encapsulation (mandatory in RFC 2003)
  tunnel between HA and COA
Care-of address COA
IP address of HA
TTL
IP identification
IP-in-IP
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
TCP/UDP/ ... payload

## Slide 15: Encapsulation II
Minimal encapsulation (optional) [RFC2004]
  avoids repetition of identical fields
  e.g. TTL, IHL, version, TOS
  only applicable for unfragmented packets, no space left for fragment identification
care-of address COA
IP address of HA
TTL
IP identification
min. encap.
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
IP address of MN
original sender IP address (if S=1)
S
lay. 4 protoc.
IP checksum
TCP/UDP/ ... payload
reserved

## Slide 16: Generic Routing Encapsulation [RFC 1701]
original
header
original data
new data
new header
outer header
GRE header
original data
original header
Care-of address COA
IP address of HA
TTL
IP identification
GRE
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
TOS
ver.
IHL
TCP/UDP/ ... payload
routing (optional)
sequence number (optional)
key (optional)
offset (optional)
checksum (optional)
protocol
rec.
rsv.
ver.
C
R
K
S
s
C: checksum present
R: offset/source routing is present
K: key field for authentication (not implemented)
S:sequence number is present
s: strict source routing is used
rec: Recursion control

## Slide 17: Optimization of packet forwarding
Triangular Routing
  sender sends all packets via HA to MN
  higher latency and network load
“Solutions”
  sender learns the current location of MN
  direct tunneling to this location
  HA informs a sender about the location of MN
  big security problems!
Change of FA
  packets on-the-fly during the change can be lost
  new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
  this information also enables the old FA to release resources for the MN

## Slide 18: Change of foreign agent
CN
HA
FAold
FAnew
MN
t
request
update
ACK
data
data
MN changes location
registration
update
ACK
data
data
data
warning
update
ACK
data
data
registration

## Slide 19: Reverse tunneling (RFC 2344)
Internet
receiver
FA
HA
MN
home network
foreign network
sender
3
2
1
1. MN sends to FA
2. FA tunnels packets to HA
by encapsulation
3. HA forwards the packet to the
receiver (standard case)
CN

## Slide 20: Mobile IP with reverse tunneling
Router accept often only “topological correct“ addresses (firewall!)
  a packet from the MN encapsulated by the FA is now topologically correct
  furthermore multicast and TTL problems solved (TTL in the home network correct, but MN is to far away from the receiver)
Reverse tunneling does not solve
  problems with firewalls, the reverse tunnel can be abused to circumvent security mechanisms (tunnel hijacking)
  optimization of data paths, i.e. packets will be forwarded through the tunnel via the HA to a sender (double triangular routing)
The new standard is backwards compatible
  the extensions can be implemented easily and cooperate with current implementations without these extensions

## Slide 21: Mobile IP and IPv6
Mobile IP was developed for IPv4, but IPv6 simplifies the protocols
  security is integrated and not an add-on, authentication of registration is included
  COA can be assigned via auto-configuration (DHCPv6 is one candidate), every node has address autoconfiguration
  no need for a separate FA, all routers perform router advertisement which can be used instead of the special agent advertisement
  MN can signal a sender directly the COA, sending via HA not needed in this case (automatic path optimization)
  „soft“ hand-over, i.e. without packet loss, between two subnets is supported
    MN sends the new COA to its old router
    the old router encapsulates all incoming packets for the MN and forwards them to the new COA
    authentication is always granted

## Slide 22: Problems with mobile IP
Security
  authentication with FA problematic, for the FA typically belongs to another organization
  no protocol for key management and key distribution has been standardized in the Internet
  patent and export restrictions
Firewalls
  typically mobile IP cannot be used together with firewalls, special set-ups are needed (such as reverse tunneling)
QoS
  many new reservations in case of RSVP
  tunneling makes it hard to give a flow of packets a special treatment needed for the QoS
Security, firewalls, QoS etc. are topics of current research and discussions!

## Slide 23: Security in Mobile IP
Security requirements (Security Architecture for the Internet Protocol, RFC 1825, RFC 1826, RFC 1827)
  Integrity any changes to data between sender and receiver can be detected by the receiver
  Authentication sender address is really the address of the sender and all data received is really data sent by this sender
  Confidentiality only sender and receiver can read the data
  Non-Repudiation sender cannot deny sending of data
  Traffic Analysis creation of traffic and user profiles should not be possible
  Replay Protection receivers can detect replay of messages

## Slide 24: IP security architecture I
not encrypted
encrypted
Two or more partners have to negotiate security mechanisms to setup a security association
  typically, all partners choose the same parameters and mechanisms
Two headers have been defined for securing IP packets:
  Authentication-Header
    guarantees integrity and authenticity of IP packets
    if asymmetric encryption schemes are used, some non-repudiation level can also be provided
  Encapsulation Security Payload
    protects confidentiality between communication partners
Authentification-Header
IP-Header
UDP/TCP-Paket
authentication header
IP header
UDP/TCP data
ESP header
IP header
encrypted data

## Slide 25: IP security architecture II
Mobile Security Association for registrations
  parameters for the mobile host (MH), home agent (HA), and foreign agent (FA)
Extensions of the IP security architecture
  extended authentication of registration
  prevention of replays of registrations
    time stamps: 32 bit time stamps + 32 bit random number
    nonces: 32 bit random number (MH) + 32 bit random number (HA)
registration reply
registration request
registration request
MH
FA
HA
registration reply
MH-HA authentication
MH-FA authentication
FA-HA authentication

## Slide 26: Key distribution
Home agent distributes session keys
foreign agent has a security association with the home agent
mobile host registers a new binding at the home agent
home agent answers with a new session key for foreign agent and mobile node
FA
MH
HA
response:
EHA-FA {session key}
EHA-MH {session key}

## Slide 27: DHCP: Dynamic Host Configuration Protocol [RFC 2131]
Application
  simplification of installation and maintenance of networked computers
  supplies systems with all necessary information, such as IP address, DNS server address, domain name, subnet mask, default router etc.
  enables automatic integration of systems into an Intranet or the Internet, can be used to acquire a COA for Mobile IP
Client/Server-Model
  the client sends via a MAC broadcast a request to the DHCP server (might be via a DHCP relay)
client
relay
client
server
DHCPDISCOVER
DHCPDISCOVER

## Slide 28: DHCP - protocol mechanisms
time
server
(not selected)
client
server
(selected)
initialization
collection of replies
selection of configuration
initialization completed
release
confirmation of
configuration
delete context
determine the
configuration
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST (reject)
DHCPACK
DHCPRELEASE
DHCPDISCOVER
DHCPOFFER
DHCPREQUEST (options)
determine the
configuration

## Slide 29: DHCP characteristics
Server
  several servers can be configured for DHCP, coordination not yet standardized (i.e., manual configuration)
Renewal of configurations
  IP addresses have to be requested periodically, simplified protocol
Options
  available for routers, subnet mask, NTP (network time protocol) timeserver, SLP (service location protocol) directory, DNS (domain name system)
Security problems!
  DHCP Authentication IETF-RFC 3118