## Slide 1: Wireless Multihop Ad Hoc Networks
Guevara Noubir
noubir@ccs.neu.edu
Some slides are from Nitin Vaidya’s tutorial.

## Slide 2: Infrastructure vs. Ad Hoc Wireless Networks
Infrastructure networks:
  One or several Access-Points (AP) connected to the wired network
  Mobile nodes communicate through the AP
Ad hoc network:
  Mobile nodes communicate directly with each other
  Multi-hop ad hoc networks: all nodes can also act as routers
Hybrid (nodes relay packets from AP):
  Goal: increase capacity, reduce power consumption, and guarantee a minimum service
Notes: Infrastructure networks:
Hybrid: Reduce infrastructure cost…
Pure Ad Hoc has limited application, pure infrastructure can be expensive (specially over high frequency bands),
Hybrid is reasonable: RF transceiver can cover areas from few meters to 20 miles (at different data rates…)

## Slide 3
Notes: Multi-interface nodes may allow to have two cluster of nodes operating over different frequencies (reducing collisions) an multi-interface node operating as a gateway.

## Slide 4: Constraints
Limited radio spectrum
Broadcast Medium (collisions)
Limited power available at the nodes
Limited storage memory
Connection QoS requirements (e.g., delay, packet loss)
Unreliable network connectivity (depends on the channel)
Dynamic topology (i.e., mobility of nodes, density)
Need to provide a full coverage
Need to enforce fairness
Notes: Problems at all layers.

## Slide 5: Parameters
Use of various coding/modulation schemes
Use of packets fragmentation
Use of various transmission power level
Use of smart antennas and MIMO systems
Use of multiple RF interfaces (multiple IF characteristics)
Clustering and backbone formation
Planning of the fixed nodes location
Packets scheduling schemes
Application adaptivity

## Slide 6: Theoretical Results
Capacity of a wireless network [Gupta & Kumar 2000]
  n identical randomly located nodes each capable of transmitting W bits can only achieve a throughput per node of
  n optimally placed nodes within a 1m2 disc with an optimal traffic pattern and an optimal transmission power can only achieve
Notes: Theta come from the Pmax/Pmin or SNR
If you remember the gain we had using h hops. In a two dimensional space if we want to have h hops => N = h^2…

## Slide 7: Adaptivity and Cooperation
Classical networking stacks have only minimum interaction between adjacent layers
Multi-hop wireless ad hoc networks require more cooperation between layers because:
  Channel variation and network topology changes affect the application
  Routing versus single hop communication considerably affects the medium access control (MAC) performance
  Collisions versus channel fading affects both the physical layer and the MAC
  Battery power has implications on all layers
Notes: Network layer needs info on status of the channel to nodes to decide on one or multiple hop transmission

## Slide 8: Adaptive Coding
Example:
  ½ rate convolutional code (K=5) versus uncoded communication
  Channel with two states: Eb/N0 = 6.8 dB or 11.3 dB (AWGN), L=200 Bytes
Need to estimate the channel and adapt to it
Differentiate between congestions and a bad channel condition
Use of Hybrid-ARQ?
Eb/N0
BER
FER
Nb_Transmit
Total_Tx_Bytes
UC
½ CC
UC
½ CC
UC
½ CC
UC
½ CC
6.8dB
10-3
10-7
0.8
1.6 10-4
5
~ 1
5*200
2*200
11.3dB
10-7
~ 0
1.6 10-4
~ 0
~ 1
~ 1
200
2*200
Notes: Coding is good but only if you use it when necessary. Otherwise you have useless redundancy

## Slide 9: Adaptive Fragmentation
Example:
  To transmit a frame of length 200 Bytes, we can fragment into 4 frames of length 50 Bytes (+ 10 Bytes overhead)
Need to estimate the channel and adapt to it
BER
FER
Nb_Transmit
Total_Tx_Bytes
(incl. overhead)
L=60B
L=200B
L=60B
L=200B
L=60B
L=200B
10-3
0.38
0.8
1.6
5
384
1000
10-7
~ 0
~ 0
~ 1
~ 1
240
200
Notes: Later on we will see how we can adapt by implicitly estimating the channel

## Slide 10: Multiple Power Levels
Using multi-hop transmission (h hops) and reducing the transmission power accordingly
  Increases capacity (factor of h)
  Reduces overall power consumption
  (by a factor of h)
In asymmetric environments
  Low power node can encode data
  and transmit it at low power
  Powerful nodes can decode use
  higher transmission power

## Slide 11: Parameters of IEEE802.11
IEEE802.11 has three mechanisms that can be used to improve performance under dynamic channels:
  Fragmentation (also used to avoid collision)
  Multiple coding/modulation schemes (8 schemes)
  8 power levels
Multiple coding/modulation schemes will be available with 802.11a products over 5GHz
Currently parameters are statically configured

## Slide 12: Problems of Multi-Hop Routing
Routing:
  How to maintain up-to-date information on the network topology? Routing messages overhead
  How to determine number of hops
  How to estimate buffers size
Higher delay
Risk of congestion on nodes

## Slide 13: Practical Approaches
Solving sub-problems independently
  Improving TCP to be wireless aware
  Routing in multi-hop wireless ad hoc networks: DSDV, DSR, AODV, TORA, FSR
    Not power or resource aware. Single hop whenever possible (no interaction with the MAC of higher layers)
  Fragmenting packets according to the channel performance
  Adapting coding/modulation scheme to the channel
  Adapting transmission power to destination
There is a need for a global approach:
  Combine: transmission power, coding, and fragmentation
  Add routing
  Add medium access control
Engineering perspective: what minimal subset of functionalities do we need to implement to achieve near optimal performance?
  What minimal set of coding/modulation schemes? What power levels do we need?
Notes: Some of these are not even implemented in real systems
It is not easy to implement multi-level power levels:
802.11 proposes 8 levels: only one is implemented (to our knowledge)
Bluetooth: proposes 3 levels only one is implemented
Trying to modify everything is utopic defacto-standards/architectures (TCP/IP) are very difficult to change

## Slide 14: Existing Unicast Routing Protocols
Types:
  Proactive protocols
    Determine routes independent of traffic pattern
    Traditional link-state and distance-vector routing protocols are proactive
  Reactive protocols
    Maintain routes only if needed
  Hybrid protocols
Some existing protocols
  Dynamic Source Routing (DSR)
  Location Aware Routing (LAR)
  Adhoc On-demand Distance Vector (AODV)
  Temporally Ordered Reversal Algorithm

## Slide 15: Trade-Off Between Proactive and Reactive
Latency of route discovery
  Proactive protocols may have lower latency since routes are maintained at all times
  Reactive protocols may have higher latency because a route from X to Y will be found only when X attempts to send to Y
Overhead of route discovery/maintenance
  Reactive protocols may have lower overhead since routes are determined only if needed
  Proactive protocols can (but not necessarily) result in higher overhead due to continuous route updating
Which approach achieves a better trade-off depends on the traffic and mobility patterns

## Slide 16: Flooding for Data Delivery
Sender S broadcasts data packet P to all its neighbors
Each node receiving P forwards P to its neighbors
Sequence numbers used to avoid the possibility of forwarding the same packet more than once
Packet P reaches destination D provided that D is reachable from sender S
Node D does not forward the packet

## Slide 17: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Represents that connected nodes are within each
other’s transmission range
Z
Y
Represents a node that has received packet P
M
N
L

## Slide 18: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Represents transmission of packet P
Represents a node that receives packet P for
the first time
Z
Y
Broadcast transmission
M
N
L

## Slide 19: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Node H receives packet P from two neighbors:
potential for collision
Z
Y
M
N
L

## Slide 20: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Node C receives packet P from G and H, but does not forward
it again, because node C has already forwarded packet P once
Z
Y
M
N
L

## Slide 21: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
Nodes J and K both broadcast packet P to node D
Since nodes J and K are hidden from each other, their
transmissions may collide
 Packet P may not be delivered to node D at all
N
L

## Slide 22: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Node D does not forward packet P, because node D
is the intended destination of packet P
M
N
L

## Slide 23: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Flooding completed
Nodes unreachable from S do not receive packet P (e.g., node Z)
Nodes for which all paths from S go through the destination D
also do not receive packet P (example: node N)
Z
Y
M
N
L

## Slide 24: Flooding for Data Delivery
B
A
S
E
F
H
J
D
C
G
I
K
Flooding may deliver packets to too many nodes
(in the worst case, all nodes reachable from sender
may receive the packet)
Z
Y
M
N
L

## Slide 25: Flooding for Data Delivery: Advantages
Simplicity
May be more efficient than other protocols when rate of information transmission is low enough that the overhead of explicit route discovery/maintenance incurred by other protocols is relatively higher
  this scenario may occur, for instance, when nodes transmit small data packets relatively infrequently, and many topology changes occur between consecutive packet transmissions
Potentially higher reliability of data delivery
  Because packets may be delivered to the destination on multiple paths

## Slide 26: Flooding for Data Delivery: Disadvantages
Potentially, very high overhead
  Data packets may be delivered to too many nodes who do not need to receive them
Potentially lower reliability of data delivery
  Flooding uses broadcasting -- hard to implement reliable broadcast delivery without significantly increasing overhead
      Broadcasting in IEEE 802.11 MAC is unreliable
  In our example, nodes J and K may transmit to node D simultaneously, resulting in loss of the packet
      in this case, destination would not receive the packet at all

## Slide 27: Flooding of Control Packets
Many protocols perform (potentially limited) flooding of control packets, instead of data packets
The control packets are used to discover routes
Discovered routes are subsequently used to send data packet(s)
Overhead of control packet flooding is amortized over data packets transmitted between consecutive control packet floods

## Slide 28: Dynamic Source Routing (DSR) [Johnson96]
When node S wants to send a packet to node D, but does not know a route to D, node S initiates a route discovery
Source node S floods Route Request (RREQ)
Each node appends own identifier when forwarding RREQ

## Slide 29: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Represents a node that has received RREQ for D from S
M
N
L

## Slide 30: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Represents transmission of RREQ
Z
Y
Broadcast transmission
M
N
L
[S]
[X,Y] Represents list of identifiers appended to RREQ

## Slide 31: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Node H receives packet RREQ from two neighbors:
potential for collision
Z
Y
M
N
L
[S,E]
[S,C]

## Slide 32: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Node C receives RREQ from G and H, but does not forward
it again, because node C has already forwarded RREQ once
Z
Y
M
N
L
[S,C,G]
[S,E,F]

## Slide 33: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
Nodes J and K both broadcast RREQ to node D
Since nodes J and K are hidden from each other, their
transmissions may collide
N
L
[S,C,G,K]
[S,E,F,J]

## Slide 34: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Node D does not forward RREQ, because node D
is the intended target of the route discovery
M
N
L
[S,E,F,J,M]

## Slide 35: Route Discovery in DSR
Destination D on receiving the first RREQ, sends a Route Reply (RREP)
RREP is sent on a route obtained by reversing the route appended to received RREQ
RREP includes the route from S to D on which RREQ was received by node D

## Slide 36: Route Reply in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
RREP [S,E,F,J,D]
Represents RREP control message

## Slide 37: Route Reply in DSR
Route Reply can be sent by reversing the route in Route Request (RREQ) only if links are guaranteed to be bi-directional
  To ensure this, RREQ should be forwarded only if it received on a link that is known to be bi-directional
If unidirectional (asymmetric) links are allowed, then RREP may need a route discovery for S from node D
  Unless node D already knows a route to node S
  If a route discovery is initiated by D for a route to S, then the Route Reply is piggybacked on the Route Request from D.
If IEEE 802.11 MAC is used to send data, then links have to be bi-directional (since Ack is used)

## Slide 38: Dynamic Source Routing (DSR)
Node S on receiving RREP, caches the route included in the RREP
When node S sends a data packet to D, the entire route is included in the packet header
  hence the name source routing
Intermediate nodes use the source route included in a packet to determine to whom a packet should be forwarded

## Slide 39: Data Delivery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
DATA [S,E,F,J,D]
Packet header size grows with route length

## Slide 40: When to Perform a Route Discovery
When node S wants to send data to node D, but does not know a valid route node D

## Slide 41: DSR Optimization: Route Caching
Each node caches a new route it learns by any means
When node S finds route [S,E,F,J,D] to node D, node S also learns route [S,E,F] to node F
When node K receives Route Request [S,C,G] destined for node, node K learns route [K,G,C,S] to node S
When node F forwards Route Reply RREP [S,E,F,J,D], node F learns route [F,J,D] to node D
When node E forwards Data [S,E,F,J,D] it learns route [E,F,J,D] to node D
A node may also learn a route when it overhears Data packets

## Slide 42: Use of Route Caching
When node S learns that a route to node D is broken, it uses another route from its local cache, if such a route to D exists in its cache. Otherwise, node S initiates route discovery by sending a route request
Node X on receiving a Route Request for some node D can send a Route Reply if node X knows a route to node D
Use of route cache
  can speed up route discovery
  can reduce propagation of route requests

## Slide 43: Use of Route Caching
B
A
S
E
F
H
J
D
C
G
I
K
[P,Q,R] Represents cached route at a node
(DSR maintains the cached routes in a tree format)
M
N
L
[S,E,F,J,D]
[E,F,J,D]
[C,S]
[G,C,S]
[F,J,D],[F,E,S]
[J,F,E,S]
Z

## Slide 44: Use of Route Caching: Can Speed up Route Discovery
B
A
S
E
F
H
J
D
C
G
I
K
Z
M
N
L
[S,E,F,J,D]
[E,F,J,D]
[C,S]
[G,C,S]
[F,J,D],[F,E,S]
[J,F,E,S]
RREQ
When node Z sends a route request
for node C, node K sends back a route
reply [Z,K,G,C] to node Z using a locally
cached route
[K,G,C,S]
RREP

## Slide 45: Use of Route Caching: Can Reduce Propagation of Route Requests
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
[S,E,F,J,D]
[E,F,J,D]
[C,S]
[G,C,S]
[F,J,D],[F,E,S]
[J,F,E,S]
RREQ
Assume that there is no link between D and Z.
Route Reply (RREP) from node K limits flooding of RREQ.
In general, the reduction may be less dramatic.
[K,G,C,S]
RREP

## Slide 46: Route Error (RERR)
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
RERR [J-D]
J sends a route error to S along route J-F-E-S when its attempt to forward the data packet S (with route SEFJD) on J-D fails
Nodes hearing RERR update their route cache to remove link J-D

## Slide 47: Route Caching: Beware!
Stale caches can adversely affect performance
With passage of time and host mobility, cached routes may become invalid
A sender host may try several stale routes (obtained from local cache, or replied from cache by other nodes), before finding a good route

## Slide 48: Dynamic Source Routing: Advantages
Routes maintained only between nodes who need to communicate
  reduces overhead of route maintenance
Route caching can further reduce route discovery overhead
A single route discovery may yield many routes to the destination, due to intermediate nodes replying from local caches

## Slide 49: Dynamic Source Routing: Disadvantages
Packet header size grows with route length due to source routing
Flood of route requests may potentially reach all nodes in the network
Care must be taken to avoid collisions between route requests propagated by neighboring nodes
  insertion of random delays before forwarding RREQ
Increased contention if too many route replies come back due to nodes replying using their local cache
  Route Reply Storm problem
  Reply storm may be eased by preventing a node from sending RREP if it hears another RREP with a shorter route

## Slide 50: Dynamic Source Routing: Disadvantages
An intermediate node may send Route Reply using a stale cached route, thus polluting other caches
This problem can be eased if some mechanism to purge (potentially) invalid cached routes is incorporated.
For some proposals for cache invalidation, see [Hu00Mobicom]
  Static timeouts
  Adaptive timeouts based on link stability

## Slide 51: Flooding of Control Packets
How to reduce the scope of the route request flood ?
  LAR [Ko98Mobicom]
  Query localization [Castaneda99Mobicom]
How to reduce redundant broadcasts ?
  The Broadcast Storm Problem [Ni99Mobicom]

## Slide 52: Location-Aided Routing (LAR) [Ko98Mobicom]
Exploits location information to limit scope of route request flood
  Location information may be obtained using GPS
Expected Zone is determined as a region that is expected to hold the current location of the destination
  Expected region determined based on potentially old location information, and knowledge of the destination’s speed
Route requests limited to a Request Zone that contains the Expected Zone and location of the sender node

## Slide 53: Expected Zone in LAR
X
Y
r
X = last known location of node
D, at time t0
Y = location of node D at current
time t1, unknown to node S
r = (t1 - t0) * estimate of D’s speed
Expected Zone

## Slide 54: Request Zone in LAR
X
Y
r
S
Request Zone
Network Space
B
A

## Slide 55: LAR
Only nodes within the request zone forward route requests
  Node A does not forward RREQ, but node B does (see previous slide)
Request zone explicitly specified in the route request
Each node must know its physical location to determine whether it is within the request zone

## Slide 56: LAR
Only nodes within the request zone forward route requests
If route discovery using the smaller request zone fails to find a route, the sender initiates another route discovery (after a timeout) using a larger request zone
  the larger request zone may be the entire network
Rest of route discovery protocol similar to DSR

## Slide 57: LAR Variations: Adaptive Request Zone
Each node may modify the request zone included in the forwarded request
Modified request zone may be determined using more recent/accurate information, and may be smaller than the original request zone
S
B
Request zone adapted by B
Request zone defined by sender S

## Slide 58: LAR Variations: Implicit Request Zone
In the previous scheme, a route request explicitly specified a request zone
Alternative approach: A node X forwards a route request received from Y if node X is deemed to be closer to the expected zone as compared to Y
The motivation is to attempt to bring the route request physically closer to the destination node after each forwarding

## Slide 59: Location-Aided Routing
The basic proposal assumes that, initially, location information for node X becomes known to Y only during a route discovery
This location information is used for a future route discovery
  Each route discovery yields more updated information which is used for the next discovery
Variations
Location information can also be piggybacked on any message from Y to X
Y may also proactively distribute its location information
  Similar to other protocols discussed later (e.g., DREAM, GLS)

## Slide 60: Location Aided Routing (LAR)
Advantages
  reduces the scope of route request flood
  reduces overhead of route discovery
Disadvantages
  Nodes need to know their physical locations
  Does not take into account possible existence of obstructions for radio transmissions

## Slide 61: Summary: Broadcast Storm Problem
Flooding is used in many protocols, such as Dynamic Source Routing (DSR)
Problems associated with flooding
  collisions
  redundancy
Collisions may be reduced by “jittering” (waiting for a random interval before propagating the flood)
Redundancy may be reduced by selectively re-broadcasting packets from only a subset of the nodes

## Slide 62: Ad Hoc On-Demand Distance Vector Routing (AODV) [Perkins99Wmcsa]
DSR includes source routes in packet headers
Resulting large headers can sometimes degrade performance
  particularly when data contents of a packet are small
AODV attempts to improve on DSR by maintaining routing tables at the nodes, so that data packets do not have to contain routes
AODV retains the desirable feature of DSR that routes are maintained only between nodes which need to communicate

## Slide 63: AODV
Route Requests (RREQ) are forwarded in a manner similar to DSR
When a node re-broadcasts a Route Request, it sets up a reverse path pointing towards the source
  AODV assumes symmetric (bi-directional) links
When the intended destination receives a Route Request, it replies by sending a Route Reply
Route Reply travels along the reverse path set-up when Route Request is forwarded

## Slide 64: Route Requests in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Represents a node that has received RREQ for D from S
M
N
L

## Slide 65: Route Requests in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Represents transmission of RREQ
Z
Y
Broadcast transmission
M
N
L

## Slide 66: Route Requests in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Represents links on Reverse Path
Z
Y
M
N
L

## Slide 67: Reverse Path Setup in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Node C receives RREQ from G and H, but does not forward
it again, because node C has already forwarded RREQ once
Z
Y
M
N
L

## Slide 68: Reverse Path Setup in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L

## Slide 69: Reverse Path Setup in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Node D does not forward RREQ, because node D
is the intended target of the RREQ
M
N
L

## Slide 70: Route Reply in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
Represents links on path taken by RREP
M
N
L

## Slide 71: Route Reply in AODV
An intermediate node (not the destination) may also send a Route Reply (RREP) provided that it knows a more recent path than the one previously known to sender S
To determine whether the path known to an intermediate node is more recent, destination sequence numbers are used
The likelihood that an intermediate node will send a Route Reply when using AODV not as high as DSR
  A new Route Request by node S for a destination is assigned a higher destination sequence number. An intermediate node which knows a route, but with a smaller sequence number, cannot send Route Reply

## Slide 72: Forward Path Setup in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
Forward links are setup when RREP travels along the reverse path
Represents a link on the forward path

## Slide 73: Data Delivery in AODV
B
A
S
E
F
H
J
D
C
G
I
K
Z
Y
M
N
L
Routing table entries used to forward data packet.
Route is not included in packet header.
DATA

## Slide 74: Timeouts
A routing table entry maintaining a reverse path is purged after a timeout interval
  timeout should be long enough to allow RREP to come back
A routing table entry maintaining a forward path is purged if not used for a active_route_timeout interval
  if no is data being sent using a particular routing table entry, that entry will be deleted from the routing table (even if the route may actually still be valid)

## Slide 75: Link Failure Reporting
A neighbor of node X is considered active for a routing table entry if the neighbor sent a packet within active_route_timeout interval which was forwarded using that entry
When the next hop link in a routing table entry breaks, all active neighbors are informed
Link failures are propagated by means of Route Error messages, which also update destination sequence numbers

## Slide 76: Route Error
When node X is unable to forward packet P (from node S to node D) on link (X,Y), it generates a RERR message
Node X increments the destination sequence number for D cached at node X
The incremented sequence number N is included in the RERR
When node S receives the RERR, it initiates a new route discovery for D using destination sequence number at least as large as N

## Slide 77: Destination Sequence Number
Continuing from the previous slide …
When node D receives the route request with destination sequence number N, node D will set its sequence number to N, unless it is already larger than N

## Slide 78: Link Failure Detection
Hello messages: Neighboring nodes periodically exchange hello message
Absence of hello message is used as an indication of link failure
Alternatively, failure to receive several MAC-level acknowledgement may be used as an indication of link failure

## Slide 79: Why Sequence Numbers in AODV
To avoid using old/broken routes
  To determine which route is newer
To prevent formation of loops
  Assume that A does not know about failure of link C-D because RERR sent by C is lost
  Now C performs a route discovery for D. Node A receives the RREQ (say, via path C-E-A)
  Node A will reply since A knows a route to D via node B
  Results in a loop (for instance, C-E-A-B-C )
A
B
C
D
E

## Slide 80: Why Sequence Numbers in AODV
  Loop C-E-A-B-C
A
B
C
D
E

## Slide 81: Optimization: Expanding Ring Search
Route Requests are initially sent with small Time-to-Live (TTL) field, to limit their propagation
  DSR also includes a similar optimization
If no Route Reply is received, then larger TTL tried

## Slide 82: Summary: AODV
Routes need not be included in packet headers
Nodes maintain routing tables containing entries only for routes that are in active use
At most one next-hop per destination maintained at each node
  DSR may maintain several routes for a single destination
Unused routes expire even if topology does not change

## Slide 83: So far ...
All protocols discussed so far perform some form of flooding
Now we will consider protocols which try to reduce/avoid such behavior

## Slide 84: Link Reversal Algorithm [Gafni81]
A
F
B
C
E
G
D

## Slide 85: Link Reversal Algorithm
A
F
B
C
E
G
D
Maintain a directed acyclic
graph (DAG) for each
destination, with the destination
being the only sink
This DAG is for destination
node D
Links are bi-directional
But algorithm imposes
logical directions on them

## Slide 86: Link Reversal Algorithm
Link (G,D) broke
A
F
B
C
E
G
D
Any node, other than the destination, that has no outgoing links
reverses all its incoming links.
Node G has no outgoing links

## Slide 87: Link Reversal Algorithm
A
F
B
C
E
G
D
Now nodes E and F have no outgoing links
Represents a
link that was
reversed recently

## Slide 88: Link Reversal Algorithm
A
F
B
C
E
G
D
Now nodes B and G have no outgoing links
Represents a
link that was
reversed recently

## Slide 89: Link Reversal Algorithm
A
F
B
C
E
G
D
Now nodes A and F have no outgoing links
Represents a
link that was
reversed recently

## Slide 90: Link Reversal Algorithm
A
F
B
C
E
G
D
Now all nodes (other than destination D) have an outgoing link
Represents a
link that was
reversed recently

## Slide 91: Link Reversal Algorithm
A
F
B
C
E
G
D
DAG has been restored with only the destination as a sink

## Slide 92: Link Reversal Algorithm
Attempts to keep link reversals local to where the failure occurred
  But this is not guaranteed
When the first packet is sent to a destination, the destination oriented DAG is constructed
The initial construction does result in flooding of control packets

## Slide 93: Link Reversal Algorithm
The previous algorithm is called a full reversal method since when a node reverses links, it reverses all its incoming links
Partial reversal method [Gafni81]: A node reverses incoming links from only those neighbors who have not themselves reversed links “previously”
  If all neighbors have reversed links, then the node reverses all its incoming links
  “Previously” at node X means since the last link reversal done by node X

## Slide 94: Partial Reversal Method
Link (G,D) broke
A
F
B
C
E
G
D
Node G has no outgoing links

## Slide 95: Partial Reversal Method
A
F
B
C
E
G
D
Now nodes E and F have no outgoing links
Represents a
link that was
reversed recently
Represents a
node that has
reversed links

## Slide 96: Partial Reversal Method
A
F
B
C
E
G
D
Nodes E and F do not reverse links from node G
Now node B has no outgoing links
Represents a
link that was
reversed recently

## Slide 97: Partial Reversal Method
A
F
B
C
E
G
D
Now node A has no outgoing links
Represents a
link that was
reversed recently

## Slide 98: Partial Reversal Method
A
F
B
C
E
G
D
Now all nodes (except destination D) have outgoing links
Represents a
link that was
reversed recently

## Slide 99: Partial Reversal Method
A
F
B
C
E
G
D
DAG has been restored with only the destination as a sink

## Slide 100: Link Reversal Methods: Advantages
Link reversal methods attempt to limit updates to routing tables at nodes in the vicinity of a broken link
  Partial reversal method tends to be better than full reversal method
Each node may potentially have multiple routes to a destination

## Slide 101: Link Reversal Methods: Disadvantage
Need a mechanism to detect link failure
  hello messages may be used
  but hello messages can add to contention
If network is partitioned, link reversals continue indefinitely

## Slide 102: Link Reversal in a Partitioned Network
A
F
B
C
E
G
D
This DAG is for destination node D

## Slide 103: Full Reversal in a Partitioned Network
A
F
B
C
E
G
D
A and G do not have outgoing links

## Slide 104: Full Reversal in a Partitioned Network
A
F
B
C
E
G
D
E and F do not have outgoing links

## Slide 105: Full Reversal in a Partitioned Network
A
F
B
C
E
G
D
B and G do not have outgoing links

## Slide 106: Full Reversal in a Partitioned Network
A
F
B
C
E
G
D
E and F do not have outgoing links

## Slide 107: Full Reversal in a Partitioned Network
A
F
B
C
E
G
D
In the partition
disconnected from
destination D, link
reversals continue, until
the partitions merge
Need a mechanism to
minimize this wasteful
activity
Similar scenario can
occur with partial
reversal method too

## Slide 108: Temporally-Ordered Routing Algorithm (TORA) [Park97Infocom]
TORA modifies the partial link reversal method to be able to detect partitions
When a partition is detected, all nodes in the partition are informed, and link reversals in that partition cease

## Slide 109: Partition Detection in TORA
A
B
E
D
F
C
DAG for
destination D

## Slide 110: Partition Detection in TORA
A
B
E
D
F
C
TORA uses a
modified partial
reversal method
Node A has no outgoing links

## Slide 111: Partition Detection in TORA
A
B
E
D
F
C
TORA uses a
modified partial
reversal method
Node B has no outgoing links

## Slide 112: Partition Detection in TORA
A
B
E
D
F
C
Node B has no outgoing links

## Slide 113: Partition Detection in TORA
A
B
E
D
F
C
Node C has no outgoing links -- all its neighbor have
reversed links previously.

## Slide 114: Partition Detection in TORA
A
B
E
D
F
C
Nodes A and B receive the reflection from node C
Node B now has no outgoing link

## Slide 115: Partition Detection in TORA
A
B
E
D
F
C
Node A has received the reflection from all its neighbors.
Node A determines that it is partitioned from destination D.
Node B propagates
the reflection to node A

## Slide 116: Partition Detection in TORA
A
B
E
D
F
C
On detecting a partition,
node A sends a clear (CLR)
message that purges all
directed links in that
partition

## Slide 117: TORA
Improves on the partial link reversal method in [Gafni81] by detecting partitions and stopping non-productive link reversals
Paths may not be shortest
The DAG provides many hosts the ability to send packets to a given destination
  Beneficial when many hosts want to communicate with a single destination

## Slide 118: TORA Design Decision
TORA performs link reversals as dictated by [Gafni81]
However, when a link breaks, it looses its direction
When a link is repaired, it may not be assigned a direction, unless some node has performed a route discovery after the link broke
  if no one wants to send packets to D anymore, eventually, the DAG for destination D may disappear
TORA makes effort to maintain the DAG for D only if someone needs route to D
  Reactive behavior

## Slide 119: TORA Design Decision
One proposal for modifying TORA optionally allowed a more proactive behavior, such that a DAG would be maintained even if no node is attempting to transmit to the destination
Moral of the story: The link reversal algorithm in [Gafni81] does not dictate a proactive or reactive response to link failure/repair
Decision on reactive/proactive behavior should be made based on environment under consideration

## Slide 120
Clustering Approache To
Multihop Ad Hoc Networks

## Slide 121: Clustering
Goal:
  Reduce channel contention
  Form routing backbone to reduce network diameter
  Abstract network state to reduce its quantity and its variability
Various approaches to clustering
  Started in the 70s with Packet Radio Network (PRNet) sponsored by DARPA
Notes: Goal: respond rapidly to network variations (topology, link quality, …) and minimize resource consumption. This is the general framework for all wireless networks. How does clustering answer this need?
Clusters try to impose a control structure on the network of mobile nodes.

## Slide 122: Clustering for Transmission Management
Goal: reduce contention
Cluster = clusterhead + gateways + ordinary nodes
Roles:
  Clusterhead: schedules traffic, allocates resources (tokens, emits busy tone, etc.). Similar to the master in a Bluetooth piconet.
  Gateways: interconnect clusters
  Ordinary nodes are 1-hop away from a clusterhead and 2-hops away from other members in the cluster
Tasks:
  Connectivity discovery
  Election of clusterheads
  Agree on Gateways
Notes: Refs: [Baker 1981, Ephremides 1987, Gerla 1995, Lin 1997, Raj?…

## Slide 123: Clustering for Transmission Management (Cont)
Clusterhead election:
  Centralized/distributed algorithms
  Node identifier/degree based
  Principles:
    Centralized: (1) elect the highest ID node and create a corresponding cluster, repeat step (1) with nodes not already members of a cluster
    Distributed:
      a node elects itself as cluster head if it has the highest ID among its neighbors
      otherwise elect a neighbor that is not member of another cluster
  Leads to disjoint clusters
Gateways:
  If connected to > 1 cluster => gateway candidate
  If num_hops (CH1) = 1 & num_hops(CH2) = 2 =>GW1 --- GW2
  When multiple candidates to connect two clusters, choose GW with highest ID
Notes: Algorithms do not use connectivity flexibility

## Slide 124: Clustering for Transmission Management (Cont)
Mobility:
  Most algorithms do not adjust to mobility. They recompute the cluster.
  Recent algorithms:
    change clusterhead status when two clusterheads become neighbors
    [Gerla-Lin 1995, 1997]: cluster maintenance
Routing:
  To avoid clusterhead congestion and improve robustness, routing is done over the flat network

## Slide 125: Clustering for Backbone Formation
Wireless multiphop networks have high end-to-end delay:
  link-layer ARQ, MAC delay, FEC/spreading, tx/rx switching time
Clustering can reduce the end-to-end delay by allowing faster forwarding through the clusterheads backbone
Approaches:
  Near-Term Digital Radio Network (NTDR) [Zavgren 1997]
  Virtual Subnet Architecture [Sharony 1996]

## Slide 126: Near-Term Digital Radio Network (NTDR)
Goal: support mobile tactical communication
Architecture: (clusterheads = gateways) + (single-hop nodes)
Communication:
  All 2-hop packets go through the clusterheads backbone
  Two frequencies: intra-cluster band + inter-cluster band
Clusterhead election:
  Clusterheads send a beacon (organization, members, TxPwrL, PL to nodes)
  Nodes elect themselves if: (1) do not receive a beacon, (2) receives beacons with different partition numbers
Preventing multiple clusterhead creation:
  Wait a random amount of time before self-election as clusterhead
  After self-election, immediately issue beacons
  Eliminate superfluous clusterheads without partitioning the network

## Slide 127: NTDR (Cont)
Cluster affiliation criteria:
  Node and clusterhead are in the same organization
  Low path loss (conserves energy)
  Resulting cluster has a small size
Canceling affiliation:
  Clusterhead relinquishes its role
  Broken link (or low quality link)
On membership change all clusterheads are updated
Routing:
  Use a link state protocol: Dijkstra’s Shortest Path First algorithm
  Resistance metric: minimize interference experienced by packets
  Does not scale for high mobility networks because of flooding cost

## Slide 128: Building a Clustering Hierarchy
Objectives:
  Minimizing the amount of routing information
  Maximize connectivity within each cluster
  Localize high-intensity traffic within one cluster
  Minimizing the number of intercluster links
  Maximizing the stability of intercluster links
  Minimizing the difference between the hierarchical route and the optimal route
Possible constraints:
  Upper/lower limit of the number of childs
  Upper limit on the diameter of each cluster
  Constant number of childs

## Slide 129: Limitations of Current Clustering Algorithms
Most clustering algorithms do not consider the flexibility/constraints of radio frequency communication:
  Connectivity is not rigid but can be controlled through power-control
  Leader consume more energy then ordinary nodes
Relation between MAC, power-control and coding:
  Coding generates more time interference (collisions?), high power generates more space interference (SNIR)
Hybrid networks require to consider fairness more seriously:
  Nodes in the vicinity of the AP would experience more traffic than nodes on the periphery