## Slide 1: Wireless Networks: Transport Protocols
Motivation
TCP-mechanisms
Indirect TCP
Snooping TCP
Mobile TCP
Fast retransmit/recovery
Transmission freezing
Selective retransmission
Transaction oriented TCP
Adapted from J. Schiller, “Mobile Communications”, Chapter 10

## Slide 2: Motivation I
Transport protocols typically designed for
  Fixed end-systems
  Fixed, wired networks
Research activities
  Performance
  Congestion control
  Efficient retransmissions
TCP congestion control
  packet loss in fixed networks typically due to (temporary) overload situations
  router have to discard packets as soon as the buffers are full
  TCP recognizes congestion only indirectly via missing acknowledgements, retransmissions unwise, they would only contribute to the congestion and make it even worse
  Reaction: cut congestion threshold by one half and go to slow start
Notes: How does TCP start: he doesn’t know the sustainable rate of the network: slow start, mult decr./add incr., …

## Slide 3: Motivation II
TCP slow-start algorithm
  sender calculates a congestion window for a receiver
  start with a congestion window size equal to one segment
  exponential increase of the congestion window up to the congestion threshold, then linear increase
  missing acknowledgement causes the reduction of the congestion threshold to one half of the current congestion window
  congestion window starts again with one segment
60
20
1.0
2.0
3.0
4.0
5.0
6.0
7.0
8.0
9.0
KB
70
30
40
50
10

## Slide 4
TCP fast retransmit/fast recovery
  TCP sends an acknowledgement only after receiving a packet
  if a sender receives several acknowledgements for the same packet, this is due to a gap in received packets at the receiver
  however, the receiver got all packets up to the gap and is actually receiving packets
  therefore, packet loss is not due to congestion, continue with current congestion window (do not use slow-start)

## Slide 5: Influences of mobility on TCP-mechanisms
TCP assumes congestion if packets are dropped
  typically wrong in wireless networks, here we often have packet loss due to transmission errors
  furthermore, mobility itself can cause packet loss, if e.g. a mobile node roams from one access point (e.g. foreign agent in Mobile IP) to another while there are still packets in transit to the wrong access point and forwarding is not possible
The performance of an unchanged TCP degrades severely
  however, TCP cannot be changed fundamentally due to the large base of installation in the fixed network, TCP for mobility has to remain compatible
  the basic TCP mechanisms keep the whole Internet together

## Slide 6: Indirect TCP I
Indirect TCP or I-TCP segments the connection
  no changes to the TCP protocol for hosts connected to the wired Internet, millions of computers use (variants of) this protocol
  optimized TCP protocol for mobile hosts
  splitting of the TCP connection at, e.g., the foreign agent into 2 TCP connections, no real end-to-end connection any longer
  hosts in the fixed part of the net do not notice the characteristics of the wireless part
mobile host
access point
(foreign agent)
„wired“ Internet
„wireless“ TCP
standard TCP

## Slide 7: I-TCP socket and state migration
mobile host
access point2
Internet
access point1
socket migration
and state transfer

## Slide 8: Indirect TCP II
Advantages
  no changes in the fixed network necessary, no changes for the hosts (TCP protocol) necessary, all current optimizations to TCP still work
  transmission errors on the wireless link do not propagate into the fixed network
  simple to control, mobile TCP is used only for one hop between, e.g., a foreign agent and mobile host
  therefore, a very fast retransmission of packets is possible, the short delay on the mobile hop is known
Disadvantages
  loss of end-to-end semantics, an acknowledgement to a sender does now not any longer mean that a receiver really got a packet, foreign agents might crash
  higher latency possible due to buffering of data within the foreign agent and forwarding to a new foreign agent

## Slide 9: Snooping TCP I
„Transparent“ extension of TCP within the foreign agent
  buffering of packets sent to the mobile host
  lost packets on the wireless link (both directions!) will be retransmitted immediately by the mobile host or foreign agent, respectively (so called “local” retransmission)
  the foreign agent therefore “snoops” the packet flow and recognizes acknowledgements in both directions, it also filters ACKs
  changes of TCP only within the foreign agent (+min. MH change)
„wired“ Internet
buffering of data
end-to-end TCP connection
local retransmission
correspondent
host
foreign
agent
mobile
host
snooping of ACKs

## Slide 10: Snooping TCP II
Data transfer to the mobile host
  FA buffers data until it receives ACK of the MH, FA detects packet loss via duplicated ACKs or time-out
  fast retransmission possible, transparent for the fixed network
Data transfer from the mobile host
  FA detects packet loss on the wireless link via sequence numbers, FA answers directly with a NACK to the MH
  MH can now retransmit data with only a very short delay
Integration of the MAC layer
  MAC layer often has similar mechanisms to those of TCP
  thus, the MAC layer can already detect duplicated packets due to retransmissions and discard them
Problems
  snooping TCP does not isolate the wireless link as good as I-TCP
  snooping might be useless depending on encryption schemes
10.8.1

## Slide 11: Mobile TCP
Special handling of lengthy and/or frequent disconnections
M-TCP splits as I-TCP does
  unmodified TCP fixed network to supervisory host (SH)
  optimized TCP SH to MH
Supervisory host
  no caching, no retransmission
  monitors all packets, if disconnection detected
    set sender window size to 0
    sender automatically goes into persistent mode
  old or new SH reopen the window
Advantages
  maintains semantics, supports disconnection, no buffer forwarding
Disadvantages
  loss on wireless link propagated into fixed network
  adapted TCP on wireless link
Notes: Problems with timer that can grow to 1min even if the connection comes back…
How is the timer computed in TCP

## Slide 12: Fast retransmit/fast recovery
Change of foreign agent often results in packet loss
  TCP reacts with slow-start although there is no congestion
Forced fast retransmit
  as soon as the mobile host has registered with a new foreign agent, the MH sends duplicated acknowledgements on purpose
  this forces the fast retransmit mode at the communication partners
  additionally, the TCP on the MH is forced to continue sending with the actual window size and not to go into slow-start after registration
Advantage
  simple changes result in significanlyt higher performance
Disadvantage
  further mix of IP and TCP (to know when there is a new registration), no transparent approach
10.10.1

## Slide 13: Transmission/time-out freezing
Mobile hosts can be disconnected for a longer time
  no packet exchange possible, e.g., in a tunnel, disconnection due to overloaded cells or mux. with higher priority traffic
  TCP disconnects after time-out completely
TCP freezing
  MAC layer is often able to detect interruption in advance
  MAC can inform TCP layer of upcoming loss of connection
  TCP stops sending, but does now not assume a congested link
  MAC layer signals again if reconnected
Advantage
  scheme is independent of data and TCP mechanisms (Ack,SN) => works even with IPsec
Disadvantage
  TCP on mobile host has to be changed, mechanism depends on MAC layer

## Slide 14: Selective retransmission
TCP acknowledgements are often cumulative
  ACK n acknowledges correct and in-sequence receipt of packets up to n
  if single packets are missing quite often a whole packet sequence beginning at the gap has to be retransmitted (go-back-n), thus wasting bandwidth
Selective retransmission as one solution
  RFC2018 allows for acknowledgements of single packets, not only acknowledgements of in-sequence packet streams without gaps
  sender can now retransmit only the missing packets
Advantage
  much higher efficiency
Disadvantage
  more complex software in a receiver, more buffer needed at the receiver
Notes: Check RFC2018

## Slide 15: Transaction oriented TCP
TCP phases
  connection setup, data transmission, connection release
  using 3-way-handshake needs 3 packets for setup and release, respectively
  thus, even short messages need a minimum of 7 packets!
Transaction oriented TCP
  RFC1644, T-TCP, describes a TCP version to avoid this overhead
  connection setup, data transfer and connection release can be combined
  thus, only 2 or 3 packets are needed
Advantage
  efficiency
Disadvantage
  requires changed TCP
  mobility not longer transparent

## Slide 16: Comparison of different approaches for a “mobile” TCP