## Slide 1: Cellular Wireless Networks
Textbook Chapter 10

## Slide 2: Cellular Network Organization
Use multiple low-power transmitters (100 W or less)
Areas divided into cells
  Each served by its own antenna
  Served by base station consisting of transmitter, receiver, and control unit
  Band of frequencies allocated
  Cells set up such that antennas of all neighbors are equidistant (hexagonal pattern)

## Slide 3: Frequency Reuse
Adjacent cells assigned different frequencies to avoid interference or crosstalk
Objective is to reuse frequency in nearby cells
  10 to 50 frequencies assigned to each cell
  Transmission power controlled to limit power at that frequency escaping to adjacent cells
  The issue is to determine how many cells must intervene between two cells using the same frequency

## Slide 4: Cellular Concept
Several small cells instead of a single transmitter=> frequency reuse: better efficiency
Fixed Channel Allocation:
Cluster of size N = i2+ij+j2; and D = sqrt(3N)R
R cell radius and
D distance at which a frequency can be reused with acceptable interference

## Slide 5: Examples

## Slide 6: Approaches to Cope with Increasing Capacity
Adding new channels
Frequency borrowing – frequencies are taken from adjacent cells by congested cells
Cell splitting – cells in areas of high usage can be split into smaller cells
Cell sectoring – cells are divided into a number of wedge-shaped sectors, each with their own set of channels
Microcells – antennas move to buildings, hills, and lamp posts

## Slide 7: Cellular System Overview

## Slide 8: Cellular Systems Basic Terms
Base Station (BS) – includes an antenna, a controller, and a number of receivers
Mobile telecommunications switching office (MTSO) – connects calls between mobile units
Two types of channels available between mobile unit and BS
  Control channels – used to exchange information having to do with setting up and maintaining calls
  Traffic channels – carry voice or data connection between users

## Slide 9: Steps in an MTSO Controlled Call between Mobile Users
Mobile unit initialization
Mobile-originated call
Paging
Call accepted
Ongoing call
Handoff

## Slide 10: Additional Functions in an MTSO Controlled Call
Call blocking
Call termination
Call drop
Calls to/from fixed and remote mobile subscriber

## Slide 11: Mobile Radio Propagation Effects
Signal strength
  Must be strong enough between base station and mobile unit to maintain signal quality at the receiver
  Must not be so strong as to create too much cochannel interference with channels in another cell using the same frequency band
Fading
  Signal propagation effects may disrupt the signal and cause errors

## Slide 12: Handoff Performance Metrics
Cell blocking probability – probability of a new call being blocked
Call dropping probability – probability that a call is terminated due to a handoff
Call completion probability – probability that an admitted call is not dropped before it terminates
Probability of unsuccessful handoff – probability that a handoff is executed while the reception conditions are inadequate

## Slide 13: Handoff Performance Metrics
Handoff blocking probability – probability that a handoff cannot be successfully completed
Handoff probability – probability that a handoff occurs before call termination
Rate of handoff – number of handoffs per unit time
Interruption duration – duration of time during a handoff in which a mobile is not connected to either base station
Handoff delay – distance the mobile moves from the point at which the handoff should occur to the point at which it does occur

## Slide 14: Handoff Strategies Used to Determine Instant of Handoff
Relative signal strength
Relative signal strength with threshold
Relative signal strength with hysteresis
Relative signal strength with hysteresis and threshold
Prediction techniques

## Slide 15: Power Control
Design issues making it desirable to include dynamic power control in a cellular system
  Received power must be sufficiently above the background noise for effective communication
  Desirable to minimize power in the transmitted signal from the mobile
    Reduce cochannel interference, alleviate health concerns, save battery power
  In SS systems using CDMA, it’s desirable to equalize the received power level from all mobile units at the BS

## Slide 16: Types of Power Control
Open-loop power control
  Depends solely on mobile unit
  No feedback from BS
  Not as accurate as closed-loop, but can react quicker to fluctuations in signal strength
Closed-loop power control
  Adjusts signal strength in reverse channel based on metric of performance
  BS makes power adjustment decision and communicates to mobile on control channel

## Slide 17: Traffic Engineering
Ideally, available channels would equal number of subscribers active at one time
In practice, not feasible to have capacity handle all possible load
For N simultaneous user capacity and L subscribers
  L < N – nonblocking system
  L > N – blocking system

## Slide 18: Blocking System Performance Questions
Probability that call request is blocked?
What capacity is needed to achieve a certain upper bound on probability of blocking?
What is the average delay?
What capacity is needed to achieve a certain average delay?

## Slide 19: Traffic Intensity
Load presented to a system:
     = mean rate of calls attempted per unit time
    h = mean holding time per successful call
    A = average number of calls arriving during average holding period
    A is also called traffic intensity (Erlangs) and

## Slide 20: Capacity in Cellular Systems
Blocking Probability (Grade Of Service): Erlang B formula
: calls arrival rate; T: calls average duration (service time: 1/)

## Slide 21: Factors that Determine the Nature of the Traffic Model
Manner in which blocked calls are handled
  Lost calls delayed (LCD) – blocked calls put in a queue awaiting a free channel
  Blocked calls rejected and dropped
    Lost calls cleared (LCC) – user waits before another attempt
    Lost calls held (LCH) – user repeatedly attempts calling
Number of traffic sources
  Whether number of users is assumed to be finite or infinite

## Slide 22: First-Generation Analog
Advanced Mobile Phone Service (AMPS)
  In North America, two 25-MHz bands allocated to AMPS
    One for transmission from base to mobile unit
    One for transmission from mobile unit to base
  Each band split in two to encourage competition (12.5MHz per operator)
  Channels of 30 KHz: 21 CtrlCh (FSK), 395 TrafficChannels (FM voice) per operator
  Frequency reuse exploited (R = 7)

## Slide 23: AMPS Operation
Subscriber initiates call by keying in phone number and presses send key
MTSO verifies number and authorizes user
MTSO issues message to user’s cell phone indicating send and receive traffic channels
MTSO sends ringing signal to called party
Party answers; MTSO establishes circuit and initiates billing information
Either party hangs up; MTSO releases circuit, frees channels, completes billing

## Slide 24: Differences Between First and Second Generation Systems
Digital traffic channels – first-generation systems are almost purely analog; second-generation systems are digital
Encryption – all second generation systems provide encryption to prevent eavesdropping
Error detection and correction – second-generation digital traffic allows for detection and correction, giving clear voice reception
Channel access – second-generation systems allow channels to be dynamically shared by a number of users

## Slide 25: Mobile Wireless TDMA Design Considerations
Number of logical channels (number of time slots in TDMA frame): 8
Maximum cell radius (R): 35 km
Frequency: region around 900 MHz
Maximum vehicle speed (Vm):250 km/hr
Maximum coding delay: approx. 20 ms
Maximum delay spread (m): 10 s
Bandwidth: Not to exceed 200 kHz

## Slide 26: Steps in Design of TDMA Timeslot

## Slide 27: GSM Network Architecture

## Slide 28: Architecture of the GSM system
GSM is a PLMN (Public Land Mobile Network)
  several providers setup mobile networks following the GSM standard within each country
  components
    MS (mobile station)
    BS (base station)
    MSC (mobile switching center)
    LR (location register)
  subsystems
    RSS (radio subsystem): covers all radio aspects
    NSS (network and switching subsystem): call forwarding, handover, switching
    OSS (operation subsystem): management of the network

## Slide 29: GSM: overview
NSS
with OSS
fixed network
BSC
BSC
MSC
MSC
GMSC
OMC, EIR, AUC
VLR
HLR
RSS
VLR

## Slide 30: GSM: elements and interfaces
NSS
MS
MS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
PDN
ISDN, PSTN
RSS
radio cell
radio cell
MS
AUC
OSS
signaling
O

## Slide 31: GSM: system architecture
Um
Abis
A
BSS
radio subsystem
MS
MS
BTS
BSC
BTS
BTS
BSC
BTS
network and switching subsystem
MSC
MSC
fixed partner networks
IWF
ISDN PSTN
PSPDN CSPDN
SS7
EIR
HLR
VLR
ISDN PSTN

## Slide 32: System architecture: radio subsystem
Components
  MS (Mobile Station)
  BSS (Base Station Subsystem): consisting of
    BTS (Base Transceiver Station): sender and receiver
    BSC (Base Station Controller): controlling several transceivers
Interfaces
  Um : radio interface
  Abis : standardized, open interface with 16 kbit/s user channels
  A: standardized, open interface with 64 kbit/s user channels
Um
Abis
A
BSS
radio subsystem
network and switching subsystem
MS
MS
BTS
BSC
MSC
BTS
BTS
BSC
BTS
MSC

## Slide 33: System architecture: network and switching subsystem
Components
  MSC (Mobile Services Switching Center):
  IWF (Interworking Functions)
  ISDN (Integrated Services Digital Network)
  PSTN (Public Switched Telephone Network)
  PSPDN (Packet Switched Public Data Net.)
  CSPDN (Circuit Switched Public Data Net.)
Databases
  HLR (Home Location Register)
  VLR (Visitor Location Register)
  EIR (Equipment Identity Register)
network subsystem
MSC
MSC
fixed partner networks
IWF
ISDN PSTN
PSPDN CSPDN
SS7
EIR
HLR
VLR
ISDN PSTN

## Slide 34: Radio subsystem
The Radio Subsystem (RSS) comprises the cellular mobile network up to the switching centers
Components
  Base Station Subsystem (BSS):
    Base Transceiver Station (BTS): radio components including sender, receiver, antenna - if directed antennas are used one BTS can cover several cells
    Base Station Controller (BSC): switching between BTSs, controlling BTSs, managing of network resources, mapping of radio channels (Um) onto terrestrial channels (A interface)
    BSS = BSC + sum(BTS) + interconnection
  Mobile Stations (MS)

## Slide 35: Mobile Station
Mobile station communicates across Um interface (air interface) with base station transceiver in same cell as mobile unit
Mobile Equipment (ME) – physical terminal, such as a telephone or PCS
  ME includes radio transceiver, digital signal processors and subscriber identity module (SIM)
GSM subscriber units are generic until SIM is inserted
  SIMs roam, not necessarily the subscriber devices

## Slide 36: Base Station Subsystem (BSS)
BSS consists of base station controller and one or more base transceiver stations (BTS)
Each BTS defines a single cell
  Includes radio antenna, radio transceiver and a link to a base station controller (BSC)
BSC reserves radio frequencies, manages handoff of mobile unit from one cell to another within BSS, and controls paging

## Slide 37: Network Subsystem (NS)
NS provides link between cellular network and public switched telecommunications networks
  Controls handoffs between cells in different BSSs
  Authenticates users and validates accounts
  Enables worldwide roaming of mobile users
Central element of NS is the mobile switching center (MSC)

## Slide 38: Mobile Switching Center (MSC) Databases
Home location register (HLR) database – stores information about each subscriber that belongs to it
Visitor location register (VLR) database – maintains information about subscribers currently physically in the region
Authentication center database (AuC) – used for authentication activities, holds encryption keys
Equipment identity register database (EIR) – keeps track of the type of equipment that exists at the mobile station

## Slide 39: TDMA Format – Time Slot Fields
Trail bits – allow synchronization of transmissions from mobile units
Encrypted bits – encrypted data
Training sequence – used to adapt parameters of receiver to the current path propagation characteristics
  Strongest signal selected in case of multipath propagation
Guard bits – used to avoid overlapping with other bursts

## Slide 40: GSM Speech Signal Processing

## Slide 41: GSM Signaling Protocol Architecture

## Slide 42: Functions Provided by Protocols
Protocols above the link layer of the GSM signaling protocol architecture provide specific functions:
  Radio resource management
  Mobility management
  Connection management
  Mobile application part (MAP)
  BTS management

## Slide 43: GSM protocol layers for signaling
CM
MM
RR
MM
LAPDm
radio
LAPDm
radio
LAPD
PCM
RR’
BTSM
CM
LAPD
PCM
RR’
BTSM
16/64 kbit/s
Um
Abis
A
SS7
PCM
SS7
PCM
64 kbit/s /
2.048 Mbit/s
MS
BTS
BSC
MSC
BSSAP
BSSAP

## Slide 44: Mobile Terminated Call
PSTN
calling
station
GMSC
HLR
VLR
BSS
BSS
BSS
MSC
MS
1
2
3
4
5
6
7
8
9
10
11
12
13
16
10
10
11
11
11
14
15
17
1: calling a GSM subscriber
2: forwarding call to GMSC
3: signal call setup to HLR
4, 5: request MSRN from VLR
6: forward responsible MSC to GMSC
7: forward call to
current MSC
8, 9: get current status of MS
10, 11: paging of MS
12, 13: MS answers
14, 15: security checks
16, 17: set up connection

## Slide 45: Mobile Originated Call
PSTN
GMSC
VLR
BSS
MSC
MS
1
2
6
5
3
4
9
10
7
8
1, 2: connection request
3, 4: security check
5-8: check resources (free circuit)
9-10: set up call

## Slide 46: MTC/MOC
BTS
MS
paging request
channel request
immediate assignment
paging response
authentication request
authentication response
ciphering command
ciphering complete
setup
call confirmed
assignment command
assignment complete
alerting
connect
connect acknowledge
data/speech exchange
BTS
MS
channel request
immediate assignment
service request
authentication request
authentication response
ciphering command
ciphering complete
setup
call confirmed
assignment command
assignment complete
alerting
connect
connect acknowledge
data/speech exchange
MTC
MOC

## Slide 47: 4 types of handover
MSC
MSC
BSC
BSC
BSC
BTS
BTS
BTS
BTS
MS
MS
MS
MS
1
2
3
4

## Slide 48: Handover decision
receive level
BTSold
receive level
BTSold
MS
MS
HO_MARGIN
BTSold
BTSnew

## Slide 49: Handover procedure
HO access
BTSold
BSCnew
measurement
result
BSCold
Link establishment
MSC
MS
measurement
report
HO decision
HO required
BTSnew
HO request
resource allocation
ch. activation
ch. activation ack
HO request ack
HO command
HO command
HO command
HO complete
HO complete
clear command
clear command
clear complete
clear complete

## Slide 50: Security in GSM
Security services
  access control/authentication
    user  SIM (Subscriber Identity Module): secret PIN (personal identification number)
    SIM  network: challenge response method
  confidentiality
    voice and signaling encrypted on the wireless link (after successful authentication)
  anonymity
    temporary identity TMSI (Temporary Mobile Subscriber Identity)
    newly assigned at each new location update (LUP)
    encrypted transmission
3 algorithms specified in GSM
  A3 for authentication (“secret”, open interface)
  A5 for encryption (standardized)
  A8 for key generation (“secret”, open interface)
“secret”:
A3 and A8 available via the Internet
network providers can use stronger mechanisms

## Slide 51: GSM - authentication
A3
RAND
Ki
128 bit
128 bit
SRES* 32 bit
A3
RAND
Ki
128 bit
128 bit
SRES 32 bit
SRES* =? SRES
SRES
RAND
SRES
32 bit
mobile network
SIM
AuC
MSC
SIM
Ki: individual subscriber authentication key SRES: signed response

## Slide 52: GSM - key generation and encryption
A8
RAND
Ki
128 bit
128 bit
Kc
64 bit
A8
RAND
Ki
128 bit
128 bit
SRES
RAND
encrypted data
mobile network (BTS)
MS with SIM
AC
BTS
SIM
A5
Kc
64 bit
A5
MS
data
data
cipher
key

## Slide 53: Data services in GSM I
Data transmission standardized with only 9.6 kbit/s
  advanced coding allows 14,4 kbit/s
  not enough for Internet and multimedia applications
HSCSD (High-Speed Circuit Switched Data)
  already standardized
  bundling of several time-slots to get higher AIUR (Air Interface User Rate) (e.g., 57.6 kbit/s using 4 slots, 14.4 each)
  advantage: ready to use, constant quality, simple
  disadvantage: channels blocked for voice transmission

## Slide 54: Data services in GSM II
GPRS (General Packet Radio Service)
  packet switching
  using free slots only if data packets ready to send (e.g., 115 kbit/s using 8 slots temporarily)
  standardization 1998, introduced 2000
  advantage: one step towards 3G, more flexible
  disadvantage: more investment needed
GPRS network elements
  GSN (GPRS Support Nodes): GGSN and SGSN
  GGSN (Gateway GSN)
    interworking unit between GPRS and PDN (Packet Data Network)
  SGSN (Serving GSN)
    supports the MS (location, billing, security)
  GR (GPRS Register)
    user addresses

## Slide 55: GPRS quality of service

## Slide 56: IS-95 (CdmaOne): [TIA/EIA IS-95]
IS-95: standard for the radio interface
IS-41: standard for the network part
Operates on 800MHz and 1900MHz bands
Uses DS-CDMA technology (1.2288 Mchips/s)
Forward link (downlink): ½ convolutional code, interleaved, 64 chips spreading sequence (Walsh-Hadamard functions)
pilot channel (code 0), synchronization channel (code 32), 7 paging channels, 55 traffic channels
Reverse link (uplink): 1/3 convolutional code, interleaved, 6 bits are mapped into a Walsh-Hadamard sequence, spreading using a User-BaseStation specific code (with period 242-1/215)
Tight power control (open-loop, fast closed loop)

## Slide 57: Advantages of CDMA Cellular
Frequency diversity – frequency-dependent transmission impairments have less effect on signal
Multipath resistance – chipping codes used for CDMA exhibit low cross correlation and low autocorrelation
Privacy – privacy is inherent since spread spectrum is obtained by use of noise-like signals
Graceful degradation – system only gradually degrades as more users access the system

## Slide 58: Drawbacks of CDMA Cellular
Self-jamming – arriving transmissions from multiple users not aligned on chip boundaries unless users are perfectly synchronized
Near-far problem – signals closer to the receiver are received with less attenuation than signals farther away
Soft handoff – requires that the mobile acquires the new cell before it relinquishes the old; this is more complex than hard handoff used in FDMA and TDMA schemes

## Slide 59: Mobile Wireless CDMA Design Considerations
RAKE receiver – when multiple versions of a signal arrive more than one chip interval apart, RAKE receiver attempts to recover signals from multiple paths and combine them
  This method achieves better performance than simply recovering dominant signal and treating remaining signals as noise
Soft Handoff – mobile station temporarily connected to more than one base station simultaneously

## Slide 60: Principle of RAKE Receiver

## Slide 61: Types of Channels Supported by Forward Link
Pilot (channel 0) - allows the mobile unit to acquire timing information, provides phase reference and provides means for signal strength comparison
Synchronization (channel 32) - used by mobile station to obtain identification information about cellular system
Paging (channels 1 to 7) - contain messages for one or more mobile stations
Traffic (channels 8 to 31 and 33 to 63) – the forward channel supports 55 traffic channels

## Slide 62: Forward Traffic Channel Processing Steps
Speech is encoded at a rate of 8550 bps
Additional bits added for error detection
Data transmitted in 2-ms blocks with forward error correction provided by a convolutional encoder
Data interleaved in blocks to reduce effects of errors
Data bits are scrambled, serving as a privacy mask

## Slide 63: Forward Traffic Channel Processing Steps (cont.)
Power control information inserted into traffic channel
DS-SS function spreads the 19.2 kbps to a rate of 1.2288 Mbps using one row of 64 x 64 Walsh matrix
Digital bit stream modulated onto the carrier using QPSK modulation scheme

## Slide 64: ITU’s View of Third-Generation Capabilities
Voice quality comparable to the public switched telephone network
144 kbps data rate available to users in high-speed motor vehicles over large areas
384 kbps available to pedestrians standing or moving slowly over small areas
Support for 2.048 Mbps for office use
Symmetrical / asymmetrical data transmission rates
Support for both packet switched and circuit switched data services

## Slide 65: ITU’s View of Third-Generation Capabilities
An adaptive interface to the Internet to reflect efficiently the common asymmetry between inbound and outbound traffic
More efficient use of the available spectrum in general
Support for a wide variety of mobile equipment
Flexibility to allow the introduction of new services and technologies

## Slide 66: Alternative Interfaces

## Slide 67: CDMA Design Considerations
Bandwidth – limit channel usage to 5 MHz
Chip rate – depends on desired data rate, need for error control, and bandwidth limitations; 3 Mcps or more is reasonable
Multirate – advantage is that the system can flexibly support multiple simultaneous applications from a given user and can efficiently use available capacity by only providing the capacity required for each service